## Slide 1: Chapter 1, part 1: Embedded and Cyber-Physical Computing
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Lay of the land.
Applications.

## Slide 3: The landscape of embedded computing
Lots of embedded applications require very high performance:
  Communications.
  Multimedia.
  Control.
Must also meet strict design goals:
  Real-time performance.
  Power/energy consumption.
  Cost.

## Slide 4: Designing embedded systems
No one architecture (hardware or software) can meet the needs of all applications.
We need to be able to design a system from the application:
  Quickly and efficiently.
  With reliable results.

## Slide 5: Aspects of embedded system design

## Slide 6: Architectures
Both hardware and software architectures are important.
The structure of the system determines cost, power, performance.
Different application requirements lead us to different architectures.

## Slide 7: Applications
You can’t design the best embedded systems if you don’t know anything about your application.
You can’t be an expert in everything.
  But a little knowledge goes a long way.
Domain expertise helps you make trade-offs:
  Can the requirements be relaxed?
  Can one requirement be traded for another?

## Slide 8: Methodologies
We must be able to reliably design systems:
  Start from requirements/specification.
  Build a system that is fast enough, doesn’t burn too much energy, and is cheap enough.
  Be able to finish it on time.
  And know before we start how difficult the project will be.
Invention lets us get around some key technical barriers.
Methodology ensures consistency.

## Slide 9: Modeling
A key aspect of methodology is modeling.
  Work with a simplified version of the object.
Modeling helps us predict the consequences of design decisions.
Models help us work faster (once we have the model).
We can afford to use models if we can reuse them in several designs---methodology relies on and enables modeling.

## Slide 10: Disciplines in embedded computing
Core areas:
  Real-time computing.
  Hardware/software co-design.
Closely related areas:
  Cyber-physical systems.
  Computer architecture.
  Software engineering.
  Low-power design.
  Operating systems.
  Programming languages and compilers.
  Networking.
  Secure and reliable computing.

## Slide 11: History of embedded computing

## Slide 12: Cyber-physical and embedded computing
Cyber-physical system: a computer-controlled physical machine.
Computational control allows a wide range of control strategies, more complex control.
Physical plant ties the computation to real-world time and energy.

## Slide 13: Networks and embedded systems
An increasing number of embedded systems connect to the Internet.
  Resource management.
  Security.
Many specialized networks have been developed for embedded systems:
  Automotive and aerospace.
  Device control.

## Slide 14: Seven layers of the OSI network stack
Physical: Electrical, physical.
Data link: Access, error control across a single link.
Network: End-to-end service.
Transport: Connection-oriented service.
Session: Control activities.
Presentation: Data exchange formats.
Application: Interface to end use.

## Slide 15: Automobiles as distributed embedded systems

## Slide 16: Automotive and aviation electronics
Some functions are safety-critical.
Must operate in real-time.
Must fit within power budget (limited by generator).
Must be lightweight to fit within vehicle weight budget.

## Slide 17: Automotive electronics/avionics uses
Operator vs. passenger: Passenger operations are less critical, more varied (TV, Internet, etc.).
Control vs. instrumentation: Instruments report on the vehicle, control closes the loop.
  Low-priority operations should not interfere with high-priority operations in the system: flight surfaces vs. instruments; instruments vs. passenger devices.

## Slide 18: Medical devices and systems
Systems-of-systems:
  each medical device is complex;
  must work together to provide information to medical personnel, perform functions on patients.
Safety-critical systems.
May operate in geographically distributed mode (remote medic, ambulance, hospital).

## Slide 19: Medical Application Platform [Hat12]
Transfers data between devices or to medical records system.
Perform signal processing to sound alarms.
Integrate information from multiple sources.
Closed-loop control.
Workflow tools to guide personnel through standard procedures.
Safety interlocks.

## Slide 20: Obstacles to adopting MAPs
Interoperability standards do not support real-time control, safety, security.
Hard to plug-and-play devices from multiple vendors.
FDA certification process is not well-suited to open platform architectures.

## Slide 21: Integrated Clinical Environment (ICE) [MDP12]

## Slide 22: Medical Device Coordination Framework [Med12]
Publish-subscribe model.

## Slide 23: Electric power
U. S. transmission is divided into several separate grids, each with complex structure.
Traditionally divided into transmission and distribution.
[Wik12]

## Slide 24: Generation management
Utilities forecast demand and schedule generation:
  Unit commitment decides when to turn on/off generators.
  Generator scheduling determines amount of power generated.
Coal generators may take 8 hours to bring on-line.

## Slide 25: Power grid structure
Transmission refers to system above the substation.
Distribution refers to substation-to-load.

## Slide 26: Energy system control architecture
Large-scale power facilities are under the control of operators.
Supervisory control and data acquisition (SCADA) manages system components.
  Fine-grained control is performed locally.
  Large-scale, longer-term control is perfomred by SCADA, supervised by operators.

## Slide 27: Smart grids
Smart grids use cyber systems to automatically control generation, consumption.
  Reducing consumption (peak shaving) can eliminate the need to start a generator.
  Energy storage can perform as an alternative to peak shaving.
Microgrids are small-scale smart grids.
Smart grids can be used in buildings, facilities, homes, as well as larger scale.

## Slide 28: Radio and networking
Modern radio systems carry digital information.
Perform modulation/ demodulation and error correction.
May also be closely tied to a networking stack.

## Slide 29: Radio and software radio
Wireless receivers (radios) perform several basic functions:
  Demodulate the signal.
  Detection bits.
  Correct errors.
Software radio performs at least some of these functions using software on CPUs.
Software defined radio (SDR) may be all software or a mix of HW and SW.

## Slide 30: SDR Forum tiers of software-defined radio
0. Hardware radio, not programmable.
1. Software-controlled radio does not perform basic modulation/filtering in software.
2. Software-defined radio may cover a wide range of techniques and several modulation methods.
3. Ideal software-defined radio goes straight from A/D conversion to software.
4. Ultimate software radio is lightweight, low power/energy, requires no external antenna.

## Slide 31: Radio operations
Modulation:
  Combinations of modulation variables (frequency, phase, amplitide) form symbols.
  Symbols may be viewed as a constellation.
Error correction:
  Performed on raw bit stream to produce data payload.
  Basic techniques like parity are often not powerful enough for noisy radio channels.
  Viterbi method is widely used.
  Example high-performance codes: turbo coding, low-density parity check (LDPC).

## Slide 32: Radios and networks
Radio may need to support an existing network (Internet, etc.).
Radio may use its own network for coordination (cell phones).
A data network may be designed to take advantage of the unique characteristics of radios (sensor networks).

## Slide 33: Example: cdma2000
Spread-spectrum for cell phones.
  Uses direct-sequence spread spectrum.
Forward
Error
Correction
Coder
Interleaver
Modulator
Spreader
data
Forward channel (transmitter)
Forward
Error
Correction
Decoder
Denterleaver
Demodulator
Despreader
data
Reverse channel (receiver)

## Slide 34: Multimedia
Image compression: Each image is coded separately.
Video compression: Takes advantage of correlation between successive frames.
Perceptual coding: lossy coding, throws away information that will not be noticed.

## Slide 35: JPEG
Discrete cosine transform (DCT) performed on 8 x 8 blocks typically, puts image into frequency domain.
Quantization determines what image data to throw out.
Lossless coding reduces the size of the representation.
Discrete
Cosine
Transform
Quantization
Lossless
coding
01001001000
image
compressed
image
data

## Slide 36: JPEG zigzag pattern
After quantization, transform coefficients must be sent to lossless coder.
Sending coefficients in zigzag pattern moves from low to high spatial frequencies.
High frequency coefficients are more likely to be zero, producing strings that are easier to Huffman code.

## Slide 37: Video compression standards
Makes use of image compression techniques.
Adds:
  Support for frame-to-frame coding.
  Audio streams, data, etc. controlled by a system steram.
Two major families:
  MPEG for broadcasting.
  H.26x for videoconferencing.
H.264/AVC combines techniques from both traditions.

## Slide 38: MPEG-1/2 style compression

## Slide 39: Motion estimation
Motion estimation compares one frame to another frame.
  Generally performed on 16 x 16 macroblocks.
Use 2-D correlation to find new position of a macroblock in the other frame.
Transmit a motion vector to describe motion.
SAD = Sx Sy | S(x,y) – R(x,y) |

## Slide 40: Audio encoding
Perceptual coding models the human auditory system to predict what information can be thrown away.
Subband decomposition helps improve the compression ratio.
MP3 = MPEG-1 Audio Layer 3.