## Slide 1: Chapter 1, part 2: Embedded and Cyber-Physical Computing
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Design methodologies.
Methodologies and standards.

## Slide 3: Design goals
Functional requirements: input/output relations.
Non-functional requirements: cost, performance, power, etc.
Some project goals may be difficult to measure.

## Slide 4: Aspects of performance
Embedded system performance can be measured in many ways:
  Average vs. worst/best-case.
  Throughput vs. latency.
  Peak vs. sustained.
Digital control systems are sampled.
  Sample period determines deadline, latency.

## Slide 5: Energy/power
Energy consumption is important for battery life.
Power consumption is important for heat generation or for generator-powered systems (vehicles).

## Slide 6: Cost
Manufacturing cost must be paid off across all the systems.
  Hardest in small-volume applications.
Manufacturing cost is incurred for each device.
Lifetime costs include software and hardware maintenance and upgrades.

## Slide 7: Other design attributes
Design time must be reasonable. May need to finish by a certain date.
System must be reliability; reliability requirements differ widely.
Quality includes reliability and other aspects: usability, durability, etc.
Systems that must be certified must use certifiable, documented design processes.

## Slide 8: Design methodology
Design methodology: a procedure for creating an implementation from a set of requirements.
Methodology is important in embedded computing:
  Must design many different systems.
  We may use same/similar components in many different designs.
  Design time, results must be predictable.

## Slide 9: Embedded system design challenges
Design space is large and irregular.
We don’t have synthesis tools for many steps.
Can’t simulate everything.
May need to build special-purpose simulators quickly.
Often need to start software development before hardware is finished.

## Slide 10: Design complexity vs. designer productivity

## Slide 11: Basic design methodologies
Figure out flow of decision-making.
Determine when bottom-up information is generated.
Determine when top-down decisions are made.

## Slide 12: Waterfall and spiral models

## Slide 13: Hardware design flow

## Slide 14: Modeling in hardware
Technology databases capture manufacturing process information.
Cell libraries describe the cells used to compose designs.
Logic synthesis systems use routability and timing models.

## Slide 15: Hardware/software co-design flow

## Slide 16: Platform-based design
Platform includes hardware, supporting software.
Two stage process:
  Design the platform.
  Use the platform.
Platform can be reused to host many different systems.

## Slide 17: Platform design
Turn system requirements and software models into detailed requirements.
  Use profiling and analysis tools to measure existing executable specifications.
Explore the design space manually or automatically.
Optimize the system architecture based on the results of simulation and other steps.
Develop hardware abstraction layers and other software.

## Slide 18: Programming platforms
Programming environment must be customized to the platform:
  Multiple CPUs.
  Specialized memory.
  Specialized I/O devices.
Libraries are often used to glue together processors on platforms.
Debugging environments are a particular challenge.

## Slide 19: Standards-based design methodologies
Standards enable large markets.
Standards generally allow products to be differentiated.
  Different implementations of operations, so long as I/O behavior is maintained.
  User interface is often not standardized.
Standard may dictate certain non-functional requirements (power consumption), implementation techniques.

## Slide 20: Reference implementations
Executable program that complies with the I/O behavior of the standard.
  May be written in a variety of language.
In some cases, the reference implementation is the most complete description of the standard.
Reference implementation is often not well-suited to embedded system implementation:
  Single process.
  Infinite memory.
  Non-real-time behavior.

## Slide 21: Designing standards-based systems
Design and implement system components that are not part of the standard.
Perform platform-independent optimizations.
Analyze optimized version of reference implementation.
Design hardware platform.
Optimize system software based on platform.
Further optimize platform.
Test for conformity to standard.

## Slide 22: H.264/AVC
Implements video coding for a wide range of applications:
  Broadcast and videoconferencing.
  Cell phone-sized screens to HDTV.
Video codec reference implementation contains 120,000 lines of C code.

## Slide 23: Design verification and validation
Showing that the design is correct and fixing bugs often takes more time than initial design.
Design correctness activities:
  Testing exercises an implementation with stimuli and observed outputs.
  Validation compares implementation to requirements or spec.
  Verification compares the design at one level of abstraction to another.

## Slide 24: V&V techniques
Simulation uses software/hardware models to compute outputs from inputs.
  Simulator-in-the-loop integrates a simulator of a physical plant with cyber controllers.
Formal methods perform proofs: equivalence, properties, etc.
Manual methods such as code reviews, walkthroughs, and inspections have been shown to catch many bugs.

## Slide 25: A methodology of methodologies
Embedded systems include both hardware and software.
  HW, SW have their own design methodologies.
Embedded system methodologies control the overall process, HW/SW integration, etc.
  Must take into account the good and bad points of hardware and software design methodologies used.

## Slide 26: Useful methodologies
Software performance analysis.
Architectural optimization.
Hardware/software co-design.
Network design.
Software verification.
Software tool generation.

## Slide 27: Joint algorithm and architecture development
Some algorithm design is necessarily performed before platform design.
Algorithm development can be informed by platform architecture design.
  Performance/power/cost trade-offs.
  Design trends over several generations.