## Slide 1: Chapter 1, part 3: Embedded and Cyber-Physical Computing
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Models of computation:
  Motivation.
  Turing machines.
  Data flow models.
  State and control.
  Parallelism and communication.
Reliability, safety, and security.
Consumer electronics.

## Slide 3: Models of computation
Models of computation affect programming style.
  No one model of computation/programming language is good for all algorithms and systems.
Large systems may require different models of computation for different parts.
  Models must communicate compatibly.

## Slide 4: Styles of programming languages and models of computation
Halting vs. non-halting:
  Turing machines, C programs are designed to finish and halt. Digital filters handle infinite data streams and never halt.
Finite vs. infinite state:
  Mode-based controllers are finite. Some on-line modeling algorithms create unlimited states.
Control vs. data:
  Filtering vs. multiple modes.
Sequential vs. parallel:
  C has a sequential model of execution; other languages explicitly capture parallelism.

## Slide 5: Heterogeneity and interoperability
Many systems require mixing several models of comptuation:
  Engine controller uses Kalman filtering but also has mulitple modes (warm-up, cruise, hill-climb, etc.)
Heterogeneous programming mixes languages with different models of comptuation.
Requires careful verification at the interfaces.

## Slide 6: Turing machine
1
0
1
0
1
0
1
0
1
1
0
1
1
0
General model of computing:
program
head
tape
state

## Slide 7: Turing machine step
Read current square.
Erase current square.
Take state-dependent action:
  Print new value.
  Move to adjacent cell.
  Set machine to next state.

## Slide 8: Turing machine properties
Example program:
  If (state = 2 and cell = 0): print 0, move left, state = 4.
  If (state = 2 and cell = 1): print 1, move left, state = 3.
Can be implemented on many physical devices.
Turing machine is a general model of computability.
Can be extended to probabilistic behavior.

## Slide 9: Turing machine properties
Infinite tape = infinite state machine.
Basic model of computability.
  Lambda calculus is alternative model.
  Other models of computing can be shown to be equivalent/proper subset of Turing machine.

## Slide 10: Signal flow graphs and digital filters
signal flow graph
IIR filter

## Slide 11: Data flow graph
Partially-ordered computations:
+
-
*
+ -, *
+, -, *
-, +, *

## Slide 12: Data flow streams
Captures sequence but not time.
Totally-ordered set of values.
  New values are appended at the end as they appear.
May be infinite.
+
88 -23 7 44 9 -28
-44 88 -23 7 44 9

## Slide 13: Firing rules
A node may have one or more firing rules.
Firing rules determine when tokens are consumed and produced.
  Firing consumes a set of tokens at inputs, generates token at output.

## Slide 14: Example firing rules
Basic rule fires when tokens are available at all inputs:
Conditional firing rule depends on control input:
+
a
b
c
a
b
T

## Slide 15: Data flow graph properties
Finite state model.
Basic data flow graph is acyclic.
Scheduling provides a total ordering of operations.

## Slide 16: Synchronous data flow
Lee/Messerschmitt: Relate data flow graph properties to schedulability.
  Synchronous communication between data flow nodes.
  Nodes may communicate at multiple rates.

## Slide 17: SDF notation
Nodes may have rates at which data are produced nor consumed.
Edges may have delays.
+
-
1
2
5

## Slide 18: SDF example
This graph has consistent sample rates:
+
+
2
1
+
1
1
2
1
separate
outputs

## Slide 19: Delays in SDF graphs
Delays do not change rates, only the amount of data stored in the system.
Changes system start-up.
+
-
1
2
5
0

## Slide 20: Kahn processes
Process has unbounded FIFO at each input:
Each channel carries a possibly infinite sequence or stream.
A process maps one or more input sequences to one or more output sequences.
process
channel

## Slide 21: Kahn process network

## Slide 22: Properties of processes
Processes are usually required to be continuous: least upper boundedness can be moved across function boundary.
Monotonicity:
  X in X’ => F(X) in F(X’)

## Slide 23: Networks of processes
A network of processes relates the streams of several processes.
If I = input sequences, X = internal sequences + outputs, then network behavior fixed point is
  X = F(X,I)

## Slide 24: Network properties
A network of monotonic processes is a monotonic process.
  Even in the presence of feedback loops.
Can add nondeterminism in several ways:
  allow process to test for emptiness;
  allow process to be internally nondeterminate;
  allow more than one process to consume data from a channel;
  etc.

## Slide 25: Finite state machine
State transition graph and table are equivalent:
s3
s1
s2
0/0
0/1
1/0
0/0
1/1
1/0
0 | s1 | s2 | 0
1 | s1 | s1 | 0
0 | s2 | s2 | 1
1 | s2 | s3 | 0
0 | s3 | s3 | 0
1 | s3 | s1 | 1

## Slide 26: Finite state machine properties
Finite state.
Nondeterministic variant.

## Slide 27: Nondeterministic FSM
Several transitions out of a state for a given input.
  Equivalent to executing all alternatives in parallel.
Can allow e moves---goes to next state without input.
s1
s2
a
a

## Slide 28: Deterministic FSM from nondeterministic FSM
Add states for the various combinations of nondeterminism.
s1
s2
a
a
s3
nondeterministic
b
s4
c
s1
s12
a
s3
b
s4
c
c
deterministic

## Slide 29: Control flow graph
Commonly used to model program structure.
x = a - b
i = 0?
y = c + d
x = a

## Slide 30: CDFG properties
Finite state model.
Single thread of control.
Can handle subroutines.

## Slide 31: Task graph
Used to model multi-rate systems.
t1
t2
P1
P2
P3
P4
P5

## Slide 32: Task graph properties
Not a Turning machine.
  No branching behavior.
  May be extended to provide conditionals.
Possible models of execution time:
  Constant.
  Min-max bounds.
  Statistical.
Can model late arrivals, early departures by adding dummy processes.

## Slide 33: Petri net
Parallel model of computation.
place
arc
token
transition

## Slide 34: Firing rule
A transition is enabled if each place at its inputs have at least one token.
  A transition doesn’t have to fire right away.
Firing a transition removes tokens from inputs and adds a token to each output place.
In general, may require multiple tokens to enable.

## Slide 35: Properties of Petri nets
Turing complete.
Arbitrary number of tokens.
  Nondeterministic behavior.
  Naturally model parallelism.

## Slide 36: Processor graph
M1
L1
M2
M3
M4
L2
L3

## Slide 37: Communicating FSMs
Control can be composed from several machines.
System behavior is defined by Cartesian product of states and transitions.
M1
M2

## Slide 38: Synchronous and asynchronous communication in FSMs

## Slide 39: Statecharts
Ancestor of UML state diagrams.
Provided composite states:
  OR states;
  AND states.
Composite states reduce the size of the state transition graph.

## Slide 40: Statechart OR state
S1
S2
S3
S4
i1
i1
i2
i2
i2
traditional
S1
S2
S3
S4
i1
i1
i2
OR state
s123

## Slide 41: Statechart AND state
S1-3
S1-4
S2-3
S2-4
S5
traditional
c
d
b
a
r
c
d
b
a
S1
S3
S2
S4
S5
AND state
c
d
r
b
a
sab
r

## Slide 42: TCAS II specification
TCAS II: aircraft collision avoidance system.
Monitors aircraft and air traffic info.
Provides audio warnings and directives to avoid collisions.
Leveson et al used RMSL language to capture the TCAS specification.

## Slide 43: RMSL
State description:
Transition bus for transitions between many states:
state1
inputs
state description
outputs
a
b
c
d

## Slide 44: TCAS top-level description
CAS
power-off
power-on
Inputs:
TCAS-operational-status {operational,not-operational}
fully-operational
C
standby
own-aircraft
other-aircraft i:[1..30]
mode-s-ground-station i:[1..15]

## Slide 45: Own-Aircraft AND state
CAS
Inputs:
own-alt-radio: integer standby-discrete-input: {true,false}
own-alt-barometric:integer, etc.
Effective-SL
Alt-SL
Alt-layer
Climb-inibit
Descend-inibit
Increase-climb-inibit
Increase-Descend-inibit
Advisory-Status
...
...
...
...
...
...
...
1
2
7
...
1
2
7
Outputs:
sound-aural-alarm: {true,false} aural-alarm-inhibit: {true, false}
combined-control-out: enumerated, etc.

## Slide 46: Reliability, safety, and security
Reliable/dependable system design: design system to operate in the face of internal or external problems.
Safety-critical system design: system operates safely under (almost) all possible scenarios.
Security: primarily deals with malicious attacks.

## Slide 47: Dependability and security
dependability
security
reliability
safety
maintainability
confidentiality
availability
integrity

## Slide 48: Faults
Reliable systems recover from faults.
Faults may be permanent or transient:
  Physical faults (manufacturing defects, radiation hazards, etc.)
  Design faults (improper design).
  Operational faults (human error, security breaches, bad human-computer interface, etc.)

## Slide 49: Reliability metrics
Reliability function R(t) is probability that system will operate correctly in interval .
  R(0) = 1, decreases monotonically with time.
Mean time to failure (MTTF):
Hazard function z(t) is failure rate of components computed from failure probability:

## Slide 50: Fault models
Fault rates may be modeled probabilistically or measured emperically.
Typical model is exponential distribution:
Weibull distribution (shape parameter , scale parameter ):

## Slide 51: Bathtub fault model
Infant mortality at start of lifetime due to marginal manufacturing.
Higher reliability in middle timeline.
Increased failures in long term due to wear.

## Slide 52: Results of a fault
Fail: many systems do not attempt to detect errors.
Detect: may provide diagnostic info.
Correct: memory parity, etc.
Recover: rollback, etc.
Contain: keep failure from corrupting other parts of the system.
Reconfigure: reallocate operations to other parts of the sytsem.
Restart.
Repair.

## Slide 53: Reliability methods
Error correction codes: widely used in memory.
Voting systems:
  Triple modular redundancy uses three units to compute function, takes majority result.
Watchdog timer:
  Timer must be reset periodically by OS; if not reset, interrupts to failure routine.
Design diversity: use hardware and software from multiple sources.
triple modular redundancy
Watchdog timer

## Slide 54: Attacks on embedded systems
IT systems use passwords, restricting physical access, etc.
Many embedded systems are physically accessible.
Internet-enabled embedded systems are vulnerable to many Internet bugs.
Flash-programmable embedded devices can be maliciously programmed: cars, etc.
Battery attack: cause activity that drains battery.
Denial-of-service.

## Slide 55: Sensor network denial-of-service attacks [Woo02]
Physical layer: jamming, tampering.
Link layer: collision, exhaustion, unfairness.
Network and routing layer: neglectd and greed, horning, misdirection, black holes, authorization, probing, redundancy.
Transport layer: flooding, desynchronization.

## Slide 56: Power attack
Logic transitions cause activity on power supply signals.
Power attack infers internal state based on power supply signals.
  Simple power analysis: examine trace manually, infer state based on knowledge of CPU function.
  Differential power analysis: correlate multiple runs to infer state.
Has been successfully demonstrated on smart cards.

## Slide 57: Physically unclonable functions (PUFs)
VLSI manufacturing shows parameter variations between chips and wafers.
Use circuit sensitive to certain parameters to generate a unique digital signature for the chip.

## Slide 58: Consumer electronics architectures
Even simple systems must support a variety of functions to provide a useful function:
  File system for music player.
Many consumer electronics devices are networked.

## Slide 59: Bluetooth
Personal area network.
Basic range of 2 meters, good antenna can range up to 30 meters.
One master, up to 7 slaves.
RFCOMM is Bluetooth serial protocol.
Bluetooth Smart provides low-energy operation.
Bluetooth transport protocols

## Slide 60: Networked home entertainment
Host computer stores music, images, etc.
Some devices are permanently attached to host.
Mobile devices may dock with host.
Devices may dock wirelessly.

## Slide 61: High-level services
Service discovery: Jini allows devices to publish services, give leases on devices for services.
Digital rights management (DRM) protects content (music, video, etc.)