## Slide 1: Chapter 1, part 4: Embedded and Cyber-Physical Computing
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Reliability, safety, and security.
Consumer electronics.

## Slide 3: Related disciplines
Reliable/dependable system design creates systems that function even in the face of internal or external errors.
Security concentrates on malicious attacks.
Safety-critical system design develops methods to ensure that systems operate safely under a wide variety of error conditions.

## Slide 4: Dependability and security
After Avizienis et al. [Avi04]

## Slide 5: Attributes of dependability and security (Avizienis et al.)
Availability of correct service.
Continuity of correct service.
Safety from catastrophic consequences.
Integrity from improper system alterations.
Maintainability through modification or repairs.
Confidentiality of information.

## Slide 6: Reliability requirements on embedded systems
Safety-critical or high-reliability applications:
  Automotive.
  Aviation.
  Medicine.
  Critical communications.
Many high-reliability applications require distributed embedded systems.
Embedded systems may be vulnerable to new types of attacks.

## Slide 7: Faults
Faults may cause errors; reliable systems recover from faults.
A fault may be transient or permanent.
Types of faults:
  Physical faults from manufacturing defects, radiation hazards, etc.
  Design faults.
  Operational faults from human error, security breaches, etc.

## Slide 8: System reliability metrics
Mean time to failure (MTTF) is the expected time for first system to fail:
Reliability function describes the probability that the system will operate correctly in the time interval [0,t].
Hazard function is the failure rate of components:

## Slide 9: Common fault distributions
Exponential distribution:
Weibull distribution:
Bathtub distributions are often empirically observed.
  High failure rates at beginning, end of component life.

## Slide 10: Possible actions after a fault
Fail.
Detect.
Correct.
Recover.
Contain.
Reconfigure.
Restart.
Repair.

## Slide 11: Reliability methods
Error-correction codes.
Voting systems.
  Triple-modular redundancy uses majority voting.
Watchdog timer must be periodically reset by system to show that system operates correctly.
Design diversity uses redundancy implemented in different types of components.

## Slide 12: Novel attacks and countermeasures
Embedded systems provide physical access, a key avenue for attack.
Internet-enabled embedded systems provide remote access to attackers.
  Example: Internet-enabled automobiles.
Battery attacks exercise the system to wear out a battery.
Quality-of-service attacks interfere with real-time behavior.

## Slide 13: Sensor network attacks (Wood and Stankovic)
Physical layer: jamming, tampering.
Link layer: collision, exhaustion, unfairness.
Network and routing layers: neglect and greed, horning, misdirection, authorization, probing, redundancy.
Transport layer: flooding, desynchronization.

## Slide 14: Power attack
Developed by Kocher et al.
Measure CPU current to determine instructions, data.
High-leakage devices are less vulnerable to power attacks.

## Slide 15: Consumer electronics architectures
Consumer electronics pushes the edge of the envelope in several directions:
  Complex functionality and high performance.
  Often battery-powered.
  Very low cost.
Generally include one or more standards.

## Slide 16: Bluetooth
Personal-area network.
  2.5 GHz band.
  Generally within 2 meters, may be extended to 30 meters.
Basic network is master-slave, but higher levels of protocol stack provide peer-to-peer operation.

## Slide 17: Bluetooth stack

## Slide 18: Bluetooth middleware group protocols
RFCOMM provides serial interface; compatible with RS-232.
Service discovery protocol discovers services (printing, etc.) on the network.

## Slide 19: Networked consumer appliances
PC acts as a host.
Some devices are semipermanently connected (USB); others are on wired Ethernet; others are on wireless networks.
Devices must be configured properly with the system.

## Slide 20: High-level services
Service discovery allows the device to find another device on the network that will provide a service (for example, printing).
  Jini lookup services hold service proxies.
  Jini uses join protocol to add a service.
  Jini client obtains a lease for a given service.

## Slide 21: Digital rights management
Digital rights management (DRM) is used to ensure that copyrighted material is used within the terms required by owner.
  Devices that can play material.
  Number of times material can be played.
  Expiration date.