## Slide 1: Chapter 2, part 1: CPUs
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
CPU metrics.
Categories of CPUs.
CPU mechanisms.

## Slide 3: Performance as a design metric
Performance = speed:
  Latency.
  Throughput.
Average vs. peak performance.
Worst-case and best-case performance.

## Slide 4: Other metrics
Cost (area).
Energy and power.
Predictability.
Security.

## Slide 5: Flynn’s taxonomy of processors
Single-instruction single-data (SISD): RISC, etc.
Single-instruction multiple-data (SIMD): all processors perform the same operations.
Multiple-instruction multiple-data (MIMD): homogeneous or heterogeneous multiprocessor.
Multiple-instruction multiple data (MISD).

## Slide 6: Other axes of comparison
RISC vs. CISC---Instruction set style.
Instruction issue width.
Static vs. dynamic scheduling for multiple-issue machines.
Vector processing.
Multithreading.

## Slide 7: Embedded vs. general-purpose processors
Embedded processors may be optimized for a category of applications.
  Customization may be narrow or broad.
We may judge embedded processors using different metrics:
  Code size.
  Memory system performance.
  Preditability.

## Slide 8: RISC processors
RISC generally means highly-pipelinable, one instruction per cycle.
Pipelines of embedded RISC processors have grown over time:
  ARM7 has 3-stage pipeline.
  ARM9 has 5-stage pipeline.
  ARM11 has eight-stage pipeline.
ARM11 pipeline [ARM05].

## Slide 9: RISC processor families
ARM: ARM7 is relatively simple, no memory management; ARM11 has memory management, other features.
MIPS: MIPS32 4K has 5-stage pipeline; 4KE family has DSP extension; 4KS is designed for security.
Power Architecture: separate embedded and server feature sets; AltiVec vector architecture; SIMD signal processing engine; variable length encoding (VLE) engine.
Intel: Atom designed for mobile and low-power; virtualization, hyper-threading, thermal management.

## Slide 10: Digital signal processors
First DSP was AT&T DSP16:
  Hardware multiply-accumulate unit.
  Harvard architecture.
Today, DSP is often used as a marketing term.
Modern DSPs are heavily pipelined.

## Slide 11: Example: TI C5x DSP
40-bit arithmetic unit (32-bit values with 8 guard bits).
Barrel shifter.
17 x 17 multiplier.
Comparison unit for Viterbi encoding/decoding.
Single-cycle exponent encoder for wide-dynamic-range arithmetic.
Two address generators.

## Slide 12: TI C55x microarchitecture

## Slide 13: TI C55x pixel interpretation co-processor
Designed to support motion estimation.
Interpolates U, M, R values given A, B, C, D pixels.
Instruction support:
  ACy = copr(K8,AC,Lmem) loads pixels and computes.
  ACy = copr(K8,Acx,Lmem)||Lmem=Acz loads pixels, computes, stores
A
U
B
M
R
C
D

## Slide 14: TI C55x motion estimation co-processor
Produces either one motion vector for 16 x 16 macroblock or four motion vectors for four 8 x 8 blocks:
  [Acx,Acy] = copr(K8,ACx,ACy,Xmem,Ymem,Coeff)
  ACx and ACy are accumulated sum-of-differences
  K8 is control bits
  Xmem, Ymem point to odd and even lines of search window

## Slide 15: TI C55x DCT co-processor
Performs 1-D 8x8 DCT.
Pipelines several DCT iterations.

## Slide 16: Parallelism extraction
Static:
  Use compiler to analyze program.
  Simpler CPU.
  Can make use of high-level language constructs.
  Can’t depend on data values.
Dynamic:
  Use hardware to identify opportunities.
  More complex CPU.
  Can make use of data values.

## Slide 17: Simple VLIW architecture
Large register file feeds multiple function units.
Register file
E box
Add r1,r2,r3; Sub r4,r5,r6; Ld r7,foo; St r8,baz; NOP
ALU
ALU
Load/store
Load/store
FU

## Slide 18: Clustered VLIW architecture
Register file, function units divided into clusters.
Execution
Register file
Execution
Register file
Cluster bus

## Slide 19: TI C62/C67
Up to 8 instructions/cycle.
32 32-bit registers.
Function units:
  Two multipliers.
  Six ALUs.
All instructions execute conditionally.

## Slide 20: TI C6x data operations
8/16/32-bit arithmetic.
40-bit operations.
Bit manipulation operations.

## Slide 21: C6x system
On-chip RAM.
32-bit external memory: SDRAM, SRAM, etc.
Host port.
Multiple serial ports.
Multichannel DMA.
32-bit timer.

## Slide 22: C6x block diagram
Data path 1/
Reg file 1
Data path 2/
Reg file 2
Execute
DMA
timers
Serial
Program RAM/cache
512K bits
Data RAM
512K bits
JTAG
PLL
bus

## Slide 23: C6x data paths
General-purpose register files (A and B, 16 words each).
Eight function units:
  .L1, .L2, .S1, .S2, .M1, .M2, .D1, .D2
Two load units (LD1, LD2).
Two store units (ST1, ST2).
Two register file cross paths (1X and 2X).
Two data address paths (DA1 and DA2).

## Slide 24: C6x function units
.L
  32/40-bit arithmetic.
  Leftmost 1 counting.
  Logical ops.
.S
  32-bit arithmetic.
  32/40-bit shift and 32-bit field.
  Branches.
  Constants.
.M
  16 x 16 multiply.
.D
  32-bit add, subtract, circular address.
  Load, store with 5/15-bit constant offset.

## Slide 25: Motorola Starcore SC140
DALU includes 4 ALUs, 1 register file.
AGU includes 2 address arithmetic units (AAU), 1 address register file.
Program sequencer and control unit (PSEQ).
Performance:
  4 million MACs per second per MHz clock.
  10 RISC MIPS per MHz clock.

## Slide 26: Typical SC140 configuration
Level 1 memory expansion
RAM, ROM
peripherals
DMA,
Cache,
Interrupts,
Level 2 mem,
Etc.
Program sequencer
ALU
ALU
ALU
ALU
AAU
AAU

## Slide 27: SC140 Core
Program
sequencer
Power
mgt
Clock/PLL
AGU
DALU
Address
Register file
2 AAUs
BMU
Data
Register file
4 ALUs

## Slide 28: Instruction format
16-bit instructions.
Up to 6 instructions per cycle.
Instructions are grouped to define allowable simultaneous operations.
MACR –D0,D1,D7
AND D4,D5
MOVE.L (R0),+N0,R6
ADDA R2,R3
DALU
AGU

## Slide 29: AGU addressing
Allowable addressing modes:
  Linear.
  Modulo.
  Reverse-carry.
  Automatic updating during register indirect.
  Stack.
Array addressing: base, offsett, modifier registers.

## Slide 30: Motorola MC8126 multiprocessor
Four SC140 cores.
  224 KB M1 memory with zero wait states.
Shared M2 memory.
  476 KB running at core frequency.
  M2-accessible multi-core bus.
64/32-bit data, 32-bit address 60x bus.
Eight-bank memory controller.
Hardware semaphores.

## Slide 31: TM-1 characteristics
Characteristics
  Floating point support
  Sub-word parallelism support
  If Conversion
  Additional custom operations

## Slide 32: Trimedia TM-1
memory interface
video in
audio in
I2C
timers
image co-p
PCI
video out
audio out
serial
VLD co-p
VLIW CPU

## Slide 33: TM-1 VLIW CPU
register file
read/write crossbar
FU1
FU27
slot 1
slot 2
slot 3
slot 4
slot 5
...

## Slide 34: Superscalar processors
Instructions are dynamically scheduled.
  Dependencies are checked at run time in hardware.
Used to some extent in embedded processors.
  Embedded Pentium is two-issue in-order.

## Slide 35: SIMD and subword parallelism
Many special-purpose SIMD machines.
Subword parallelism is widely used for video.
  ALU is divided into subwords for independent operations on small operands.
Vector processing is widely used for integer values.

## Slide 36: Multithreading
Low-level parallelism mechanism.
Hardware multithreading alternately fetches instructions from separate threads.
Simultaneous multithreading (SMT) fetches instructions from several threads on each cycle.

## Slide 37: Example: Sandbridge Sandblaster

## Slide 38: GPUs
Graphics processing units (GPUs) are widely used in desktop/laptop systems and increasingly used in cell phones.
SIMD architecture maps onto frame buffer.
screen
frame buffer
PE
PE
PE
PE
PE
PE
GPU

## Slide 39: NVIDID Fermi architecture
Three types of processing units:
  cores, load/store, special function;
  controlled by warp scheduler/dispatch.
Warp is group of 32 parallel threads.
Register file, shared memory, L1 and uniform cache for data.
instruction cache
Warp scheduler/ dispatch
Warp scheduler/ dispatch
register file
cores
load/ stores
special function units
Interconnection network
shared memory/L1 cache
uniform cache

## Slide 40: CUDA core architecture
Thread is most basic unit of programming.
  Each thread has its own PC, registers, private memory, inputs, outputs.
Thread block is set of threads with block ID that share memory.
Grid is an array of thread blocks executing on same kernel, sharing global memory.
dispatch port
operand collector
result queue
floating point unit
integer unit

## Slide 41: Available parallelism in multimedia applications (Talla et al.)

## Slide 42: Operand characteristics in MediaBench (Fritts)

## Slide 43: Dynamic behavior of loops in MediaBench (Fritts)
Path ratio = (instructions executed per iteration) / (total number of loop instructions).
MediaBench shows small path ratio -> considerable conditional behavior in loops.

## Slide 44: Dynamic voltage scaling (DVS)
Power scales with V2 while performance scales roughly as V.
Reduce operating voltage, add parallel operating units to make up for lower clock speed.
DVS doesn’t work in high-leakage processors.

## Slide 45: Dynamic voltage and frequency scaling (DVFS)
Scale both voltage and clock frequency.
Can use control algorithms to match performance to application, reduce power.

## Slide 46: Razor architecture
Used specialized latch to detect errors.
Recovers only on errors, gains average-case performance.