## Slide 1: Chapter 2, part 2: CPUs
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Memory systems.
  Memory component models.
  Caches and alternatives.
Code compression.

## Slide 3: Generic memory block

## Slide 4: Simple memory model
Core array is n rows x m columns.
Total area .
Row decoder area Ar = arm.
Core area Ax = axmn.
Precharge circuit area Ap = apm.
Column decoder area Ac = acm.

## Slide 5: Simple energy and delay models
.
Total energy E = ED + ES.
  Static energy component ES is a technology parameter.
  Dynamic energy ED = Er + Ex + Ep + Ec.

## Slide 6: Multiport memories
structure
Delay vs. memory size
and number of ports.

## Slide 7: Kamble and Ghose cache power model
Cache is m-way set-associative, capacity of D bytes, T bits of tag and L bytes of line, St status bits per block frame.
Bit line energy:

## Slide 8: Kamble/Ghose, cont’d.
Word line energy:
Output line energy:
Address input lines:

## Slide 9: Shiue and Chakrabarti cache energy model
add_bs: number of transitions on address bus per instruction.
data_bs: number of transitions on data bus per instruction.
word_line_size: number of memory cells on a word line.
bit_line_size: number of memory cells on a bit line.
Em: Energy consumption of a main memory access.
a, b, g: technology parameters.

## Slide 10: Shiue/Chakrabarti, cont’d.

## Slide 11: Memory arrays
Build large memory from multiple blocks.
  Can provide long words or taller memory, depending on address bits.
  Separate address bits provide multiple banks.
mem
b
mem
b
adrs

## Slide 12: Memory controller
Memory controller sits between CPU/bus and DRAM:
  Hides details of DRAM timing parameters.
  Small queues allow reordering of requests to maximize performance.
McKee et al. proposed combination of compile-time detection of streams with run-time scheudling.
Rixner et al. used one buffer per bank to hold pending references.
Lee et al. proposed layered architecture: performance-oriented vs. SDRAM refresh, etc.
Cho et al. proposed accuracy-aware SRAM for mobile multimedia:
  Errors in low-order bits cause less perceptual damage to image.
  Reducing power supply voltage gives quadratic reduction in energy.
  Architecture allows column-by-column changes to power supply voltage.

## Slide 13: Register files
First stage in the memory hierarchy.
When too many values are live, some values must be spilled onto main memory and read back later.
  Spills cost time, energy.
Register file parameters:
  Number of words.
  Number of ports.

## Slide 14: Performance and energy vs. register file size.
[Weh01] © 2001 IEEE

## Slide 15: Cache size vs. energy
[Li98]
© 1998 IEEE

## Slide 16: Cache parameters
Cache size:
  Larger caches hold more data, burn more energy, take area away from other functinos.
Number of sets:
  More independent references, more locations mapped onto each line.
Cache line length:
  Longer lines give more prefetching bandwidth, higher energy consumption.

## Slide 17: Wolfe/Lam classification of program behavior in caches
Self-temporal: same array element is accessed in different loop iterations.
Self-spatial reuse: same cache line is accessed in different loop iteraitons.
Group-temporal reuse: different parts of the program access the same array element.
Group-spatial reuse: different parts of the program access the same cache line.

## Slide 18: Multilevel cache optimization
Gordon-Ross et al adjust cache parameters in order:
  Cache size.
  Line size.
  Associativity.
Design cache size for first level, then second level; line size for first, then second level; associativity for first, then second level.

## Slide 19: Scratch pad memory
Scratch pad is managed by software, not hardware.
  Provides predictable access time.
  Requires values to be allocated.
Use standard read/write instructions to access scratch pad.

## Slide 20: Code compression
Extreme version of instruction encoding:
  Use variable-bit instructions.
  Generate encodings using compression algorithms.
Generally takes longer to decode.
Can result in performance, energy, code size improvements.
IBM CodePack (PowerPC) used Huffman encoding.

## Slide 21: Terms
Compression ratio:
  Compressed code size/uncompressed code size * 100%.
  Must take into account all overheads.

## Slide 22: Wolfe/Chanin approach
Object code is fed to lossless compression algorithm.
  Wolfe/Chanin used Huffman’s algorithm.
Compressed object code becomes program image.
Code is decompressed on-the-fly during execution.
Source code
compiler
Object code
compressor
Compressed
object code

## Slide 23: Wolfe/Chanin execution
Instructions are decompressed when read from main memory.
  Data is not compressed or decompressed.
Cache holds uncompressed instructions.
  Longer latency for instruction fetch.
CPU does not require significant modifications.
CPU
decompressor
cache
memory

## Slide 24: Huffman coding
Input stream is a sequence of symbols.
Each symbol’s probability of occurrence is known.
Construct a binary tree of probabilities from the bottom up.
  Path from room to symbol gives code for that symbol.

## Slide 25: Wolfe/Chanin results
[Wol92] © 1992 IEEE

## Slide 26: Compressed vs. uncompressed code
Code must be uncompressed from many different starting points during branches.
Code compression algorithms are designed to decode from the start of a stream.
Compressed code is organized into blocks.
  Uncompress at start of block.
Unused bits between blocks constitute overhead.
add r1, r2, r3
mov r1, a
bne r1, foo
uncompressed
compressed

## Slide 27: Block structure and compression
Trade-off:
  Compression algorithms work best on long blocks.
  Program branching works best with short blocks.
Labels in program move during compression.
Two approaches:
  Wolfe and Chanin used branch table to translate branches during execution (adds code size).
  Lefurgy et al. patched compressed code to refer branches to compressed locations.

## Slide 28: Branch tables for branch target mapping

## Slide 29: Compression ratio vs. block size
[Lek99b] © 1999 IEEE

## Slide 30: Compression formats
Lefurgy et al. used first four bits to define length of compressed sequence (8, 12, 16, 23 bits).
Ishiura and Yamaguchi automatically extracted fields from instructions to optimze encoding.
Larin and Conte tailored the encoding of fields to the range of values used in that field by the program.

## Slide 31: Pre-cache compression
Decompress as instructions come out of the cache.
One instruction must be decompressed many times.
Program has smaller cache footprint.

## Slide 32: Encoding algorithms
Data compression has developed a large number of compression algorithms.
These algorithms were designed for different constraints:
  Large text files.
  No real-time or power constraints.
Evaluate existing algorithms under the requirements of code compressions, develop new algorithms.

## Slide 33: Energy savings evaluation
Yoshida et al. used dictionary-based encoding.
Power reduction ratio:
  N: number of instructions in original program.
  m: bit width of those instructions.
  n: number of compressed instructions.
  k: ratio of on-chip/off-chip memory power dissipation.

## Slide 34: Arithmetic coding
Huffman coding maps symbols onto the integer number line.
Arithmetic coding maps symbols onto the real number line.
  Can handle arbitrarily fine distinctions in symbol probabilities.
Table-based method allows fixed-point arithmetic to be used.
[Lek99c]
© 1999 IEEE

## Slide 35: Markov models
A Markovian state machine allows us to define conditional probabilities of sequences of symbols.
State in Markov model is a subset of the previously seen sequence.
Transitions out of each state are conditioned on next symbol.
Probabilities of transitions vary from state to state.

## Slide 36: Arithmetic coding and Markov model
Lekatsas and Wolf combined arithmetic coding and Markov models (SAMC).
Markov model has limited depth to avoid blow-up.
  Long bit sequences wrap around both horizontally and vertically.
  Model depth should multiply/divide instruction size.

## Slide 37: Markov model example

## Slide 38: SAMC results
[Lek99a] © 1999 IEEE

## Slide 39: Tunstall coding
Tunstall coding transforms variable-sized strings into equal-sized codes.
Coding three has 2N leaf nodes.
  Depth of tree varies.
Xie and Wolf added Markov model to Tunstall coding.
Allows parallel decoding of segments of the codeword.

## Slide 40: Tunstall/Markov coding results
[Xie02] © 2002 IEEE

## Slide 41: Dictionary-based methods
Liao et al. identified common code sequences, synthesized subroutines.
  Also proposed hardware implementation.
Kirovski et al. proposed a procedure cache for software-controlled code compression.
  Handler maps procedure identifiers to code during execution.
  Handler also manages free space.
Chen at al.: software-controlled Java byte-code compression.
Lefurgy et al. proposed exception mechanism to manage compressed code in the cache.

## Slide 42: Lefurgy et al. execution time vs. instruction cache miss ratio
[Lef00] © 2000 IEEE

## Slide 43: Lefurgy et al. selective compression results

## Slide 44: Code and data compression
Unlike (non-modifiable) code, data must be compressed and decompressed dynamically.
Can substantially reduce cache footprints.
Requires different trade-offs.

## Slide 45: Lempel-Ziv algorithm
Dictionary-based method.
Decoder builds dictionary during decompression process.
LZW variant uses a fixed-size buffer.
Source
text
Uncompressed
source
Coder
Dictionary
Coder
Dictionary
Compressed
text

## Slide 46: Lempel-Ziv example

## Slide 47: MXT
Tremaine et al. has 3-level cache system.
  Level 3 is shared among several processor, connected to main memory.
  Data and code are compressed/uncompressed as they move between main memory and level 3 cache.
Uses a variant of Lempel-Ziv 1977 algorithm.
  All compression engines share the same dictionary.
  Typically, 1 KB blocks are divided into 256-byte compression blocks.

## Slide 48: Other applications
Benini et al. evaluated energy savings of post-cache decompression.
  Simple dictionary gave 35% energy savings.
Lekatsas et al. combined data and code compression and encryption.
  Modified operating system performs compression, encryption at proper point in memory access process.