## Slide 1: Chapter 2, part 3: CPUs
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Bus encoding.
Security-oriented architectures.
CPU simulation.
Configurable processors.

## Slide 3: Bus encoding
Encode information on bus to reduce toggles and dynamic energy consumption.
  Count energy consumption by toggle counts.
Bus encoding is invisible to rest of architecture.
Some schemes transmit side information about encoding.
mem
CPU
enc
dec
encoded
bus
side
information

## Slide 4: Bus-invert coding
Stan and Burleson: take advantage of correlation between successive bus values.
Choose sending true or complement form of bus values to minimize toggles.
Can break bus into fields and apply bus-invert coding to each field.

## Slide 5: Working zone encoding
Mussoll et al.: working-zone encoding divides address bus into working zones.
  Address in a working zone is sent as an offset from the base in a one-hot code.
[Mus98] © 1998 IEEE

## Slide 6: Address bus encoding
Benini et al: cluster correlated address bits, encode clusters, use combinational logic to encode/decode.
Compute correlation coefficients of transition variables to determine clusters:

## Slide 7: Benini et al. results
[Ben98] © 1998 IEEE

## Slide 8: Dictionary-based encoding
Considers correlations both within a word and between successive words.
ENS(x,y) is 0 if both lines stay the same, 1 if one changes, 2 if both change.
Energy model includes transitions (ET) and interwire (EI).

## Slide 9: Lv et al. pattern frequency results
[Lv03] © 2003 IEEE

## Slide 10: Lv et al. dictionary-based architecture
[Lv03] © 2003 IEEE

## Slide 11: Lv et al. energy savings
[Lv03] © 2003 IEEE

## Slide 12: Security-oriented architectures
A variety of attacks:
  Typical desktop/server attacks, such as Trojan horses and viruses.
  Physical access allows side channel attacks.
Cryptographic instruction sets have been developed for several architectures.
Embedded systems architecture must add protection for side effects, consider energy consumption.

## Slide 13: Smart cards
Used to identify holder, carry money, etc.
Self-programmable one-chip microcomputer architecture:
  Allows processor to change code or data.
  Memory is divided into two sections.
  Registers allow program in one section to modify the other section without interfering with the executing program.

## Slide 14: Secure architectures
MIPS, ARM offer security extensions, including encryption instructions, memory management, etc.
SAFE-OPS embeds a watermark into code using register assignment. FPGA accelerator checks the validity of the watermark during execution.

## Slide 15: Power attacks
Kocher et al.: Adversary can observe power consumption at pins and deduce data, instructions within CPU.
Simple power analysis: manually analyze power supply signal, look for patterns.
Differential power analysis: run experiments, correlate multiple power supply signal traces, identify

## Slide 16: Power attack countermeasures
Yang et al.: Dynamic voltage/frequency scaling (DVFS) can be used as a countermeasure.
  Scrambles power signature by changing frequency, voltage.
  Small performance penalty compared to maximum performance.

## Slide 17: DVFS countermeasure results
[Yan05] © 2005 ACM Press

## Slide 18: Physically unclonable functions
Manufacturing parameters change within a wafer, between wafers.
Can use parameters’ effects on logic performance to generate unique signatures.
Lofstrom et al. used an array of transistors and addressing circuitry; distinguished 1 million signatures with error rate < 10-7.
Lim et al. used an arbiter to compare the delays of two copies of the same function.
  Minimizes the sensitivity of delay measurement to temperature, etc.

## Slide 19: CPU simulation
Performance vs. energy/power simulation.
Temporal accuracy.
Trace vs. execution.
Simulation vs. direct execution.

## Slide 20: Engblom embedded vs. SPEC comparison
[Eng99b]
© 1999 ACM Press

## Slide 21: Trace-based analysis
Instrumentation generates side information.
PC-sampling checks PC value during execution.
Can measure control flow, memory accesses.

## Slide 22: Microarchitecture-modeling simulators
Varying levels of detail:
  Instruction scheduler is not cycle-accurate.
  Cycle timers are cycle-accurate.
Can simulate for performance or energy/power.
Typically written in general-purpose programming language, not hardware description language.

## Slide 23: PC sampling
Example: Unix prof.
Interrupts are used to sample PC periodically.
  Must run on the platform.
  Doesn’t provide complete trace.
  Subject to sampling problems: undersampling, periodicity problems.

## Slide 24: Call graph report
Main 100%
f1
f2
---
f1 37%
g1
g2
---
f2 23%
g3
g4
Cumulative execution time

## Slide 25: Program instrumentation
Example: dinero.
Modify the program to write trace information.
  Track entry into basic blocks.
  Requires editing object files.
  Provides complete trace.

## Slide 26: Cycle-accurate simulator
Models the microarchitecture.
  Simulating one instruction requires executing routines for instruction decode, etc.
Models pipeline state.
  Microarchitectural registers are exposed to the simulator.

## Slide 27: Trace-based vs. execution-based
Trace-based:
  Gather trace first, then generate timing information.
  Basic timing information is simpler to generate.
  Full timing information may require regenerating information from the original execution.
  Requires owning the platform.
Execution-based:
  Simulator fully executes the instruction.
  Requires a more complex simulator.
  Requires explicit knowledge of the microarchitecture, not just instruction execution times.

## Slide 28: Sources of timing information
Data book tables:
  Time of individual instructions.
  Penalties for various hazards.
Microarchitecture:
  Depends from the structure of machine.
  Derived from execution of the instruction in the microarchitecture.

## Slide 29: Levels of detail in simulation
Instruction schedulers:
  Models availability of microarchitectural resources.
  May not capture all interactions.
Cycle timers:
  Models full microarchitecture.
  Most accurate, requires exact model of the microarchitecture.

## Slide 30: Modular simulators
Model instructions through a description file.
  Drives assembler, basic behavioral simulation.
Assemble a simulation program from code modules.
  Can add your own code.

## Slide 31: Early approaches to power modeling
Instruction macromodels:
  ADD = 1 mw, JMP = 2 mw, etc.
Data-dependent models:
  Based on data value statistics.
Transition-based models.

## Slide 32: Power simulation
Model capacitance in the processor.
Keep track of activity in the processor.
  Requires full simulation.
Activity determines capacitive charge/discharge, which determines power consumption.

## Slide 33: SimplePower simulator
Cycle-accurate simulator.
  SimpleScalar-style cycle-accurate simulator.
Transition-based power analysis.
  Estimates energy of data path, memory, and busses on every clock cycle.

## Slide 34: RTL power estimation interface
A power estimator is required for each functional unit modeled in the simulator.
  Functional interface makes the simulator more modular.
Power estimator takes same arguments as the performance simulation module.

## Slide 35: Switch capacitance tables
Model functional units such as ALU, register files, multiplexers, etc.
Capture technology-dependent capacitance of the unit.
Two types of model:
  Bit-independent: each bit is independent, model is one bit wide.
  Bit-dependent: bits interact (as in adder), model must be multiple bits.
Analytical models used for memories.
Adder model is built from sub-model for adder slice.

## Slide 36: Array model
Analytical model:
  Decoder.
  Wordline drive.
  Bitline discharge.
  Sense amp output.
Register file word line capacitance:
  Cdiff (word line driver) + Cgate(cell access)*nbit_lines + Cmetal * Word_line_length

## Slide 37: Bus, function unit models
Bus model based upon length of bus, capacitance of bus lines.
Models for ALUs, etc. based upon transistion models.

## Slide 38: Clock network power model
Clock is a major power sink in modern designs.
Major elements of the clock power model:
  Global clock lines.
  Global drivers.
  Loads on the clock network.
Must handle gated clocks.

## Slide 39: Power and thermal simulation and modeling
Wattch, SimplePower power simulators both built on top of SimpleScalar.
  Adds parameterized power models for the functional units.
HotSpot models thermal characteristics using a floorplan model:
  Ambient temperature , thermal capacitance C, power P.

## Slide 40: Automated CPU design
Customize aspects of CPU for application:
  Instruction set.
  Memory system.
  Busses and I/O.
Tools help design and implement custom CPUs.
FPGAs make it easier to implement custom CPUs.
Application-specific instruction processor (ASIP) has custom instruction set.
Configurable processor is generated by a tool set.M

## Slide 41: Types of customization
New instructions: operations, operands, remove unused instructions.
Specialized pipelines.
Specialized memory hierarchy.
Busses and peripherals.

## Slide 42: Techniques
Architecture optimization tools help choose the instruction set and microarchitecture.
Configuration tools implement the microarchitecture (and perhaps compiler).
Early example: MIMOLA analyzed programs, created microarchitecture and instructions, synthesized logic.

## Slide 43: CPU configuration process

## Slide 44: Tensilica configuration options
© 2004 Tensilica

## Slide 45: Tensilica EEMBC comparison
© 2004 Tensilica

## Slide 46: Tensilica energy consumption by subsystem
© 2006 Tensilica

## Slide 47: Toshiba MePcore

## Slide 48: LISA language
[Hof01] © 2001 IEEE

## Slide 49: LISA descriptions and generation
Memory model includes registers and other memories.
Uses clause binds operations to hardware.
Timing specified by PIPELINE, IN, ACTIVATION, ENTITY.
Generates hierarchical VHDL design.

## Slide 50: PEAS-III
Synthesis driven by:
  Architectural parameters such as number of pipeline stages.
  Declaration of function units.
  Instruction format definitions.
  Interrupt conditions and timing.
  Micro-operations for instructions and interrupts.
Generates both simulation and synthesis models in VHDL.

## Slide 51: Instruction set synthesis
Generate instruction set from application program, other requirements.
Sun et al. analyzed design space for simple BYTESWAP() program.
[Sun04] © 2004 IEEE

## Slide 52: Holmer and Despain
1% rule---don’t add instruction unless it improves performance by 1%.
Objective function (C = # cycles, I = # instruction types, S = # instructions in program):
  100 ln C + I
  100 ln C + 20 ln S + I
Used microcode compaction algorithms to find instructions.

## Slide 53: Other techniques
Huang and Despain used simulated annealing to search the design space.
  Moves could reschedule micro-op, exchange micro-ops, insert or delete time steps.
Kastner et al. used clustering to generate instructions.
  Clusters must cover the program graph.

## Slide 54: Biswas et al.
Biswas et al. used Kernighan-Lin partitioning to find instructions.
Argue against large functions.
[Bis05] © 2005 IEEE Computer Society

## Slide 55: Complex function definition
Atasu et al. try to combine many operations into an instruction:
  Disjoint operator graphs.
  Multi-output instructions.
Operator graph must be convex---value cannot leave, then re-enter the instruction.
[Ata03] © 2003 ACM Press

## Slide 56: Other techniques
Pozzi and Ienne extract large instructions, generating multi-cycle operations and multiple memory ports.
Tensilica Xpres compiler designs instruction sets: operator fusion, vector, etc.

## Slide 57: Limited-precision arithmetic
Fang et al. used affine arithmetic to analyze numerical characteristics of algorithms.
Mahlke synthesize variable bit-width architectures given bit-width requirements.
Cluster operations to find a small number of distinct bit widths.
[Mah01] © 2001 IEEE