## Slide 1: Chapter 3, part 1: Programs
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Code generation and back-end compilation.
Memory-oriented software optimizations.

## Slide 3: Embedded vs. general-purpose compilers
General-purpose compilers must generate code for a wide range of programs:
  No real-time requirements.
  Often no explicit low-power requirements.
  Generally want fast compilation times.
Embedded compilers must meet real-time, low-power requirements.
  May be willing to wait longer for compilation results.

## Slide 4: Code generation steps
Instruction selection chooses opcodes, modes.
Register allocation binds values to registers.
  Many DSPs and ASIPs have irregular register sets.
Address generation selects addressing mode, registers, etc.
Instruction scheduling is important for pipelining and parallelism.

## Slide 5: twig model for instruction selection
twig models instructions, programs as graphs.
Covers program graph with instruction graph.
  Covering can be driven by costs.

## Slide 6: twig instruction models
Rewriting rule:
  replacement<- template {cost} = action
Dynamic programming can be used to cover program with instructions for tree-structured instructions.
  Must use heuristics for more general instructions.

## Slide 7: ASIP instruction description
PEAS-III describes pipeline resources used by an instruction.
Leupers and Marwedel model instructions as register transfers and NOPs. Register transfers are executed under conditions.

## Slide 8: Register allocation and lifetimes

## Slide 9: Clique covering
Cliques in graph describe registers.
  Clique: every pair of vertices is connected by an edge.
Cliques should be maximal.
Clique covering performed by graph coloring heuristics.

## Slide 10: VLIW register files
VLIW register sets are often partitioned.
  Values must be explicitly copied.
Jacome and de Veciana divide program into windows:
  Window start and stop, data path resource, set of activities bound to that resource within the time range.
Construct basic windows, then aggregated windows.
Schedule aggregated windows while propagating delays.

## Slide 11: FlexWare instruction definition
[Lie94] © 1994 IEEE

## Slide 12: Other techniques
PEAS-III categorizes instructions: arithmetic/logic, control, load/store, stack, special.
  Compiler traces resource utilization, calculates latency and throughput.
Mesman et al. modeled code scheduling constraints with constraint graph.
  Model data dependencies, multicycle ops, etc.
  Solve system by adding some edges to fix some operation times.

## Slide 13: Araujo and Malik
Optimal selection/ allocation/ scheduling algorithm for limited architecture---location can have either one or unbounded number available.
Use a tree-grammar paerser to select instructions and allocate registers; use O(n) algorithm to schedule instructions.
[Ara95] © 1995 IEEE

## Slide 14: Constraint graphs and linear inequalities

## Slide 15: Araujo and Malik algorithm
[Ara95] © 1995 IEEE

## Slide 16: Code placement
Place code to minimize cache conflicts.
Possible cache conflicts may be determined using addresses; interesting conflicts are determined through analysis.
May require blank areas in program.

## Slide 17: Code placement in main memory and cache

## Slide 18: Hwu and Chang
Analyzed traces to find relative execution times.
Inline expanded infrequently used subroutines.
Placed frequently-used traces using greedy algorithm.

## Slide 19: McFarling
Analyzed program structure, trace information.
Annotated program with loop execution count, basic block size, procedure call frequency.
Walked through program to propagate labels, group code based on labels, place code groups to minimize interference.

## Slide 20: McFarling procedure inlining
Estimated number of cache misses in a loop:
  sl = effective loop body size.
  sb = basic block size.
  f = average execution frequency of block.
  Ml = number of misses per loop instance.
  l = average number of loop iterations.
  S = cache size.
Estimated new cache miss rate for inlining; used greedy algorithm to select functions to inline.

## Slide 21: Pettis and Hansen
Profiled programs using gprof.
Put caller and callee close together in the program, increasing the chance they would be on the same page.
Ordered procedures using call graph, weighted by number of invocations, merging highly-weighted edges.
Optimized if-then-else code to take advantage of the processor’s branch prediction mechanism.
Identified basic blocks that were not executed by given input data; moved to separate processes to improve cache behavior.

## Slide 22: Tomiyama and Yasuura
Formulated trace placement as an integer linear programming.
Basic method increased code size.
Improved method combined traces to create merged traces that fit evenly into cache lines.

## Slide 23: FlexWare programming environment
[Pau02] © 2002 IEEE

## Slide 24: Memory-oriented optimizations
Memory is a key bottleneck in many embedded systems.
Memory usage can be optimized at any level of the memory hierarchy.
Can target data or instructions.
Global flow analysis can be particularly useful.

## Slide 25: Loop transformations
Data dependencies may be within or between loop iterations.
A loop nest has loops enclosed by other loops.
A perfect loop nest has no conditional statements.

## Slide 26: Types of loop transformations
Loop permutation changes order of loops.
Index rewriting changes the form of the loop indexes.
Loop unrolling copies the loop body.
Loop splitting creates separate loops for operations in the loop body.
Loop merging combines loop bodies.
Loop padding adds data elements to change cache characteristics.

## Slide 27: Polytope model
Loop transformations can be modeled as matrix operations:

## Slide 28: Loop permutation and fusion

## Slide 29: Kandemir et al. loop energy experiments
[Kan00] © 2000 ACM Press

## Slide 30: Java transformations
Real-Time Specification for Java (RTSJ) specifies Java for real time:
  Scheduling: requires fixed-priority scheduler with at least 28 priorities.
  Memory management: allows program to operate outside the heap.
  Synchronization: additional mechanisms.

## Slide 31: Reliability
Rehman et al. developed Instruction Vulnerability Index (IVI) to measure the vulnerability of an instruction in a pipeline:
  Processor component c with area Ac.
  Probability of a fault at c Pfault(c).
  Number of bits required for architecturally correct execution ACEc.
  Vulnerable period is operand lifetime, spatial vulnerability determined by area Ar.
Transformations that enhance reliability:
  Optimize data type size to reduce load/store vulnerabilities.
  Loop unrolling balances load/store with longer lifetimes.

## Slide 32: Optimizing compiler flow (Bacon et al.)
Procedure restructuring inlines functions, eliminates tail recursion, etc.
High-level data flow optimization reduces operator strength, moves loop-invariant code, etc.
Partial evaluation simplifies algebra, computes constants, etc.
Loop preparation peels loops, etc.
Loop reordering interchanges, skews, etc.

## Slide 33: Catthoor et al. methodology
Memory-oriented data flow analysis and model extraction.
Global data flow transformations.
Global loop and control flow optimizations.
Data reuse decisions for memory hierarchy.
Memory organization.
In-place optimization.

## Slide 34: Buffer management
Excessive dynamic memory management wastes cycles, energy with no functional improvements.
IMEC: analyze code to understand data transfer requirements, balance concerns across program.
Panda et al.: loop transformations can improve buffer utilization.
Before:
  for (i=0; i<N; ++i)
  for (j=0; j<N-L; ++j)
  b[i][j] = 0;
  for (i=0; i<N; ++i)
  for (j=0; j<N-L; ++j)
  for (k=0; k<L; ++k)
  b[i][j] = a[i][j+k];
After:
  for (i=0; i<N; ++i)
  for (j=0; j<N-L; ++j)
  b[i][j] = 0;
  for (k=0; k<L; ++k)
  b[i][j] = a[i][j+k];
closer

## Slide 35: Cache optimizations
Strategies:
  Move data to reduce the number of conflicts.
  Move data to take advantage of prefetching.
Need:
  Load map.
  Information on access frequencies.

## Slide 36: Cache data placement
Panda et al.: place data to reduce cache conflicts.
Build closeness graph for accesses.
Cluster variables into cache-line sized units.
Build a cluster interference graph.
Use interference graph to optimize placement.
[Pan97] © 1997 ACM Press

## Slide 37: Array placement
Panda et al.: improve conflict test to handle arrays.
Given addresses X, Y. Cache line size k holding M words.
Formulas for X and Y overlapping:

## Slide 38: Array assignment algorithm
[Pan97] © 1997 IEEE

## Slide 39: Data and loop transformations
Kandemir et al.: combine data and loop transformations to optimize cache performance.
Transform loop nest to make the innermost index as the only array element in one array dimension (unused in other dimensions).
Align references to the right side to conform to the left side.
Search right-side transformations to choose best one.

## Slide 40: Scratch pad optimizations
Panda et al.: assign scalars statically, analyze cache conflicts to choose between scratch pad, cache.
VAC(u): variable access count.
IAC(u): interference access count.
IF(u): total interference count VAC(u) + IAC(u).
LCF(u): loop conflict factor.
TCF(u): total conflict factor.

## Slide 41: Scratch pad allocation formulation
AD( c ): access density.

## Slide 42: Scratch pad allocaiton algorithm
[Pan00] © 2000 ACM Press

## Slide 43: Scratch pad allocation performance
[Pan00] © 2000 ACM Press

## Slide 44: Main memory-oriented optimizations
Memory chips provide several useful modes:
  Burst mode accesses sequential locations.
  Paged modes allow only part of the address to be transmitted.
  Banked memories allow parallel accesses.
Access times depend on address(es) being accessed.
banked memory