## Slide 1: Chapter 3, part 2: Programs
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Program performance analysis.
Models of computation and programming.

## Slide 3: Varieties of performance metrics
Worst-case execution time (WCET):
  Factor in meeting deadlines.
Average-case execution time:
  Load balancing, etc.
Best-case execution time (BCET):
  Factor in meeting deadlines.

## Slide 4: Performance analysis techniques
Simulation.
  Not exhaustive.
  Cycle-accurate CPU models are often available.
WCET analysis.
  Formal method; may make use of some simulation techniques.
  Bounds execution time but hides some detail.

## Slide 5: WCET analysis approach
Path analysis determines worst-case execution path.
Path timing determines the execution time of a path.
The two problems interact somewhat.

## Slide 6: Performance models
Simple model---table of instructions and execution times.
  Ignores instruction interactions, data-dependent effects.
Timing accident: a reason why an instruction takes longer than normal to execute.
Timing penalty: amount of execution time increase from a timing accident.

## Slide 7: Path analysis
Too many paths to enumerate.
Use integer linear programming (ILP) to implicitly solve for paths.
Li and Malik:
  Structural constraints describe program structure.
  Finiteness and start constraints bound loop iterations.
  Tightening constraints come from path infeasibility or from user.

## Slide 8: Structural constraints

## Slide 9: Flow constraints
Flow is conserved over the program.
i + b = o + t

## Slide 10: User constraints and objectives
User may bound loop iterations, etc.
Objective function minimizes total flow through the network.

## Slide 11: Li/Malik ILP results
[Li97c]
© 1997 IEEE Computer Society

## Slide 12: Cache behavior and timing
Cache affects instruction fetch time.
  Time depends on state of the cache.
Li and Malik break the program into units of cache lines.
  Each basic block constitutes one or more l-blocks that correspond to cache lines.
  Each l-block has hit, miss execution times.
  Cache conflict graph models states of the cache lines.

## Slide 13: Cache conflict graph
[Li95] © 1995 IEEE

## Slide 14: Path timing
Includes processor modeling:
  Pipeline state.
  Cache state.
Also includes loop iteration bounding.
  Loops with conditionals, data-dependent bounds create problems.

## Slide 15: Healy et al. loop iteration bounding
Use an iterative algorithm to identify branches that affect loop termination.
Identifies the loop iteration on which those branches change direction.
Determine whether these branches are reached.
Calculate iteration bounds.

## Slide 16: Loop iteration example (Healy et al)
for (i=0, j=1;
i<100;
i++, j+=3) {
if (j>75 and somecond || j>300)
break;
}
i=0, j=1 jump
j>75, jump if false
somecond, jump if false
return
j>300, jump if true
i++, j+=3
j<100, jump if false
jump
iteration 26
iteration 101
iteration 101
Lower bound: 26
Upper bound: 101
Redundant code

## Slide 17: Ermedahl et al. clustering analysis
Find clusters to determine what parts of a program must be handled together.
Annotate program with flow facts:
  Defining scope.
  Context identifier.
  Constraint expressions on execution count, etc.

## Slide 18: Eremdahl et al. example
[Erm05] © 2005 IEEE

## Slide 19: Healy et al. cache behavior analysis
Worst-case instruction categories:
  Always miss.
  Always hit.
  First miss---not in cache on first iteration but guaranteed to be in cache on subsequent iterations.
  First hit---always in cache on first iteration but not guaranteed thereafter.
Best-case instruction categories:
  Always miss.
  Always hit.
  First miss---not in cache on first iteration but may be later.
  First hit---may be in cache on first iteration but guaranteed not to be in subsequent iterations.
Table describes worst-case, best-case times for instructions at each pipeline stage.

## Slide 20: Healy et al. analysis algorithm
[Hea99b]
© 1999
IEEE

## Slide 21: Thieling et al. abstract interpretation
Executes a program using symbolic values.
  Allows behavior to be generalized.
  Concrete state is full state; abstract state is one-to-many onto the concrete state.
Cache behavior may be analyzed using abstract state.
  Must analysis looks at upper bounds of memory block ages.
  May analysis looks at lower bounds.
  Persistence analysis looks at behavior after first access.

## Slide 22: Wilhelm modular approach
Abstract interpretation analyzes processor behavior.
ILP analyzes program path behavior.
Abstract interpretation helps exclude impossible timing analysis.

## Slide 23: Simulation and WCET
Some detailed effects require simulation.
  Consider only parts of program, machine.
Engblom and Ermedahl simulated pipeline effects using cycle-accurate simulator.
Healy et al. used tables of structural and data hazards to analyze pipeline interactions.
Engblom and Jonsson developed a single-issue in-order pipeline model.
  Analyzed constraints to determine which types of pipelines have long timing effects.
  Crossing critical path property means that pipeline does not have long timing effects.

## Slide 24: Timing bounds and security
Zimmer et al. propose WCET bounds to identify compromised real-time software:
  T-Rex checks execution time of short paths, watchdog flags codes that does not meet bound.
  T-ProT sets timing checkpoints dynamically using previous time between checkpoints as bound for next checkpoint.
  T-AxT probes PC value during scheduler preemption and checks against allowable address range.

## Slide 25: Programming languages
Embedded computing uses many models of computation:
  Signal processing.
  Control/protocols.
  Algorithmic.
Different languages have specialized uses, require different compilation methods.
Models of computations must interact properly.

## Slide 26: Reactive systems and synchronous languages
Reactive systems react to inputs, generate outputs.
Synchronous languages were designed to model reactive systems.
  Allows a program to be written as several interacting modules.
Synchronous languages are deterministic.
  Very different from Hoare-style asynchronous communication.

## Slide 27: Benveniste and Berry rules of synchronous languages
A change in the state of one module is simultaneous with receipt of inputs.
Outputs from a module are simultaneous with changes in state.
Communication between modules is synchronous and instantaneous.
Output behavior of the modules is determined by the interleaving of input signals.

## Slide 28: Interrupt-oriented languages
Interrupts are important sources of asynchronous behavior and timing constraints.
Interrupt handlers are difficult to debug.
  Layered approach is slow.
Languages compile efficient implementations of drivers.

## Slide 29: Video driver language
Thibault et al. developed a language for X Windows video device drivers.
Abstract machine defines operations, data transfers, control operations.
Language can be used to describe details of the video adapter, program the interface.

## Slide 30: Conway and Edwards NDL
State of I/O device is declared as part of the NDL program.
  Memory-mapped I/O locations are defined using ioport construct.
NDL program declares device’s states, which includes actions to occur when in those states.
Interrupt handler is controlled by Boolean condition.

## Slide 31: Data flow languages
Many types of data flow.
Synchronous dataflow (SDF) introduced in Chapter 1.
A computational unit may be called a block or an actor.

## Slide 32: Synchronous data flow scheduling
Determine schedule for data flow network (PAPS):
  Periodic.
  Admissible---blocks run only when data is available, finite buffers.
  Parallel.
Sequential schedule is PAPS.

## Slide 33: Describing the SDF network (Lee/Messerschmitt)
Topology matrix G.
  Rows are edges.
  Columns are nodes.
1 | -1 | 0
0 | 1 | -1
2 | 0 | -1
a
b
c
1
1
2
1
1
1
a
b
c
a
b
c
a
c
b

## Slide 34: Feasibility tests
Necessary condition for PASS schedule:
  rank(G) = s-1 (s = number of blocks in graph).
Rank of example is 3: no feasible schedule.
1 | -1 | 0
0 | 1 | -1
2 | 0 | -1
a
b
c
a
c
b
a
b
c
1
1
2
1
1
1
a
b
c

## Slide 35: Fixing the problem
New graph has rank 2.
a
b
c
1
1
2
1
1
2
a
b
c
1 | -1 | 0
0 | 2 | -1
2 | 0 | -1
a
b
c
a
c
b

## Slide 36: Serial system schedule
time
a
b
c

## Slide 37: Allocating data flow graphs
If we assume that function units operate at roughly the same rate as SDF graph, then allocation is 1:1.
Higher data rates might allow multiplexing one function unit over several operators.
a
b
c
1
1
2
1
1
2
a
b
c

## Slide 38: Fully sequential implementation
Data path + sequencer perform operations in total ordering:
registers
a
b
c
c

## Slide 39: SDF scheduling
Write schedules as strings: a(2bc)bc = abcbc.
Lee and Messerschmitt: periodic admissible sequential schedule (PASS) is one type of schedule that can be guaranteed to be implementable.
  Buffers are bounded.
Necessary condition for PASS is that, given s blocks in graph, rank of topology matrix must be s-1.

## Slide 40: Bhattacharyya et al. SDF scheduling algorithms
One subgraph is subindependent of another if no samples from the second subgraph are consumed by the first one in the same schedule period in which they are produced.
Loosely interdependent graph can be partitioned into two subgraphs, one subindependent of other.
Single-appearance schedule has each SDF node only once.

## Slide 41: Clustering and single-appearance schedules
[Bha94a]

## Slide 42: Common code space set graph

## Slide 43: Bhattacharyya and Lee buffer analysis and synthesis
Static buffer: ith sample always appears in the same location in the buffer.
  Static buffering scheme simplifies addressing.
Pointer into buffer must be spilled iff a cycle in the common code space set graph accesses an arc non-statically.
  Analyze using first-reaches table.
May be able to overlay values in buffers for long schedules.

## Slide 44: Overlay analysis
[Bha94b] © 1994 IEEE

## Slide 45: LUSTRE
Synchronous dataflow language.
Variables represent flows, or sequences of values.
  Value of a flu is the nth member of the sequence.
Temporal operators:
  pre(E) gives previous value of flow E.
  E -> F gives new flow with first value from E and rest from F.
  E when B gives a flow with a slower clock as controlled by B.
  current operator produces a stream with a faster clock.

## Slide 46: SIGNAL
Synchronous language written as equations and block diagrams.
Signal is a sequence of data with an implicit time sequence.
  y $ I delays y by I time units.
Y when C produces Y when both Y and C are present and C is true, nothing otherwise.
Y default X merges Y and X.
Systems can be described as block diagrams.

## Slide 47: Caspi et al. distributed implementations of programs
Algorithm for compiling synchronous languages into distributed implementations.
Replication and localization.
Insertion of puts.
Insertion of gets.
Synchronization of threads.
Elimination of redundant operators.
May insert puts/gets either bottom-up or top-down.

## Slide 48: Compaan
Synthesizes process network models from Matlab.
Uses polyhedral reduced dependence graph (PRDG) to analyze program.
Nodes in PRDG are mapped into process network for implementation.

## Slide 49: Control-oriented programming languages
Control can be partitioned to provide modularity.
Event-driven state machine model is a common basic for control-oriented languages.

## Slide 50: Statecharts
OR state
AND state

## Slide 51: Compiling and verifying Statecharts
Wasowski: use hierarchy trees to keep track of Statechart state during execution of program.
  Levels of tree alternate between AND and OR.
Alur and Yannakakis developed verification algorithms.
  Invariants can be checked more efficiently because component FSMs need to be checked only once.

## Slide 52: Esterel example
[Bou91] © 1991 IEEE

## Slide 53: Edwards multi-threaded Esterel compilation
[Edw00] © 2000 ACM Press

## Slide 54: Java memory management
Traditional garbage collectors are not designed for real time, low power.
  Application program that uses the garbage collector is called mutator.

## Slide 55: Bacon et al. garbage collector
Memory for objects are segregated into free lists by size.
Objects are usually not copied.
When a page becomes fragmented, its objects are copied to another page.
A forwarding pointer helps relocation.
Garbage is collected using incremental mark-sweep.
Large arrays are broken into fixed-sized pieces.
Maximum mutator utilization approaches
  ut = QT/[QT + CT]

## Slide 56: Hterogeneous models of computation
Lee and Parks proposed coordination languages based on Kahn process networks.
Input to a process is guarded by infinite-capacity FIFO that carries a stream of values.
Monotonicity is related to causality.
Lee/Parks showed that a network of monotonic processes is itself monotonic.

## Slide 57: Dataflow actors and multiple models of computation
Can coordinate between languages using a strict condition: actor’s outputs are functions of present input functions and not prior state, no side effects.
Ptolemy II three-phase execution:
  Setup phase.
  Iteration = prefiring, firing, postfiring.
  Wrapup phase.

## Slide 58: Metropolis
Categories of description:
  Computation vs. communication.
  Functional specification vs. implementation platform.
  Function/behavior vs. nonfunctional requirements.
Constraints on communication in linear-time temporal logic:
  Rates.
  Latencies.
  Jitter.
  Throughput.
  Burstiness.

## Slide 59: Model-integrated computing
Generate software from domain-specific modeling languages:
  Model environment.
  Model application.
  Model hardware platform.
[Kar03] © 2003 IEEE