## Slide 1: Chapter 4, part 1: Processes and Operating Systems
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Real-time scheduling.
Scheduling for power/energy.
Languages and scheduling.

## Slide 3: Real-time scheduling terminology
Process: unique execution of a program
Context switch: operating system switch from one process to another.
Time quantum: time between OS interrupts.
Schedule: sequence of process executions or context switches.
Thread: process that shares address space with other threads.
Task: a collection of processes.
Subtask: one process in a task.

## Slide 4: Real-time scheduling algorithms
Static scheduling algorithms determine the schedule off-line.
  Constructive algorithms don’t have a complete schedule until the end of the algorithm.
  Iterative improvement algorithms build a schedule, then modify it.
Dynamic scheduling algorithms build the schedule during system operation.
  Priority schedulers assign priorities to processes.
  Priorities may be static or dynamic.

## Slide 5: Timing requirements
Real-time systems have timing requirements.
  Hard: missing a deadline causes system failure.
  Soft: missing a deadline does not cause failure.
Deadline: time at which computation must finish.
Release time: first time that computation may start.
Period (T): interval between deadlines.
Relative deadline: release time to deadline.

## Slide 6: Timing behavior
Initiation time: time when process actually starts executing.
Completion time: time when process finishes.
Response time = completion time – release time.
Execution time (C): amount of time required to run the process on the CPU.

## Slide 7: Task graphs
Edges in task graph describe data dependencies between processes.
An application may contain several task graphs, each with its own period.

## Slide 8: Utilization
Total execution time C required to execute processes 1..n is the sum of the Cis for the processes.
Given available time t, utilization U = C/t.
  Generally expressed as a percentage.
  CPU can’t deliver more than 100% utilization.

## Slide 9: Static scheduling algorithms
Often take advantage of data dependencies.
  Resource dependencies come from the implementation.
As-soon-as-possible (ASAP): schedule each process as soon as data dependencies allow.
As-late-as-possible (ALAP): schedule each process as late as data dependencies and deadlines allow.

## Slide 10: List scheduling
A common form of constructive scheduler.

## Slide 11: Interval scheduling
Chou and Borriello: statically schedule deadline-driven operations.
Processes and timing constraints represented by weighted directed graph.
Constructive algorithm formulated recursively.
  Partial schedule is valid at each step.
[Cho95a] © 1995 ACM Press

## Slide 12: Priority-driven scheduling
Each process has a priority.
Processes may be ready or waiting.
Highest-priority ready process runs in the current quantum.
Priorities may be static or dynamic.

## Slide 13: Rate-monotonic scheduling
Liu and Layland: proved properties of static priority scheduling.
No data dependencies between processes.
Process periods may have arbitrary relationships.
Ideal (zero) context switching time.
Release time of process is start of period.
Process execution time is fixed.

## Slide 14: Critical instant

## Slide 15: Critical instant analysis
Process 1 has shorter period, process 2 has longer period.
If process 2 has higher priority, then:
Schedulability condition:
Utilization is:
Utilization approaches:

## Slide 16: Earliest-deadline-first (EDF) scheduling
Liu and Layland: dynamic priority algorithm.
  Process closest to its deadline has highest priority.
Relative deadline D.
Process set must satisfy:

## Slide 17: Least-laxity-first (LLF) scheduling
Laxity or slack: difference between remaining computation time and time until deadline.
  Process with smallest laxity has highest priority.
Unlike EDF, takes into account computation time in addition to deadline.

## Slide 18: Response time
Joseph and Pandya described response time:
  Period Ti, computation time Ci.
  Set of tasks with priority higher than i = hp(i).

## Slide 19: Priority inversion
RMS and EDF assume no dependencies or outside resources.
When processes use external resources, scheduling must take those into account.
Priority inversion: external resources can make a low-priority process continue to execute as if it had higher priority.

## Slide 20: Priority inversion example

## Slide 21: Priority inheritance protocols
Sha et al.: basic priority inheritance protocol, priority ceiling protocol.
Process in a critical section executes at highest priority of any process that shares that critical section.
  Can deadlock.
Priority ceiling protocol: each semaphore has its own priority ceiling.
  Required priority to obtain semaphore depends on priorities of other locked semaphores.
Schedulability:

## Slide 22: Multi-criticality scheduling
Proposed by Vestal:
  Some tasks are critical to operation.
  Other tasks are less critical.
  Variations in CPU time, job mix can change observed schedule.
  Give higher weight to higher-criticality tasks when adjusting schedule.
Typically tasks are classified as high or low criticality.

## Slide 23: Multi-criticality scheduling algorithms
Vestal: variation of preemptive fisxed priority scheduling:
  If a high-criticality task exceeds its CPU time, period and execution time are reduced by factor of n to be at or below lowre-criticality tasks.
Li and Baruah: load-based algorithm.
  Recursively construct priority order of tasks.
  Identify tasks as low-priority based on available CPU time.
  Provably schedulable under some load conditions.

## Slide 24: PRLS
Combination of off-line and on-line priority.
Off-line, job is assigned lowest priority if
Prioritiy list used at run time to assign priorities to ready jobs.
  Priority list is represented as a set of intervals.

## Slide 25: Criticality-based earliest deadline first
Off-line schedules high-criticality jobs in EDF order, calculates slacks.
At run-time select job depending on state of ready job queue:
  Low priority only, high priority only, both low and high priority available.

## Slide 26: Ductility-based scheduling
Given a set of k criticality levels, ductility matrix D has 1 entry if task r at criticality c can meet its deadlines with a given system workload.
Summary of D:
Use zero-slack scheduling for uniprocessors.

## Slide 27: Scheduling for dynamic voltage scaling
Dynamic voltage scaling (DVS): change processor voltage to save power.
  Power consumption goes down as V2, performance goes down as V.
Must make sure that the process finishes its deadline.

## Slide 28: Yao et al. DVS for real-time
Intensity of an interval defines lower bound on average speed required to create a feasible schedule.
Interval that maximizes the intensity is the critical interval.
Optimal schedule is equal to the intensity of the critical interval.
Average rate heuristic:

## Slide 29: DVS with discrete voltages
Ishihara and Yasuura: two voltage levels are sufficient if a finite set of discrete voltage levels are used.

## Slide 30: Voltage scaling with two voltages
[Ish98a] © 1998 IEEE

## Slide 31: Kim et al. slack-based scheduling
[Kim02] © 2002 IEEE

## Slide 32: Checkpoint-driven scheduling
Azevedo et al. used profile data to guide DVS.
  Designer inserts checkpoints in program to measure performance and energy.
Scheduler considers all possible events from current checkpoint to deadline.
[Aze03] © 2002 IEEE Computer Society

## Slide 33: Procrastination scheduling
Family of algorithms that maximizes lengths of idle periods.
  CPU can be turned off during idle periods, further reducing energy consumption.
Jejurkar et al.: Power consumption P = PAC + PDC + Pon.
Minimum breakeven time tth = Esd/Pidle.
Guarantees deadlines if:

## Slide 34: Performance estimation
Multiple processes interfere in the cache.
  Single-process performance evaluation cannot take into account the effects of a dynamic schedule.
Kirk and Strosnider: segment the cache, allow processes to lock themselves into a segment.
Mueller: use software methods to partition.

## Slide 35: Cache modeling and scheduling
Li and Wolf: each process has a stable footprint in the cache.
Two-state model:
  Process is in the cache.
  Process is not in the cache.
Characterize execution time in each state off-line.
Use CPU time measurements along with cache state to estimate process performance at each quantum.
Kastner and Thiesing: scheduling algorithm takes cache state into account.

## Slide 36: Languages and scheduling
Programming language can capture information about tasks.
Compilation can generate specialized implementations, implement static schedules.

## Slide 37: Codesign finite state machines (CFSMs)
Control model for hardware and software.
Four-state execution:
  Idle.
  Detect input events.
  Go to new state based on current state and inputs.
  Emit outputs.
Chiodo et al. compiled by generating an s-graph.
  Analyze with Shannon decomposition.

## Slide 38: Lin and Zhu static scheduling using Petri nets
Find maximal acyclic fragments of program, schedule operations in each fragment.
Expansion of a Petri net: acyclic Petri net in which every transition has one input or output or output place, no input transitions, and at least one place with no output transitions.
Maximal expansion is transitively closed.
Code is generated form maximally expanded fragment by pre-ordering operations.

## Slide 39: Maximal expansions
[Lin98] © 1998 IEEE Computer Society

## Slide 40: Software thread integration
Dean: schedule multiple threads statically in a single program.
Primary thread has real-time requirements.
Secondary thread does not have real-time requirements.

## Slide 41: Software thread integration and CDGs
Thread is represented as control dependence graph (CDG).
  Annotated with execution times of each blocks.
Code from primary thread must be replicated in secondary thread to be sure that it is executed along every path.
  Insertion points must meet primary thread deadlines.

## Slide 42: Giotto
Language for describing concurrent systems.
Execution is organized into modes: repeated invocation of a sequence of tasks in a fixed order.
  Single invocation is a round.

## Slide 43: Giotto execution cycle
Task output and internal ports are updated.
Actuator ports are updated.
Sensor ports are updated.
Modes are updated, possibly selecting some target modes.
Mode ports are updated.
Mode time is updated.
Task input ports are updated.
Set of active tasks is updated.
Time clock is updated.

## Slide 44: SHIM
Programming model connects sequential processes through fixed communication channels.
Processes communicate with rendezvous (no buffers).
Model is deterministic.
SHIM specifications can be implemented in single thread using Lin/Zhu algorithm.