## Slide 1: Chapter 5, part 1: Multiprocessor Architectures
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Motivation.
Architectures for embedded multiprocessing.
Interconnection networks.

## Slide 3: Generic multiprocessor
Shared memory:
Message passing:
PE
mem
PE
mem
PE
mem
…
…
Interconnect network
PE
mem
PE
mem
PE
mem
…
Interconnect network

## Slide 4: Design choices
Processing elements:
  Number.
  Type.
  Homogeneous or heterogeneous.
Memory:
  Size.
  Private memories.
Interconnection networks:
  Topology.
  Protocol.

## Slide 5: Why embedded multiprocessors?
Real-time performance---segregate tasks to improve predictability and performance.
Low power/energy---segregate tasks to allow idling, segregate memory traffic.
Cost---several small processors are more efficient than one large processor.

## Slide 6: Example: cell phones
Variety of tasks:
  Error detection and correction.
  Voice compression/decompression.
  Protocol processing.
  Position sensing.
  Music.
  Cameras.
  Web browsing.

## Slide 7: Example: video compression
QCIF (177 x 144) used in cell phones and portable devices:
  11 x 9 macroblocks of 16 x 16.
  Frame rate of 15 or 30 frames/sec.
  Seven correlations per macroblock = 25,344 comparisons per frame.
  Feig/Winograd DCT algorithm uses 94 multiplications and 454 additions per 8 x 8 2D DCT.

## Slide 8: Austin et al.: portable supercomputer
Next-generation workload on portable device:
  Speech compression.
  Video compression and anaysis.
  High-resolution graphics.
  High-bandwidth wireless communications.
Workload is 10,000 SPECint = 16 x 2GHz Pentium 4.
Battery provides 75 mW.

## Slide 9: Performance trends on desktop
[Aus04] © 2004 IEEE Computer Society

## Slide 10: Energy trends on desktop
[Aus04] © 2004 IEEE Computer Society

## Slide 11: Specialization and multiprocessing
Many embedded multiprocessors are heterogeneous:
  Processing elements.
  Interconnect.
  Memory.
Why use heterogeneous multiprocessors:
  Some operations (8 x 8 DCT) are standardized.
  Some operations are specialized.
  High-throughput operations may require specialized units.
Heterogeneity reduces power consumption.
Heterogeneity improves real-time performance.

## Slide 12: Multiprocessor design methodologies
Analyze workload that represents application’s usage.
Platform-independent optimizations eliminate side effects due to reference software implementation.
Platform design is based on operations, memory, etc.
Software can be further optimized to take advantage of platform.

## Slide 13: Cai and Gajski modeling levels
Implementation: corresponds directly to hardware.
Cycle-accurate computation: captures accurate computation times, approximate communication times.
Time-accurate communication: captures communication times accurately but computation times only approximately.
Bus-transaction: models bus operations but is not cycle-accurate.
PE-assembly: communication is untimed, PE execution is approximately timed.
Specification: functional model.

## Slide 14: Cai and Gajski modeling methods
[Cai03]

## Slide 15: Multiprocessor systems-on-chips
MPSoC is a complete platform for an application.
Generally heterogeneous processing elements.
Combine off-chip bulk memory with on-chip specialized memory.

## Slide 16: Qualcomm Snapdragon 800
High-end smartphone system-on-chip.
  Krait 400 ARM-based CPU.
  Graphics processor.
  DSP.
  Connectivity unit for 4GLTE, WiFi, USB, etc.
  Multimedia unit.
  Camera unit.
  Navigation unit for GPS.

## Slide 17: Philips Viper Nexperia

## Slide 18: Viper Nexperia characteristics
Designed to decode 1920 x 1080 HDTV.
Trimedia runs video processing functions.
MIPS runs operating system.
Synchronous DRAM interface for bulk storage.
Variety of I/O devices.
Accelerators: image composition, scaler, MPEG-2 decoder, video input processors, etc.

## Slide 19: TI OMAP
Designed for mobile multimedia.
C55x DSP performs signal processing as slave.
ARM runs operating system, dispatches tasks to DSP.

## Slide 20: TI OMAP 5912

## Slide 21: Freescale Qorivva MPC5676R
Designed for engine control units:
  Two Power Architecture CPUs.
  Two 36-channel time processing units for high-frequency events (spark plugs, etc.)
  FlexRay controller.
  Crossbar itnerconnect.

## Slide 22: Processing elements
How many do we need?
What types of processing elemetns do we need?
Analyze performance/power requirements of each process in the application.
Choose a processor type for each process.
Determine what processes should share processing elementng

## Slide 23: Interconnection networks
Client: sender or receiver on network.
Port: connection to a network.
Link: half-duplex or full-duplex.
Network metrics:
  Throughput.
  Latency.
  Energy consumption.
  Area (silicon or metal).
Quality-of-service (QoS) is important for multimedia applications.

## Slide 24: Interconnection network models
Source <- line -> termination.
Throughput T, latency D.
Link transmission energy Eb.
Physical length L.
Traffic models:
  Poisson E(x) = m, Var(x) = m.

## Slide 25: Network topologies
Major choices.
  Bus.
  Crossbar.
  Buffered crossbar.
  Mesh.
  Application-specific.

## Slide 26: Bus network
Throughput:
  T = P/(1+C).
Advantages:
  Well-understood.
  Easy to program.
  Many standards.
Disadvantages:
  Contention.
  Significant capacitive load.

## Slide 27: Crossbar
Advantages:
  No contention.
  Simple design.
Disadvantages:
  Not feasible for large numbers of ports.

## Slide 28: Buffered crossbar
Advantages:
  Smaller than crossbar.
  Can achieve high utilization.
Disadvantages:
  Requires scheduling.
Xbar
Input-buffered
Internally buffered

## Slide 29: Mesh
Advantages:
  Well-understood.
  Regular architecture.
Disadvantages:
  Poor utilization.

## Slide 30: Application-specific.
Advantages:
  Higher utilization.
  Lower power.
Disadvantages:
  Must be designed.
  Must carefully allocate data.

## Slide 31: Routing and flow control
Routing determines paths followed by packets.
  Connection-oriented or connectionless.
  Wormhole routing divides packets into flits.
  Virtual cut-through ensures entire path is available before starting transmission.
  Store-and-forward routing stores inside network.
Flow control allocates links and buffers as packets move through the network.
  Virtual channel flow control treats flits in different virtual channels differently.

## Slide 32: Networks-on-chips
Help determine characteristics of MPSoC:
  Energy per operation.
  Performance.
  Cost.
NoCs do not have to interoperate with other networks.
  NoCs have to connect to existing IP, which may influence interoperability.
QoS is an important design goal.

## Slide 33: Nostrum
Mesh network---switch connects to four nearest neighbors and local processor/memory.
Each switch has queue at each input.
Selection logic determines order in which packets are sent to output links.
[Kum02] © 2002 IEEE Computer Society

## Slide 34: SPIN
Scalable network based on fat-tree.
  Bandwidth of links is larger toward root of tree.
All routing nodes use the same routing function.

## Slide 35: Input queues and partial crossbars in SPIN
From Guerrier and Greiner
[Gre00] ©2000 ACM Press. Reprinted by permission.

## Slide 36: Slim-spider
Hierarchical star topology.
Global network is star.
Each subnetwork is a star.
Stars occupy less area than mesh networks.

## Slide 37: Yet et al. energy model
Energy per packet is independent of data or packet address.
Histogram captures distribution of path lengths.
Energy consumption of a class of packet:
  M = maximum number of hops.
  h = number of hops.
  N(h) = value of hth histogram bucket.
  L = number of flits per packet.
  Eflit = energy per flit.

## Slide 38: Goossens et al. NoC methodology

## Slide 39: Coppola et al. OCCN methodology
Three layers:
  NoC communication layer implements lower layers of OSI stack.
  Adaptation layer uses hardware and software to implement OSI middle layers.
  Application layer built on top of communication API.

## Slide 40: QNoC
Designed to support QoS.
Two-dimensional mesh, wormhole routing.
  Fixed x-y routing algorithm.
Four different types of service.
  Each service level has its own buffers.
  Next-buffer-state table records number of sloots for each output in each class.
  Transmissions based on next stage, service levels, and round-robin ordering.
Can be customized to application-specific.

## Slide 41: Xpipes and NetChip
IP-generation tools for NoCs.
xpipes is library of soft IP macros for network switches and links.
NetChip generates custom NoC designs using xpipes components.
Links are pipelined.

## Slide 42: Xu et al. H.264 network design
Designed NoC for H.264 decoder.
Process -> PE mapping was given.
Compared RAW mesh, application-specific networks.
[Xu06] © 2006 ACM Press

## Slide 43: Application-specific network for H.264
[Xu06] © 2006 ACM Press

## Slide 44: RAW/application-specific network comparison
[Xu06] © 2006 ACM Press

## Slide 45: Sopnics SiliconBackplane III
Designed for nonblocking, streaming communication.
Raw data bandwidth of 4.8 GBps at 300 MHz.
Provides bursting, multicast.