## Slide 1: Chapter 5, part 2: Multiprocessor Architectures
High Performance Embedded Computing
Marilyn Wolf

## Slide 2: Topics
Memory systems.
Physically distributed multiprocessors.
Design methodologies.

## Slide 3: Parallel memory systems
n memory banks can be accessed independently.
Peak access rate given by n parallel accesses.
Performance can be estimated statistically.
Bank 0
Bank 1
Bank 2
Bank 3
address
data

## Slide 4: Memory bank usage
for (i=0; i<N; i++)
a[i] = b[i] + c[i];
a[0]
b[0]
c[0]
a[1]
b[1]
c[1]
a[2]
b[2]
c[2]
a[3]
b[3]
c[3]
a[0]
b[0]
c[0]
a[0]
a[1]
a[2]
b[0]
b[1]
b[2]
c[0]
c[1]
c[2]
a[0]
b[0]
c[0]

## Slide 5: Memory system performance
Peak:
  (# banks) * (access time per bank).
Average (with contention):
About 20% of instructions are branches.
Probability of instruction sequence of length m including a branch:
p(1) = 
p(k) = (1 - ) ^(k-1) 
p(m) = (1 - )^(m-1)
Mean branchless sequence length:
bm =  k p(k)
= [1 - (1 - )^m] / 

## Slide 6: Memory system design
Parameters: area, performance, energy.
Delay is a nonlinear function of memory size.
Delay is a nonlinear function of the number of ports.

## Slide 7: Dutta et al. memory system design methodology
[Dut98] © 1998 IEEE

## Slide 8: Heterogeneous memory systems
Heterogeneous memory improves real-time performance:
  Accesses to the same bank interfere, even if not to the same location.
  Segregating real-time locations improves predictability, reduces access time variance.
Heterogeneous memory improves power:
  Smaller blocks with fewer ports consume less energy.

## Slide 9: HP DesignJet printer
[Meb92]

## Slide 10: Cache consistency in multiprocessors
Critical sections guard shared variables using spin locks.
Caches need to be consistent.
  Use snooping caches in scientific processors.

## Slide 11: Consistent parallel memory systems
Agkul and Mooney: SoC lock cache.
  Combined hardware/software implementation.
Moshovos et al.: JETTY monitors level 2 cache state, saves cache references for some locations that are not in the cache.

## Slide 12: ARM MPCore
Embedded multiprocessor with four identical PEs.
Memory system configuration is programmable.
  Asymmetric or symmetric operation.
  Protected memory, etc.

## Slide 13: Networks and physically-distributed embedded systems
Examples: automobiles, airplanes.
Nodes connected by a network.
  Network delay is noticeable.
Reasons for physically distributed nodes:
  Must keep some computation close to mechanics to reduce latency.
  May reduce network bandwidth by processing data locally.
  Modular design may be assembled from components by different vendors.

## Slide 14: CAN bus
Widely used in cars, entered production in 1991.
  Twisted pair or optical physical layer.
Synchronous protocol, CSMA/AMP.
  Device priority determined by address.
  Devices check for conflicts during addressing phase.
Any device can generate an error frame.
Checkoway et al. analyzed security vulnerability of cars with CAN bus.

## Slide 15: Time-Triggered Architecture
TTH has a notion of real time.
  Correct partial order is not sufficient.
TTH timestamp is based on GPS clock.
  64-bit value.
  Fractions of second in three lower bytes, seconds in five upper bytes.
  GPS epoch starts at 0:00:00 UCT Jan 6, 1980.

## Slide 16: Sparse model of time
Allows predictable interaction between physical time and discrete time.
Active periods denoted by e.
Idle periods denoted by d.
Events occur during e, never during d.
Duration of e, d is larger than precision of the clock.

## Slide 17: Communications network itnerface
Helps maintain consistent view of time.
  Between host controller and communications controller.
Enforces unidirectional flow of data.
  One inbound, one outbound channel.

## Slide 18: TTA topologies

## Slide 19: Cliques
In a fault-tolerant system, failures cause internal inconsistencies.
  Different nodes have different views of the system state.
Clique avoidance algorithm identifies faulty nodes.
  Protocols can identify state inconsistency.
  Action on faulty nodes is determined by the application.

## Slide 20: FlexRay
Second-generation automotive network.
Host runs application.
Communication controller provides high-level functions.
Bus drivers provide physical itnerface.
Bus guardians watch system for errors.

## Slide 21: FlexRay real-time performance
Static phase is scheduled statically for real-time behavior.
Dynamic phase provides non-time-critical time slots.
Microtick comes from application internal clock.
Macrotick comes from clusterwide synchronized clock.

## Slide 22: FlexRay timing
Action points are boundaries between macroticks.
Arbitration grid determines boundaries between messages.
Communication cycle:
  Static segment.
  Dynamic segment.
  Symbol window.
  Network idle time.

## Slide 23: FlexRay network stack
Physical defines structure of connections.
Interface defines physical connections.
Protocol engine defines frame formats and communication nodes.
Controller host interface provides status, etc.
Host layer provides applications.

## Slide 24: FlexRay active star topology
basic
redundant

## Slide 25: FlexRay frame format

## Slide 26: FlexRay static segment

## Slide 27: FlexRay dynamic segment

## Slide 28: FlexRay dynamic segment timing
Slots are arbitrated using a deterministic algorithm.
Messages sent at minislot boundaries.
Message lasts longer than a minislot if sent.

## Slide 29: FlexRay timekeeping
Global time is synthesized by clock synchronized process (CSP.
Macroticks are managed by macrotick generation process.

## Slide 30: Aircraft networks
Avionics categories:
  Instrumentation.
  Navigation/communication.
  Control.
Control networks must perform hard real-time, safety-critical tasks.
Management networks control noncritical devices.
Passenger networks manage entertainment, internet access, etc.

## Slide 31: ARINC 644 standard
Aircraft network is divided into four domains with firewalls between them:
Flight deck network is deterministic.
Separate network for OEM equipment with temporal determinism.
Airline systems network supports entertainment, etc.
Passenger subnetwork provides Internet access.

## Slide 32: Multiprocessor design methodologies
MPSoC built from many hardware and software modules.
  Many modules are existing IP.
  Some IP may be unmodifiable, other IP may be modified.
  Some modules are created for the project.

## Slide 33: Characteristics of modern SoC designs
Too big to be designed at register-transfer level.
  CPUs running software.
  Memory.
  Devices.
Too big to design all the IP blocks yourself.
Too big to be verified solely by cycle-level simulation.

## Slide 34: IBM CoreConnect
[Ber01] © 2001 IEEE Computer Society

## Slide 35: Coral design methodology
Virtual components describe a class of real components.
Coral synthesizes glue logic between components.
Interconnection engine generates netlist, checks designs.
[Ber01] © 2001 IEEE Computer Society

## Slide 36: Coral virtual-to-real synthesis
[Ber01]
© 2001
IEEE Computer Society

## Slide 37: Component-based design
Cesario/Jerraya: build MPSoCs from components to allow design reuse.
Components + wrappers can be connected to channels.
P1
wrapper
channel

## Slide 38: Challenges in heterogeneous multiprocessors
Multiple bus/network masters makes it harder to synchronize communications.
Multiple busses/networks rather than single bus.
Need specialized hardware for interprocess communication to offload the CPU.
Need high-level communication operations that can be off-loaded from CPU. Shared memory I/O is too low-level.

## Slide 39: Challenges for EDA industry
Must verify protocols, etc. without resorting to cycle-level simulation for everything.
Chips will include several types of processors, making software development harder.
Must adapt CPU, hardware IP blocks to the underlying communication fabric.

## Slide 40: Application vs. task-specific software stacks
Host CPU and task-specific CPUs tend to run different stacks:
Hardware
Host CPU
Drivers
Host OS
Programming API
Application
Hardware
Task-specific CPU
Drivers
Custom OS
Task-specific API
Specialized tasks

## Slide 41: Software adaptations for a dedicated CPU
Adapt to hardware platform’s communication primitives.
Provide optimized versions of host OS communication functions.
Provide synchronization functions.

## Slide 42: Abstract architecture template
Application libraries provide application-specific functions.
OS and communication system provide scheduling and resource management.
Hardware abstraction layer provides clock, interrupts, etc.
CPU wrapper translates signals between CPU and network.

## Slide 43: Hardware and software abstraction layers
[Ces04]
© 2004
Morgan Kaufman

## Slide 44: System-level design flow (Jerraya et al.)
requirements
SW model
HW model
Abstract platform
Performance/power
Analysis
HW/SW partitioning
Golden abstract
architecture