## Slide 1: Chapter 6, part 1: Multiprocessor Software
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Performance analysis of multiprocessor software.
  Models.
  Analysis.
  Simulation.

## Slide 3: What is different about embedded multiprocessor software?
How does it differ from general-purpose multiprocessor software?
How does it differ from a uniprocessor?

## Slide 4: Heterogeneity
Hardware platforms are heterogeneous:
  Practical problems.
  Must ensure that models of computations work together.
  Resource allocation problem is restricted.

## Slide 5: Delay variations
Delay variations are harder to predict in multiprocessors:
  Subtle timing bugs are more likely to be exposed.
  Makes it harder to use system resources.
  Long memory access times complicate algorithm design and programming.
Scheduling a multiprocessor is hard---information about the state of the processors costs time, energy.

## Slide 6: Role of the multiprocessor operating system
Simple multiprocessor OS has one master, one or more slaves.
  Simple to implement.
  Heterogeneous processors limit resource allocation options.
More general architecture uses communicating PE kernels.
  PE kernels pass information required for scheduling.
  Information about other PEs may be incomplete or late.

## Slide 7: Vercauteren et al. kernel architecture
Kernel includes scheduling and communication layers.
Basic communication operations implemented by interrupt service routines.
Kernel channel used only for kernel-to-kernel communication.
Service
task
Application
task
ISR
Scheduling layer
CPU
ISR

## Slide 8: OMAP C5510 performance/power for AAC decoding (from TI)
Rate | Mcycles/ sec | mA @ 1.5V | mA @ 1.2V
64K | 22.1 | 8.0 | 6.4
48K | 16.2 | 5.8 | 4.7
32K | 11.4 | 4.1 | 3.3

## Slide 9: Stone multiprocessor scheduling
Schedule tasks on two CPUs.
  Actually allocates tasks to the CPUs to satisfy scheduling constraint.
General scheduling problem is NP-complete, but this problem can be solved in polynomial time.
  Exact solution for two processors.
  Heuristics for more processors.
Solve using network flow algorithms.

## Slide 10: Stone multiprocessor modeling
Table provides execution time of processes on the two CPUs.
Intermodule connection graph describes the time cost of communication between two processes when they run on different CPUs.
  Communication time within a CPU is zero.
Modify intermodule communication graph:
  Add source node for CPU 1 and sink node for CPU 2.
  Add edges from each non-sink node to source and sink. Weight of edge to source is cost of executing on CPU 2 (sink). Weight of edge to sink is cost of executing on CPU 1 (source).
Minimize total time by finding a minimum-cost cutset of the modified intermodule connection graph.

## Slide 11: Stone multiprocessor example
[Sto77]

## Slide 12: Static vs. dynamic task allocation
Dynamic task allocation can choose the CPU for a task at run time.
Static task allocation determines allocation to CPU at design time.
Static task allocation reduces OS overhead, allows more analysis.
Dynamic task allocation helps manage dynamic loads.

## Slide 13: Bhattacharyya et al. SDF scheduling
Interprocessor communication modeling (IPC) graph has same nodes as SDF, all SDF edges, plus additional edges.
  Added edges model sequential schedule.
Edges that cross processor boundaries are called IPC edges.

## Slide 14: Scheduling and graph analysis
Edges not in a strongly connected component are not bounded.
Simpler protocols can be used on bounded edges.
An edge is redundant if another path between the source/sink pair has a longer delay.
Cycle mean T:

## Slide 15: Critical cycles
Maximum cycle mean is the largest cycle mean for any strongly connected component.
Critical cycle has the maximum cycle mean.
Construct strongly connected synchronization graph by adding edges between strongly connected components.
Add delays to the added edges to ensure deadlock.
  Delays are implemented with buffer memory.

## Slide 16: Rate analysis (Gupta et al.)
Goal: identify rates at which processes can run.
Model includes multiple processes with control dependencies.
  CDFG-style model within each process.

## Slide 17: Process model
Edges are labeled with (min,max) delays from activation signal to start of execution.
Process starts executing after all its enables signals have been ready.
P1
P2
[3,4]
[1,5]
[min,max]

## Slide 18: Rate analysis
Delay around a cycle in the graph is S di.
Maximum mean cycle delay is l.
In a strongly connected graph all nodes execute at the same rate l.
Given a producer and consumer, bounds on rates of consumer is:
  [ min{rl(P),rl(C)}, min{ru(P),ru(C)} ]

## Slide 19: Lehoczky et al. CPU utilization
Lehoczky et al gave algorithm for computing utilization.
P1 is highest priority process with period p1. wi is the worst-case response time for Pi measured from initiation. Given by smallest non-negative root of
x = g(x) = ci + S1<=i<=mcj * ceil(x/pj)
g(x) is the time required for Pi and processes of higher priority.
Can be efficiently solved using numerical techniques.

## Slide 20: Distributed system performance
Longest-path algorithms don’t work under preemption.
Several algorithms unroll the schedule to the length of the least common multiple of the periods:
  produces a very long schedule;
  doesn’t work for non-fixed periods.
Schedules based on upper bounds may give inaccurate results.
Simulation does not provide guarantees.

## Slide 21: Data dependencies help
P3 cannot preempt both P1 and P2.
P1 cannot preempt P2.
P1
P2
P3

## Slide 22: Preemptive execution hurts
Worst combination of events for P5’s response time:
  P2 of higher priority
  P2 initiated before P4
  causes P5 to wait for P2 and P3.
Independent tasks can interfere—can’t use longest path algorithms.
P1
M1
P5
P2
M2
P4
P3
M3

## Slide 23: Period shifting example
P2 delayed on CPU 1; data dependency delays P3; priority delays P4. Worst-case t3 delay is 80, not 50.
task period
t1 150
t2 70
t3 110
process CPU time
P1 30
P2 10
P3 30
P4 20
CPU 1
P1
P2
CPU 2
P3
P4
P2
P3
P4
P1
P2
P4
P3
t1
t2
t3

## Slide 24: Network of RMA processors
Run rate-monotonic scheduling on each node.
Yen/Wolf algorithm can tightly bound performance (including min/max).
P1
P2
P3

## Slide 25: Performance analysis strategy (Yen/Wolf)
Timing problem with max constraints.
Need to know bounds on request, finish times for each process:
  earliest[Pi.request,finish]
  latest[Pi.request,finish]
Top-level procedure, DelayEst(G), uses these procedures to iteratively tighten bounds. Alternate between:
  critical path analysis
  max separations

## Slide 26: DelayEst
DelayEst(G) {
initialize maxsep[] to infinity;
step = 0;
do {
    foreach Pi { EarliestTimes(Gi); LatestTimes(Gi); }
    foreach Pi { MaxSeparations(Gi); }
    step++;
} while (maxsep[] changed and step < limit);
}

## Slide 27: DelayEst summary
Gi is subgraph rooted at Pi.
Use maximum separations to improve delay estimates in LatestTimes(); call MaxSeparations() to derive maximum separations.
Step limit can be used to limit CPU time used for estimates.

## Slide 28: Ernst et al. SymTA/S
Event-driven analysis model.
Compute bounds on start, stop of computation.
Use constraints to tighten result:
  Dependencies between streams.
  Dependencies within a stream.

## Slide 29: Event models
Simple event model P is strictly periodic.
Jitter event model adds variation (jitter).
  Parameterized by (P,J).
Event functional model allows us to vary the number of events in an interval.
Periodic with jitter event model:
time
P
J

## Slide 30: Events and jitter
Input events produce output events.
Computation may introduce jitter between input and output.
Add response time jitter to input jitter to get output event jitter:

## Slide 31: Cyclic scheduling dependencies
[Hen05] © 2005 IEEE

## Slide 32: AND activation
AND inputs are buffered.
  All inputs have same arrival rate.
Fires when all its inputs are available.
AND output jitter is equal to maximum jitter of any input.

## Slide 33: OR activation
Does not require buffers.
Jitter computation is more complex.
  Must be approximated.
[Hen05] © 2005 IEEE

## Slide 34: OR jitter derivation
Must satisfy:
Evaluate piecewise:
Approximate as:

## Slide 35: Kang et al. distributed signal processing synthesis

## Slide 36: Event-driven simulation
Event: change in visible state.
Event-driven simulation evaluates only signals that may change.
  Component receives event.
  Component may emit an event.
Sensitivity list describes what signals can affect a component.
A
1
1
0
1
0
0
0
1

## Slide 37: SystemC
C++-based system modeling language.
C++ library provides simulation functions.
C++ operator overloading, etc., provide syntax.

## Slide 38: Component model
Ports connect to other components.
Processes describe the functionality of the model.
Internal data, channels.
Sensitivity list describes what channels can activate this component.
Component may be built hierarchically.

## Slide 39: Simulation model
Two-phase execution semantics:
  Evaluate.
  Update.
Request-update access to channels supports two-phase semantics.
Sensitivity list determines chains of activation:
  Static sensitivity list.
  Dynamic sensitivity list.

## Slide 40: SystemC modeling styles
Register-transfer.
  Cycle-accurate.
Behavioral.
  Not cycle-accurate.
Transaction-level.
  More abstract than behavioral.

## Slide 41: Hardware/software co-simulation
Multi-rate simulation:
  Hardware is modeled with cycle-level accuracy.
  Software is modeled as instructions or source code.
Simulation engine manages communication between models.
Simulation manager
SW
model
HW
model
HW
model

## Slide 42: Compiled co-simulation
Zivojnovic/Meyr: combine compiled SW simulation with HW simulation.
Software is compiled into host instructions.
  Directly executed on the host.
Translator provides hooks to communicate with HW simulators.