## Slide 1: Chapter 6, part 2: Multiprocessor Software
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Multiprocessor scheduling.
Middleware and software services.
Design verification.

## Slide 3: Scheduling with dynamic tasks
Can’t guarantee that all tasks can be handled.
  Can’t guarantee start time for a process.
In a real time system, once we start a process, we want to guarantee its completion time.
Admission control determines what processes can execute based on resources, load.

## Slide 4: Ramarithram et al. myopic scheduling
Assumptions:
  Tasks are nonperiodic.
  Tasks are executed non-preemptively.
  No data dependencies between tasks.
Task characterized by arrival time, deadline, worst-case processing time, resource requirements.

## Slide 5: Myopic scheduling algorithm
Constructs partial schedules.
  Search includes backtracking.
Add a task to a partial schedule.
  Partial schedule is strongly feasible if the schedule itself is feasible and every possible next choice for a task also gives a feasible schedule.
Searches only first k tasks sorted by deadlines.

## Slide 6: Load balancing
Move tasks to new processing element during execution.
Task migration moves an executing task:
  Harder on heterogeneous multiprocessor.
  Harder still if memory is not shared.

## Slide 7: Load balancing scheduling
Shin and Chang: schedule using buddy list for each processing element.
  List of other processing elements with which it can share tasks.
  Subdivided into preferred list, ordered by communication distance to the buddy.
When moving a job, search the buddy list in order, checking load until a satisfactory node is found.

## Slide 8: Middleware and software services
Operating systems provide services for shared resources in uniprocessors.
Must generalize this notion for multiprocessors.
  Need distributed information about resource state.
Middleware provides services in distributed systems.
  Generic services such as data transport.
  Application-specific services such as signal processing.

## Slide 9: Uses of middleware
Services allow applications to be developed more quickly.
Simplifies porting application to a new platform.
Ensures that key functions are correct and efficient.

## Slide 10: Middleware vs. libraries
Traditional software libraries may provide functions but don’t manage resources.
  Need to know global state, have privileges to manage resources.
Resources must be managed dynamically when requests come in dynamically.
Statically designing the system for worst-case costs too much.

## Slide 11: Embedded vs. general-purpose middleware
Embedded middleware must be very efficient:
  Small software footprint.
  Low latency.
  Predictable performance.
Embedded middleware may reside entirely within a chip or may communicate with other systems-on-chips.

## Slide 12: CORBA
Common Object Request Broker Architecture is widely used in business-oriented software.
Metamodel using an object-oriented paradigm.
Can be implemented in any programming language.
Objects and variables are typed.

## Slide 13: CORBA requests
Requests handled by object request broker (ORB).
Client and object may be on different machines.
  ORBs may communicate.
A given service appears as an object but may be implemented with a thread pool.
Object request broker
Client
Object
Object
Stub
Stub
Thread pool
request

## Slide 14: RT-CORBA
Schmidt et al.: Real-time part of CORBA specification.
Designed for fixed-priority systems.
Thread pool may be divided into lanes to help manage responsiveness.

## Slide 15: Dynamic Real-Time CORBA
Real-time daemon implements dynamic real-time services.
Clients specify timing constraints using timed distributed method invocation.
  Can describe deadline, importance.
Server objects can examine TDMI characteristics.
Latency service determines times required to communicate with an object.
Priority service records object priorities.
Real-time event service exchanged named events. Deadlines may be relative to global clock or to an event.

## Slide 16: ARMADA
Middleware system for fault tolerance and QoS.
  Real-time communication.
  Group communication and fault tolerance.
  Dependability tools.
Communication guarantees are divided into clips, which are guaranteed delivery by a deadline.
Real-time connection ordination protocol manages requests for connections.
Real-time primary-backup service replicates states.

## Slide 17: MPI
Widely used in scientific clusters.
Decouples architectural parameters (# PEs) from algorithmic parameters (# data elements).
Six basic MPI functions:
  MPI_Init().
  MPI_Comm_rank().
  MPI_Comm_size().
  MPI_Send().
  MPI_Recv().
  MPI_Finalize().

## Slide 18: Software stacks in MPSoCs
Software stack manages resources, abstracts hardware details.
Performance, power requirements dictate a shorter stack than in general-purpose systems.

## Slide 19: Typical MPSoC stack
Application layer provides user function.
Application-specific libraries are tailored.
Interprocess communicaiton provides services across multiprocessor.
RTOS controls basic system functions.
HAL uniformly abstracts basic hardware services.
Hardware abstraction layer
Real-time operating system
Interprocess communication
Applications
Application-specific
libraries

## Slide 20: Multiflex programming environment
Paulin et al.: uses hardware accelerators plus software to provide multiprocessor communication.
Two models:
  Distributed system object component (DSOC).
  Symmetric multiprocessing (SMP).
DSOC is an object-oriented model.
  Client marshals data for call.
  Server side unmarshals data for use.
SMP engine uses memory-mapped reads/writes.

## Slide 21: MultiFlex concurrency engine
[Pau06] © 2006 IEEE

## Slide 22: Ensemble
Library for large data transfers.
Used with annotated Java.
  Analyze array accesses and data dependencies.
Provides send and receive fucntions.

## Slide 23: Example: OMAP software platform
ARM CSL (OS-independent)
DSP CSL (OS-independent)
High-
Level
OS
Device
Drivers
DSP
RTOS
Device
Drivers
DSP/BIOS
Bridge
CSLAPI
Gateway components
DSP SW components
DSP Bridge
API
DDAPI
DDAPI
MM OS server
App-
specific
MM services, plug-ins, protocols
Multimedia APIs

## Slide 24: DSPBridge
Abstracts the DSP software architecture for the general-purpose software environment.
APIs include driver interfaces and application interfaces:
  Initiate and control DSP tasks.
  Exchange messages with DSP.
  Stream data to/from DSP.
  Check status.

## Slide 25: Resource manager
API interface to the DSP.
  Loads, initiates, and controls DSP applications.
Keeps track of resources:
  CPU time, memory pool, utilizatoin, etc.
Controls:
  Tasks.
  Data streams between DSP and CPU.
  Memory allocation.

## Slide 26: Multimedia messaging service
Minimum requirement from spec:
  JPEG, MIME text with SMS, GSM AMR, H.263, SVG for graphics.
Optional: AAC, MP3, MIDI, MP4, and GIF.
Must provide: MM presentation, user notification, MM message retrieval.
Additional functions: MM composition, MM submission, MM message storage, encryption/decryption, user profile management.

## Slide 27: Algorithm DSP
eXpressDSP compliant libraries must implement IALG:
  algAlloc() declares memory requirements.
  algInit() initializes persistent memory.
  algFree() frees memory.
Application-specific functions manipulated through vtable (table of function pointers).

## Slide 28: Network-on-chip services
Nostrum supports a communications protocol stack.
  Delivers packets with destination process identifiers.
  Three compulsory layers: physical layer; data link layer; network layer.
Sgroi et al.: on-chip networking with Metropolis.
  Refine protocol stack by adding adaptors.
  Behavior adaptors communicate between components with different models of computation.
  Channel adapters correct for limitations of channels.
Benini and De Micheli use micronetwork stack to manage NoC power:
  Physical layer.
  Architecture and control layer.
  Software layer.

## Slide 29: Quality-of-service
QoS must be measured system-wide.
  One component can destroy system QoS characteristics.
QoS modeling:
  Contract specifies resources.
  Protocol manages the contract.
  Scheduler implements the contract.
Resources must be available to deliver on the contract.

## Slide 30: Multiparadigm scheduling
Gill et al.: mix-and-match scheduling policies.
Can combine static, priority, and hybrid scheduling algorithms.
[Gil03] © 2003 IEEE

## Slide 31: Scheduler synthesis
Combaz et al.: Generate QoS software that can handle critical and best-effort communication.
Use control-theoretic methods to determine a schedule.
Synthesize statically scheduled code to implement the schedule.

## Slide 32: RT CORBA approaches
Ahluwalia et al.: reactive system modeling and monitoring using RT CORBA.
InteractionElement type specifies an interaction.
Operators allow interaction elements to be combined.
[Ahl05] © 2005 ACM Press

## Slide 33: CORBA-based QoS
Krishnamurthy et al. use several mechanisms.
Contract objects encapsulate agreement in quality description language.
Delegate objects proxy remote objects.
Property managers handle QoS implementation.

## Slide 34: Notification service
Gore et al. use CORBA notification service to support QoS.
  Reliability.
  Priority.
  Expiration time.
  Earliest deliveries time.
  Maximum events per consumer.
  Order policy.
  Discard policy.

## Slide 35: QoS for NoCs
GMRS uses ripple scheduling.
  Scheduling spanning tree organizes resource management process.
QNoC provides four levels of services: urgent, short messages; real-time services; read-write; block-transfer.
Looped containers in Nostrum implement QoS.
  When a packet reaches its destination, return the message to the source to help reserve the network resources.

## Slide 36: Design verification
Verifying multiprocessors is hard:
  Observe and control data.
  Drive part of the system into a desired state.
  Generate and test timing effects.

## Slide 37: CoMET simulator
Virtual processor model describes function of the application running on the processor.
Model cache, I/O, etc. separately.
Simulation backplane connects processor models and hardware models.
[Hel99] © 1999 IEEE

## Slide 38: MESH simulator
Heterogeneous systems simulator.
Events are tagged with either logical or physical time.
Model relationships between logical and physical time using macro and micro events.