## Slide 1: Chapter 7, part 1: Hardware/Software Co-Design
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Performance analysis.
Design representations.

## Slide 3: Data path/controller architecture
Data path performs regular operations, stores data in registers.
Controller provides required sequencing.
Data path
controller

## Slide 4: High-level synthesis
High-level synthesis creates register-transfer description from behavioral description.
Schedules and allocates:
  Operators.
  Variables.
  Connections.
Control step or time step is one cycle in system controller.
Components may be selected from technology library.

## Slide 5: Models
Model as data flow graph.
Critical path is set of nodes on path that determines schedule length.

## Slide 6: Schedules
As-soon-as-possible (ASAP) pushes all nodes to start of slack region.
As-late-as-possible (ASAP) pushes all nodes to end of slack region.
Useful for bounding schedule.
ASAP
ALAP

## Slide 7: First-come first-served, critical path
FCFS walks through data flow graph from sources to sinks.
Schedules each operator in first available slot based on available resources.
Critical-path scheduling walks through critical nodes first.

## Slide 8: List scheduling
Improvement on critical path scheduling.
Estimates importance of nodes off the critical path.
  Estimates how close node is to being critical.
  D, number of descendants, estimates criticality.
  Node with fewer descendants is less likely to become critical.
Traverse graph from sources to sinks.
  For nodes at a given depth, order nodes by criticality.

## Slide 9: Force-directed scheduling
Forces model the connections to other operators.
  Forces on operator change as schedule of related operators change.
Forces are a linear fucntion of displacement.
Predecessor/successor forces relate operator to nearby operators.
Place operator at minimum-force location in schedule.

## Slide 10: Distribution graph
Bound schedule using ASAP, ALAP.
Count number of operators of a given type at each point in the schedule.
  Weight by how likely each operator is to be at that time in the schedule.

## Slide 11: Path-based scheduling
Minimizes the number of control states in controller.
Schedules each path independently, then combines paths into a system schedule.
Schedule path combinations using minimum clique covering.

## Slide 12: Accelerator estimation
How do we use high-level synthesis, etc. to estimate the performance of an accelerator?
We have a behavioral description of the accelerator function.
Need an estimate of the number of clock cycles.
Need to evaluate a large number of candidate accelerator designs.
  Can’t afford to synthesize them all.

## Slide 13: Estimation methods
Hermann et al. used numerical methods.
  Estimated incremental costs due to adding blocks to the accelerator.
Henkel and Ernst used path-based scheduling.
  Cut CFDG into subgraphs: reduce loop iteration count; cut at large joins; divide into equal-sized pieces.
  Schedule each subgraph independently.

## Slide 14: Henkel and Ernst path-based estimation
[Hen01] © 2001 IEEE

## Slide 15: Fast incremental evaluation
Vahid and Gajski estimate controller and data path costs incrementally.
Hardware cost:
  FU = function units.
  SU = storage units.
  M = multiplexers.
  C = control logic.
  W = wiring.
[Vah95] © 1995 IEEE

## Slide 16: Vahid and Gajski estimation procedure
Compile information on data path inputs and outputs, function and storage units, controller states, etc.
Update algorithm changes tables based on incremental hardware changes.
Executes in constant time for reasonable design characteristics.
[Vah95] © 1995 IEEE

## Slide 17: Single- vs. multi-threaded
One critical factor is available parallelism:
  single-threaded/blocking: CPU waits for accelerator;
  multithreaded/non-blocking: CPU continues to execute along with accelerator.
To multithread, CPU must have useful work to do.
  But software must also support multithreading.

## Slide 18: Total execution time
Single-threaded:
Multi-threaded:
P2
P1
A1
P3
P4
P2
P1
A1
P3
P4

## Slide 19: Execution time analysis
Single-threaded:
  Count execution time of all component processes.
Multi-threaded:
  Find longest path through execution.

## Slide 20: Hardware-software partitioning
Partitioning methods usually allow more than one ASIC.
Typically ignore CPU memory traffic in bus utilization estimates.
Typically assume that CPU process blocks while waiting for ASIC.
CPU
ASIC
ASIC
mem

## Slide 21: Synthesis tasks
Scheduling: make sure that data is available when it is needed.
Allocation: make sure that processes don’t compete for the PE.
Partitioning: break operations into separate processes to increase parallelism, put serial operations in one process to reduce communication.
Mapping: take PE, communication link characteristics into account.

## Slide 22: Scheduling and allocation
Must schedule/allocate
  computation
  communication
Performance may vary greatly with allocation choice.
P1
P2
P3
P1
P2
P3
CPU1
ASIC1

## Slide 23: Problems in scheduling/allocation
Can multiple processes execute concurrently?
Is the performance granularity of available components fine enough to allow efficient search of the solution space?
Do computation and communication requirements conflict?
How accurately can we estimate performance?
  software
  custom ASICs

## Slide 24: Partitioning example
before
after
r = p1(a,b);
s = p2(c,d);
z = r + s;
r=p1(a,b);
s=p2(c,d);
z = r + s

## Slide 25: Problems in partitioning
At what level of granularity must partitioning be performed?
How well can you partition the system without an allocation?
How does communication overhead figure into partitioning?

## Slide 26: Problems in mapping
Mapping and allocation are strongly connected when the components vary widely in performance.
Software performance depends on bus configuration as well as CPU type.
Mappings of PEs and communication links are closely related.

## Slide 27: Program representations
CDFG: single-threaded, executable, can extract some parallelism.
Task graph: task-level parallelism, no operator-level detail.
  TGFF generates random task graphs.
UNITY: based on parallel programming language.

## Slide 28: Platform representations
Technology table describes PE, channel characteristics.
  CPU time.
  Communication time.
  Cost.
  Power.
Multiprocessor connectivity graph describes PEs, channels.
Type | Speed | cost
ARM 7 | 50E6 | 10
MIPS | 50E6 | 8
PE 1
PE 2
PE 3