## Slide 1: Chapter 7, part 2: Hardware/Software Co-Design
High Performance Embedded Computing, second edition
Marilyn Wolf

## Slide 2: Topics
Hardware/software partitioning.
Co-synthesis for general multiprocessors.

## Slide 3: Hardware/software partitioning assumptions
CPU type is known.
  Can determine software performance.
Number of processing elements is known.
  Simplifies system-level performance analysis.
Only one processing element can multi-task.
  Simplifies system-level performance analysis.

## Slide 4: Two early HW/SW partitioning systems
Vulcan:
  Start with all tasks on accelerator.
  Move tasks to CPU to reduce cost.
COSYMA:
  Start with all functions on CPU.
  Move functions to accelerator to improve performance.

## Slide 5: Gupta and De Micheli
Target architecture: CPU + ASICs on bus
Break behavior into threads at nondeterministic delay points; delay of thread is bounded
Software threads run under RTOS; threads communicate via queues

## Slide 6: Specification and modeling
Specified in Hardware C. Spec divided into threads at non-deterministic delay points.
Hardware properties: size, # clock cycles.
CPU/software thread properties:
  thread latency
  thread reaction rate
  processor utilization
  bus utilization
CPU/ASIC execution are non-overlapping.

## Slide 7: HW/SW allocation
Start with unbounded-delay threads in CPU, rest of threads in ASIC.
Optimization:
  test one thread for move
  if move to SW does not violate performance requirement, move the thread
  feasibility depends on SW, HW run times, bus utilization
  if thread is moved, immediately try moving its successor threads

## Slide 8: COSYMA
Ernst et al.: moves operations from software to hardware.
Operations are moved to hardware in units of basic blocks.
Estimates communication overhead based on bus operations and register allocation.
Hardware and software communicate by shared memory.

## Slide 9: COSYMA design flow

## Slide 10: Cost estimation
Speedup estimate for basic block b:
  Dc(b) = w(tHW(b) - tSW(b) + tcom(Z) - tcom(Z + b)) * It(b)
  w = weight, It(b) = # iterations taken on b
Sources of estimates:
  Software execution time (tSW ) is estimated from source code.
  Hardware execution time (tHW ) is estimated by list scheduling.
  Communiation time (tcom ) is estimated by data flow analysis of adjacent basic blocks.

## Slide 11: COSYMA optimization
Goal: satisfy execution time. User specifies maximum number of function units in co-processor.
Start with all basic blocks in software.
Estimate potential speedup in moving a basic block to software using execution profiling.
Search using simulated annealing. Impose high cost penalty for solutions that don’t meet execution time.

## Slide 12: Improved hardware cost estimation
Used BSS high-level synthesis system to estimate costs.
  Force-directed scheduling.
  Simple allocation.
CDFG
scheduling
allocation
controller
generation
logic
synthesis
Area,
Cycle time

## Slide 13: Vahid et al.
Uses binary search to minimize hardware cost while satisfying performance.
Accept any solution with cost below Csize.
Cost function:
  kperf(S performance violations) + karea(S hardware size).
[Vah94]

## Slide 14: CoWare
Describe behavior as communicating processes.
Refine system description to create an implementation.
Co-synthesis implements communicating processes.
Library describes CPU, bus.

## Slide 15: Simulated annealing vs. tabu search
Eles et al. compared simulated annealing, tabu search.
  Tabu search uses short-term and long-term memory data structures.
Objective function:
Showed that simulated annealing, tabu search gave similar results but tabu is 20 times faster.

## Slide 16: LYCOS
Unified representation that can be derived from several languages.
Quenya based on colored Petri nets.
[Mad97]

## Slide 17: LYCOS HW/SW partitioning
Speedup for moving BSB to hardware:
Evaluates sequences of BSBs, tries to find combination of non-overlapping BSBs that gives largest speedup, satisfies area constraint.

## Slide 18: Estimation using high-level synthesis
Xie and Wolf used high-level synthesis to estimate performance and area.
  Used fast ILP-based high-level synthesis system.
Global slack: slack between deadline and task completion.
Local slack: slack between accelerator’s completion time and start of successor tasks.
Start with fast accelerators, use global and local slacks to redesign and slow down accelerators.

## Slide 19: Serra
Combines static and dynamic scheduling.
  Static scheduling performed by hardware unit.
  Dynamic scheduling performed by preemptive scheduler.
Never set defines combinations of tasks that cannot execute simultaneously.
Uses heuristic form of dynamic programming to schedule.

## Slide 20: Co-synthesis to general architectures
Allocation and scheduling are closely related:
  Need schedule/performance information to choose allocation.
  Can’t determine performance until processes are allocated.
Must make some assumptions to break the Gordian knot.
Systems differ in the types of assumptions they make.

## Slide 21: Co-synthesis as ILP
Prakash and Parker formulated distributed system co-synthesis as an ILP problem:
specified as a system of tasks = data flow graph;
architecture model is set of processors with direct and indirect communication;
constraints modeled data flow, processing times, communication times.

## Slide 22: Kalavade et al.
Uses both local and global measures to meet performance objectives and minimize cost.
Global criterion: degree to which performance is critically affected by a component.
Local criterion: heterogeneity of a node = implementation cost.
  a function which has a high cost in one mapping but low cost in the other is an extremity
  two functions which have very different implementation requirements (precision, etc.) repel each other into different implementations

## Slide 23: GCLP algorithm
Schedule one node at a time:
  compute critical path
  select node on critical path for assignment
  evaluate effect of change in allocation of this node
  if performance is critical, reallocate for performance, else reallocate for cost
Extremity value helps avoid assigning an operation to a partition where it clearly doesn’t belong.
Repellers help reduce implementation cost.

## Slide 24: Two-phase optimization
Inner loop uses estimates to search through design space quickly.
Outer loop uses detailed measurements to check validity of inner loop assumptions:
  code is compiled and measured
  ASIC is synthesized
Results of detailed estimate are used to apply correction to current solution for next run of inner loop.

## Slide 25: SpecSyn
Supports specify-explore-refine methodology.
Functional description represented in SLIF.
Statechart-like representation of program state machine.
SLIF annotated with area, profiling information, etc.
[Gaj98]

## Slide 26: SpecSyn synthesis
Allocation phase can allocate standard/custom processors, memories, busses.
Partitioning assigns operations to hardware.
Refined design continues to be simulatable and synthesizable:
  Control refinement adds detail to protocol, etc.
  Data refinement updates vlalues of variables.
  Architectural refinements resolve conflicts, improve data transfers.

## Slide 27: SpecSyn refinement
[Gon97b]
© 1997
ACM Press

## Slide 28: Successive-refinement co-synthesis
Wolf: scheduling, allocation, and mapping are intertwined:
  process execution time depends on CPU type selection
  scheduling depends on process execution times
  process allocation depends on scheduling
  CPU type selection depends on feasibility of scheduling
Solution: allocate and map conservatively to meet deadlines, then re-synthesize to reduce implementation cost.

## Slide 29: A heuristic algorithm
1. Allocate processes to CPUs and select CPU types to meet all deadlines.
2. Schedule processes based on current CPU type selection; analyze utilization.
3. Reallocate processes to CPUs to reduce cost.
4. Reallocate again to minimize inter-CPU communication.
5. Allocate communication channels to minimize cost.
6. Allocate devices, to internal CPU devices if possible.

## Slide 30: Example
1—allocate and
map for deadlines:
P1
CPU1:ARM9
P2
CPU2:ARM7
P3
3—reallocate
for cost:
CPU3:ARM9
P1
CPU1:VLIW
P2
CPU2:ARM7
P3
4—reallocate for
communication:
P1
CPU1:ARM9
P3
CPU2:ARM7
P2
5—allocate
communication:
P1
CPU1:ARM9
P2
CPU2:ARM7
P3

## Slide 31: PE cost reduction step
Step 3 contributes most to minimizing implementation cost. Want to eliminate unnecessary PEs.
Iterative cost reduction:
  reallocate all processes in one PE;
  pairwise merge PEs;
  balance load in system.
Repeat until system cost is not reduced.

## Slide 32: COSYN
Dave and Jha: co-synthesize systems with large task graphs.
Prototype task graph may be replicated many times.
  Useful in communication systems---many separate tasks performing same operation on different data streams.
COSYN will adjust deadlines by up to 3% to reduce the length of the hyperperiod.

## Slide 33: COSYN task and hardware models
Technology table.
Communication vector gives communication time for each edge in task graph.
Preference vector identifies the PEs to which a process can be mapped.
Exclusion vector identifies processes that cannot share a PE.
Average power vector.
Memory vector defines memory requirements.
Preemption overhead for each PE.

## Slide 34: COSYN synthesis procedure
Cluster tasks to reduce search space.
Allocate tasks to PEs.
  Driven by hardware cost.
Schedule tasks and processes.
  Concentrates on scheduling first copy of each task.
  Allows mixed supply voltages.
[Dav99b] © 1999 IEEE

## Slide 35: Allocating concurrent tasks for pipelining
Proper allocation helps pipelining of tasks.
Allocate processes in hardware pipeline to minimize communication cost, time.

## Slide 36: Hierarchical co-synthesis
Task graph node may contain its own task graph.
Hardware node is built from several smaller PEs.
Co-synthesize by clustering, allocating, then scheduling.

## Slide 37: Co-synthesis for fault tolerance
COFTA uses two types of checks:
  Assertion tasks compute assertions and issue an error when the assertion fails.
  Compare tasks compare results of duplicate copies of tasks and issue error upon disagreement.
System designer specifies assertions.
  Assertions can be much more efficient than duplication.
Duplicate tasks are generated for tasks that do not have assertions.

## Slide 38: Allocation for fault tolerance
Allocation is key phase for fault tolerance.
Assign metrics to each task:
  Assertion overhead of task with assertion is computation + communication times for all tasks in transitive fanin.
  Fault tolerance level is assertion overhead plus maximum fault tolerance level of all processes in its fanout.
  Both values must be recomputed as design is reclustered.
COFTA shares assertion tasks when possible.

## Slide 39: Protection in a failure group
1-by-n failure group:
  m service modules that perform useful work.
  One protection module.
Hardware compares protection module against service modules.
General case is m-by-n.
[Dav99b]