## Slide 1: Electronic computers
The Physics of Computing
Chapter 1: Electronic Computers

## Slide 2: Topics
Mechanical computing devices
Theories of computing
Electronic computers
Computer system metrics

## Slide 3: Jacquard loom
Represented weaving pattern on cards that guided/blocked needles.
Early form of memory or programming.

## Slide 4: Babbage analytical engine
Built in 1833.
Punched cards for memory a la Jacquard.
Powered by steam engine.
Gears and shafts represent numbers.

## Slide 5: Astanoff-Berry Computer
First electronic digital computer.
300 vacuum tubes.
Capacitors on rotating drum for memory.
No program store.
By User:Manop - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=887139

## Slide 6: Analog computers
Widely used:
  Electronic music
  Aircraft simulation.
  Process control.
Problems:
  Temperature sensitivity.
  Component variation sensitivity.
  Non-programmable.

## Slide 7: Core memory
Widely used as main memory into the 1970s.
Bit stored on magnetic donut.
  Wires through donut hole provide currents for reading, writing.
Cores had to be strung by hand.
  High cost, limited size.
Marilyn Wolf

## Slide 8: Computability and computational theory
Hilbert: Is there a mechanical procedure for proving whether a mathematical statement is true or false?
Algorithm: effective procedure.

## Slide 9: l calculus
Church and Kleene showed that some number theoretic functions could be represented as recursive functions.
Defines a set of expressions.
  Abstractions: variable x, M in L -> (lx.M) in L
  Applciations: M, N in L -> (M N) in L

## Slide 10: Turing machine
Infinite tape divided into cells.
Head can read/write symbols on tape (not always 0/1).
Action table or transition function defines actions based on current tape symbol.
State register stores current state.
…
…

## Slide 11: Turing machine formal definition
Q is a finite, non-empty set of states.
G is a finite, non-empty set of tape symbols.
B ∈G is the blank symbol.
S ⊆G is the set of input symbols
q0 ∈Q is the initial state
F ⊆Q is the set of accepting states
D: Q/F X G -> Q x G x {L,R} is the transition function.

## Slide 12: Church-Turing thesis
Every effectively calculable function is a computable function.
Many models of computation are equivalent to Turing machines---Turing complete.

## Slide 13: What cannot be computed?
If the algorithm never terminates with an answer, the problem is undecidable.
Halting problem: can’t show in general what set of Turing machine programs will terminate.
Many interesting problems are semi-decidable:
  Generate all possible answers of length 0, 1, …
  If you find an answer that works, you are done.
  If no such answer exists, you will never stop.
Godel undecidability theorem:
  Some statements have proofs of both proof and falsity.

## Slide 14: Church vs. Turing
Turing machine was proposed as second model of computation.
More closely reflects the physical nature of computation.
  Tape is a form of memory.
If algorithms are written as recursive functions, they still have to be mapped onto a non-recursive Turing/von Neumann machine to be executed.

## Slide 15: Turing vs. physics
Similarities:
  Discrete values.
  Discrete time.
  Read an instruction from tape/memory.
  Write values to memory.
Real computer has finite memory.
  A big enough memory approximates an infinite tape.
State representation relies on approximations.
von Neumann machine stores the program in the same memory as data.
Turing didn’t bother with a mechanism to change the program.

## Slide 16: Computer system metrics
Performance: how fast?
  A common marketing figure and important practical metric.
Energy and power: how much energy per operation?
  Critical for both data centers and mobile devices.
Thermal: how hot?
  Fan noise,reliability, …
Reliability: how often does it make mistakes?
  A fundamental trade-off in design.