## Slide 1: Integrated circuits
The Physics of Computing
Chapter 2: Integrated Circuits

## Slide 2: Topics
Moore’s Law
Manufacturing processes
Lithography
Yield
Separation of concerns

## Slide 3: Moore’s Law
Proposed by Gordon Moore.
Number of transistors per chip doubles periodically.
  18 months rate holds for much of history.
Process is often named after size of smallest feature or channel length.
Technology node: a manufacturing process at a given line width.
Chart: Year
| 1971 | 1974 | 1978 | 1979 | 1982 | 1985 | 1989 | 1993 | 1995 | 1997 | 1999 | 2002 | 2003 | 2004 | 2008 | 2010 | 2012 | 2014
transistor count | 2300 | 3500 | 29000 | 68000 | 134000 | 275000 | 1200000 | 3100000 | 5500000 | 7500000 | 9500000 | 55000000 | 220000000 | 592000000 | 758000000 | 1160000000 | 3100000000 | 4200000000

## Slide 4: Transistor length over time (ITRS)
Transistor sizes have shrunk exponentially for over 50 years.
Chart: year
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
 | 65 | 53 | 45 | 37 | 32 | 28 | 25 | 23 | 29 | 27 | 24 | 22 | 20 | 18 | 17 | 15.3 | 14 | 12.8 | 11.7 | 10.6 | 9.7 | 8.9 | 8.1 | 7.4 | 6.6 | 5.9

## Slide 5: Manufacturing processes
Planar process: transistors are built horizontally.
Wires are built up over silicon dioxide.
  Via is a metal-filled hole used to connect material on two layers.
Manufactured in clean rooms due to extremely small feature sizes.
via
via
channel
channel

## Slide 6: Manufacturing steps
Manufacturing step:
  Use mask to pattern material using photoresist.
  Deposit or remove material.
  Process material.
Full process requires many steps:
  Front-end-of-line (FEOL) primarily transistors.
  Back-end-of-line (BEOL) mostly wiring.
Devices must be tested:
  Functional testing.
  Parametric testing.
pattern
deposit material
process material
processing step
wafer prep
diffusions
polysilicon
metal
passivation
process

## Slide 7: Packaging
Wafer is sawed into chips.
Chips are packaged:
  Provides larger, easier connections using pins.
  Protects from the environment.

## Slide 8: Lithography
Patterns are formed on the wafer by the mask using lithography.
Optics limits minimum feature size.

## Slide 9: Rayleigh’s criterion
Features produce diffraction patterns when projected.
Rayleigh’s criterion:
  Minimum resolution occurs when center of one diffraction pattern is aligned with first minimum of other diffraction pattern.
Resolution largely determined by wavelength of light used.

## Slide 10: Example: lithographic resolution
Krypton fluoride (KrF) laser wavelength of 248 nm.
Minimum resolution .
Visible light does not provide enough resolution for modern feature sizes.
Optical enhancements: immerse optics in liquid, reduce aperture.
Masking: computational lithography, double patterning.
Light source: use short-wavelength light source.

## Slide 11: Yield
Manufacturing processes have natural variation.
Yield: fraction of chips that work.
Each manufacturing step limits yield:
Manufacturing problems can affect parameters: device current, etc.

## Slide 12: Example: sensitivity of drain current

## Slide 13: Separation of concerns
Some characteristics are determined by the process:
  Device transconductance.
  Oxide thickness.
  Wire thickness.
Some characteristics are chosen by circuit designer.
  Transistor size.
  Wire width and length.

## Slide 14: Parameter relationships
gate oxide
thickness
threshold
voltage
drain
current
1/x
x
W/L
x
gate
capacitance
1/x
x