## Slide 1: The CMOS inverter and static characteristics
The Physics of Computing
Chapter 3: Logic Gates

## Slide 2: Topics
The CMOS inverter
Static gate characteristics

## Slide 3: Physical properties
Performance---speed.
Energy and power.
Reliability

## Slide 4: Complementary MOS
Circuits make use of both n-type and p-type transistors.
Twin-tub process---each type of transistor is built in a tub with the proper doping.
  Connections between the tubs must be made with metal wires.
  Tubs must be connected to proper power supply terminal for biasing.
n-type
p-type
p
p
n
n

## Slide 5: Static CMOS inverter
Static CMOS composed of pullup and pulldown networks.
  Pulldown is n-type.
  Pullup is p-type.
Operation:
  Input at ground---p-type transistor on, output connected to VDD.
  Input at VDD ---n-type transistor is on, output connected to ground.
+

## Slide 6: Voltages and logic levels
Each logic level is represented by a range of voltages.
Unknown value X represents intermediate region between logic 0 and logic 1.
  Separating 0 and 1 regions is important to reliability.
X is very different from logic don’t-care:
  Input don’t-cares are shorthand.
  Output don’t-cares are incomplete specification.
  X is a distinct logic value.
VDD
VSS
VH
VL
logic 1
logic 0
unknown (X)

## Slide 7: Voltage waveforms and logic levels
Voltage waveforms can be mapped onto logic levels.
Time intervals for each logic level are determined by waveform and logic level definitions.
VDD
VSS
VH
VL
1
0
X
time
t1
t0
time
t1
t0
1
X
0

## Slide 8: Transfer curves
Gate transfer curve is a static characteristic---no time involved.
  Vin on x axis, Vout on y axis.
Operating regions:
  Low Vin, p-type saturated, n-type off or linear.
  Midrange, both transistors saturated.
  High Vin, p-type linear or off, n-type saturated.
Vout
Vin
VDD
VSS
VSS
VDD
p saturated,
n linear
n saturated,
p linear
both saturated

## Slide 9: Transfer curve and transistor sizes
Transfer curve depends on transistor W/Ls.
Equal-sized transistors give a weak pullup.
Equal-be3ta transistors give equal pullup, pulldown currents, moves transfer curve to right.
Chart: Vin

## Slide 10: Transfer curve and logic levels
Transfer curve can be used to establish logic levels.
Separate input and output levels:
  Input low VIL, output low VOL.
  Input high VIH, output high VOH.
Commonly used criteria: slope = -1 points.
Vout
Vin
VOH
VOL
slope = -1
slope = -1
VIL
VIH

## Slide 11: Logic level compatibility
We require that output logic levels be compatible with input levels:
  VOH > VIH
  VOL < VIL
Ensuring compatibility allows gates to restore logic levels.
Noise margins measure compatibility:
VOH > VIH
VOL < VIL

## Slide 12: Noise margins and device characteristics
If transconductances are equal:
Increasing threshold voltage improves noise margins.

## Slide 13: Middle voltage
Middle voltage VM is a useful analysis tool.
Transistor gates are connected:
Drain currents equal:
Sum of drain/source voltages:
Saturation drain currents:
Middle voltage: