## Slide 1: Delay and power
The Physics of Computing
Chapter 3: Logic Gates

## Slide 2: Topics
Transistor models
RC models for delay
Drive and loads
Power and energy

## Slide 3: Transistor model
Even long-channel MOSFET model is too complex for hand analysis of gates.
Simple model:
  Resistor controlled by a switch.
  Characterized by effective resistance.

## Slide 4: Effective resistance
Average of two resistances:
  Linear region resistance.
  Saturation region resistance.
Linear region:
Saturation region:
Vds
Id
Vgs = VDD
VSS
VDD
plin
psat
1/Rlin
1/Rsat
linear-saturation boundary

## Slide 5: Effective resistance, cont’d.
Resistances in each region:
Effective resistance:
Use for generic transistor, for n-type, for p-type.
Effective resistance scales with .

## Slide 6: Example: transistor effective resistance
n-type |  | 
p-type |  | 
n-type |  | 
p-type |  | 

## Slide 7: Example: sensitivity of Rt
Chart: Vt
| 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6
Rt | 4115.2263 | 4659.3885 | 5349.7942 | 6249.0474 | 7458.8477
Chart: k'
| 6.4999999999999997E-4 | 6.9999999999999999E-4 | 7.5000000000000002E-4 | 8.0000000000000004E-4 | 8.4999999999999995E-4 | 8.9999999999999998E-4
Rt | 6666.6667 | 6190.4762 | 5777.7778 | 5416.6667 | 5098.0392 | 4814.8148

## Slide 8: Waveforms and delay
Measure delay relative to waveform.
  Use different voltage levels than for static logic levels.
Terms:
  Rise time 0->1 transition.
  Fall time 1->0 transition.
Rise and fall times are not always equal.
time
V1
V2
0->1 delay
(rise time)
1->0 delay
(fall time)

## Slide 9: Capacitive load
Each gate drives a capacitive load.
  Formed by the transistor gate capacitances of the next logic gate.
  .
  Both transistors contribute even if off.
Delay cannot be determined without knowing capacitive load.
  Same gate, different loads -> different delays.

## Slide 10: Inverter switched resistor model
Pullup, pulldown modeled by switched resistors.
Input voltage controls both transistors.
+
Vin
+
Vout
+
Rp
Rn
CL

## Slide 11: RC delay model
Logic gate input controls effective resistance.
Fall time case:
  Load capacitance is charged to VDD.
  Effective resistance connected to ground.
Complementary configuration for rise time case.
Vin
+
Rn
CL
Vout
-

## Slide 12: Rise time and fall time
Simplifying assumption---input is step, only one transistor is on at a time.
Allows us to consider only one effective resistance at a time.
+
Vin
+
Vout
+
Rp
Rn
CL

## Slide 13: Swimming pool model of charge
Water corresponds to charge.
Water flow corresponds to current.
Height of water tower corresponds to voltage.
How long does it take to fill the pool?
  Height of water tower.
  Diameter (resistance) of water spout.
  Size of pool.
I
V
C

## Slide 14: Fall time analysis
Time constant .
Vout
t
Vin
VSS
VDD
VSS
VDD

## Slide 15: Delay metrics
Delay: 0-50% (or 50%-0) time.
Transition (rise/fall) time: 10%-90% (or 90%-10%) delay.

## Slide 16: Example: inverter delay
,
delay (falling) | 
fall time | 
delay (rising) | 
rise time | 
delay (falling) | 
fall time | 
delay (rising) | 
rise time | 

## Slide 17: Example: inverter delay plot
RC approximation compares well with detailed transistor models.
Chart: time (s)

## Slide 18: Transistor sizing
Circuit designer can choose transistor W/Ls.
  Every transistor can be of a different size.
  Transconductance k’ fixed by manufacturing.
Effective resistance scales with :

## Slide 19: Example: transistor sizing
Chart: W/L
| 1 | 2 | 3 | 4 | 5
t_f | 3.975e-10 | 1.9875e-10 | 1.325e-10 | 9.9375e-11 | 7.95e-11

## Slide 20: Transconductances and delay
p-type transistor has lower transconductance than n-type.
To give equal rise/fall times, p-type transistor must be larger.

## Slide 21: Drives and loads
Increasing transistor sizes increases drive of the gate.
Also increases load presented to the previous gate, slowing down that gate.

## Slide 22: Driving large loads
How to efficiently drive a large capacitive load?
  Off-chip connections, clock network, etc.
Use a series of scaled inverters:
C1
Cbig

## Slide 23: Power and energy
Power and energy consumption are key metrics for many systems.
Low power consumption was critical to early success of CMOS.

## Slide 24: Why complementary logic?
Not all logic families are complementary.
nMOS uses a pullup transistor that is always on.
Short circuit current flows continuously when pulldown is on.
+
in
out
+
in
out

## Slide 25: Switching energy
Energy to charge capacitor
Switching energy includes charge, discharge energy:

## Slide 26: Short circuit current
Both transistors may be on during part of the transition.
Short circuit current does not help to charge the load capacitance.
No short circuit current if
Chart: Vin (V)

## Slide 27: Power
Power is energy per unit time.
Given operating frequency :

## Slide 28: Delay vs. power
CMOS logic can operate over a wide range of power supply voltages.
Consider effective resistance at end of saturation range:
Effective resistance and delay scale linearly with power supply voltage.
Speed-power product

## Slide 29: Static power
Modern devices are not ideal, use current even when below threshold voltage.
Leakage current contributes to power consumption.
Total power is dynamic plus static
Leakage current stops only when transistor is off.
  Use sleep transistor to control power supply to gate.

## Slide 30: Dynamic voltage and frequency scaling
Dynamic voltage and frequency scaling (DVFS) takes advantage of relationship between power supply voltage and delay:
  Delay scales linearly with power supply voltage.
  Power consumption scales quadratically with power supply voltage.
DVFS allows logic to be set to minimum voltage level that provides required performance.
  Save power when maximum performance is not needed.

## Slide 31: Race-to-dark
In advanced processes, leakage power is larger than dynamic power.
Gates must be turned off to eliminate leakage.
Race-to-dark:
  Run as fast as possible to finish task.
  Turn off logic when done.