## Slide 1: Combinational logic
The Physics of Computing
Chapter 4: Sequential Machineco

## Slide 2: Topics
Event model
Network model
Gain and reliability
Gain and delay
Gain and power
Noise and reliability
Power supply and reliability
Noise and input/output coupling

## Slide 3: Event model
First step in abstracting voltage waveforms.
Discrete values on signals: 0, 1, X.
  A change in value is an event or transition.
An event is a value-time pair .
g1
i1
i2
o1
delay d = 1
o2

## Slide 4: How gates process events
A gate accepts events at its inputs and generates events at its output.
  Time delay from input to output.
Simple gate delay model: constant, value-independent.
Simplifying assumption: if input does not cause a change to the gate’s output value, no event is generated.
time
0
1
2
3
g1
i1
o1
i2
o2

## Slide 5: Gate delay models
Inertial delay ignores glitches---input must change for some minimum time to create an output event.
Transport delay propagates all changes.

## Slide 6: Combinational logic networks
Gates are connected into combinational logic networks:
  Primary inputs.
  Primary outputs.
Can be modeled as a graph.
  Often called a netlist.
No cycles in a combinational logic network.
g1
g2
g3
g4
0
1
1
1
1
0
0
0
0
primary
inputs
primary
outputs

## Slide 7: Event propagation
Output events of one gate become input events to next gate.
A signal may see several events before settling to its final value.
g1
i1
i2
o1
g2
i3
o2
o3
o4
o5
time
0
1
2
3
g1
g2
i1
i3
i2
o1
o4
o3
o2
o5

## Slide 8: Worst-case delay
Many logic design problems depend on worst-case delay from any primary input to any primary output.
Determined by the critical path(s) through the logic.
  Label distance to each node in forward and backward directions.
  Critical nodes do not move.
Delay model:
  Directed edges.
  Delay weights on logic gate nodes.

## Slide 9: Delay optimization
To reduce worst-case delay, must speed up all the critical paths.
Find a custet through the critical path:
  Removing cutset edges eliminates all paths from primary inputs to primary outputs.

## Slide 10: Gain and reliability
Logic gates are amplifiers.
Gain is a basic characteristic of amplifiers:
Can measure gain from inverter transfer curve.
  Gain varies, typically interested in gain at middle of curve.
Vout
Vin
VDD
VSS
VSS
VDD
A

## Slide 11: Saturating inverter model
Simple model for inverter: constant gain in middle of range, saturated at ends of range.
Vin
v
v
-v
-v
VIH
VIL
Vout
gain |A|

## Slide 12: Gain and signal levels
Slope affects translation of input levels to output levels.
At high gains, output voltage is higher than input voltage---restores logic levels.
At low gains, output voltage is lower than input voltage---less reliable.
v
v
-v
-v
VIH
VIL
Vout
gain |A| < 1
gain |A| > 1

## Slide 13: Gain and delay
Gain improves delay for slow-rising inputs.
Gain helps with cascaded logic:

## Slide 14: Gain and delay example
time
v
-V
t
|A|=1
VL
VH
time
v
-V
t
VL
VH
|A| > 1
time
v
-V
t
VL
VH
|A| < 1

## Slide 15: Transistor-level view of-slow rising inputs
Drain current depends on gate voltage.
Fast-rising inputs cause transistor to reach maximum saturation current quickly.
Slow-rising inputs mean transistor is in saturation but not at its maximum current.
Slow-rising inputs result in longer gate delays.
Vds
Id
linear
saturation
fast-rising input
slow-rising
input

## Slide 16: Step vs. ramp input
Chart: time (s)

## Slide 17: Delay and power
Making gates faster costs power.
Speeding up gates not on the critical path doesn’t help delay but costs power.

## Slide 18: Signal integrity
Wires need to carry correct, uncorrupted values.
Noise can come from many sources:
  Other wires.
  Power/ground networks.
  Output coupling.

## Slide 19: Power supply and reliability
Power and ground are signals carried by physical wires.
Noise may be injected at many points.
A finite power supply may not be able to supply high demand at critical times.

## Slide 20: Example: metal wire resistance
Assume resistance per unit length
One transistor draws .
Solve for length of wire that gives 0.1 V drop:

## Slide 21: Power/ground wiring
Power and ground are global signals that must be distributed everywhere.
Interdigitated wires allow power and ground to be delivered to all gates.
Power distribution spread over several layers:
  Higher layers distribute globally.
  Lower layers distribute locally.

## Slide 22: Pin inductance
Pins on packages have inductance.
Rapid changes in current will cause voltage drops across the pin inductance.
Can reduce by spreading power/ground over many pins.

## Slide 23: Example: processor pinout
Intel Xeon E7-8800:
  1581 pins total.
  381 power.
  471 ground.
Assume pin inductance .
Current fluctuation .
Voltage drop across each pin .
If all current carried on one pin,

## Slide 24: Circuit effects of power/ground noise
Noise is a problem for both VDD, ground.
  Concentrate here on ground for simplicity.
Noise can be modeled as a voltage source on the ground pin of each gate.
  Every gate may see different ground noise.

## Slide 25: Ground bounce and current
Ground bounce affects discharge.
  Reduces Vds, reducing current.

## Slide 26: Ground bounce and output levels
Ground bounce affects output voltage level.
  Positive bounce---final voltage is high.
  Negative bounce---final voltage is low.
Chart: 
VIL
VIH
VOL
VOH

## Slide 27: Ground bounce and cascaded gates
If ground bounces enough, logic levels may be violated.
  Large bounce on first gate causes high output voltage.
  Second gate didn’t see bounce, expects normal logic levels.
VB
VOL1
VIL2

## Slide 28: Current demands
Current demands of logic depend on activity.
Different logic blocks may see different activity patterns.
Worst case is when many blocks need current at once.
Power delivery network must be designed for worst case.
VDD
VSS
V
+
-
Logic 1
Logic 2

## Slide 29: Decoupling
Add decoupling capacitance to reduce power/ground noise.
  Low-pass filter on power delivery network.
  Charge reservoir.
CD stores charge, releases it when the power network voltage droops.
  Effect is temporary---can’t compensate for undersized power supply.
CD

## Slide 30: Decoupling capacitor analysis
Voltage droop .
gates each draw for time .
Example:

## Slide 31: Noise and I/O coupling
Gate/source and gate/drain capacitances couple input and output of gate.
Coupling results in feedback.
+

## Slide 32: Miller effect
Effects of coupling can be approximated using Miller effect.
Coupling capacitance Cgd can be approximated by input capacitance Cgd(1+A).
  Increases delay.
Cgd
A
Cgd(1+A)
A