## Slide 1: Interconnect
The Physics of Computing
Chapter 4: Sequential Machines

## Slide 2: Topics
Parasitic impedance
Transmission lines
Crosstalk
Wiring complexity and Rent’s Rule

## Slide 3: Parasitic wiring impedance
Physical material of wires introduces parasitic resistance, capacitance, and inductance.
  We will concentrate here on R and C.
Wire impedance must be taken into account during circuit analysis.
  Wire delay can be larger than gate delay.
Vertical dimensions are fixed by manufacturing.
  Calculate parasitic values based on length and width.

## Slide 4: Parasitic resistance
Sheet resistance is measured in (ohms per square).
Resistance of a wire depends on aspect ratio independent of size:
  Two unit squares in series have resistance .
  Parallel combination of series squares has resistance .
R
R
R
R

## Slide 5: Resistance and current flow
Must know direction of current flow.
R = (sheet resistance)*L/W.
Height of material is determined by manufacturing.
square
square
square
I
L
W

## Slide 6: Parasitic capacitance
Plate spacing is determined by manufacturing.
Capacitance depends on area of plates.
More detailed models:
  Fringing capacitance depends on perimeter.
  Diffusion wires have junction capacitance; may use separate sidewall, bottomwall values.
A

## Slide 7: Example: resistance and capacitance
Metal wire .
Sheet resistance .
Unit capacitance .

## Slide 8: Transmission lines
Lumped model of long wires is inadequate.
Must be modeled as a distributed inductance.
  Current and voltage are functions of both space and time.
We will concentrate on RC transmission lines.

## Slide 9: RC transmission lines
RC transmission line is modeled as a series of RC setions.
Assume step input.
Capacitors closer to input charge before capacitors near the output.

## Slide 10: Step input propagation
x
voltage

## Slide 11: Pulse propagation
Pulse is delayed and distorted.
x
voltage

## Slide 12: RC section pulse response
Chart: time (s)

## Slide 13: Elmore model
Simple estimate of RC wire delay.
Use the mean (50%) voltage as a measure of delay.
Each capacitor is charged by all of the resistances before it.
Delay is proportional to square of wire length.
  Worse than ideal scaling model.
r1
r2
r3
c1
c2
c3

## Slide 14: Elmore delay
General case of arbitrary combinations of wire sections:
Special case of uniform wire sections:

## Slide 15: Example: Elmore delay
Metal wire . Divide into sections.
One section:
Total delay:
Longer wire---use same section size, more sections:

## Slide 16: Non-uniform wires
Non-uniform wires can be modeled by Elmore delay.
Wide sections near source give low resistance to feed later sections.
Narrow sections near sink have smaller capacitance.
r1, c1
r2, c2
r3, c3

## Slide 17: Crosstalk
Wire sides, top, bottom form parallel plates with other wires.
Coupling capacitance causes one wire to inject noise into other wires.
Wires can also be inductively coupled---we concentrate here on capacitive coupling.

## Slide 18
Substrate capacitance
Coupling capacitance

## Slide 19: Crosstalk modeling
Aggressor net injects noise into victim net.
  Roles can be reversed.
Transition on aggressor causes across coupling capacitance.
Substrate voltage doesn’t change in ideal case, coupling to substrate doesn’t inject noise.
aggressor
victim
C
i

## Slide 20: Crosstalk analysis
Coupling capacitance , ground capacitance .
Charge delivered by aggressor:
Resulting voltage change on victim:
Typically so crosstalk is a significant problem.

## Slide 21: Crosstalk mitigation
Interleave signals and ground:
  Coupling to stable ground signal dominates.
Twizzle signals:
  Same total coupling but not all to the same signal.

## Slide 22: Wiring complexity
Wiring complexity helps us estimate design time, potential for crosstalk, etc.
Model complexity by partitioning:
  Find partition that minimizes total wires between partitions.
  Use number of wires as an estimate of complexity.
Can recursively partition to provide finer-grained estimate.
CL 1
CL 2

## Slide 23: Wire length estimation
Given an estimate of logic block placement, can estimate wire length.
Allows early identification of critical paths.
CL
CL
CL
CL
CL
CL
CL
CL
CL

## Slide 24: Rent’s Rule
An empirical model of the relationship between logic and I/O.
Log/log relationship:
is Rent’s constant.
For random logic, .
For microprocessors, .
number of pins
number of gates