## Slide 1: Sequential machines
The Physics of Computing
Chapter 4: Sequential Machines

## Slide 2: Topics
Sequential models
Registers
Clocking
Metastability

## Slide 3: Combinational vs. sequential logic
Combinational logic can be abstracted to Boolean functions.
  No details of internal gate structure.
Combinational logic provides discrete values but not discrete time.
g1
g2
g3
g4
0
1
1
1
1
1
0
0
0
0
Combinational logic

## Slide 4: Discrete time
Turing model requires discrete time.
Sequential machines allow us to operate combinational logic in discrete time.
time
0
1
2
3
0
1
a
b
c
0
0
1
0
0
0
0
1
1
1

## Slide 5: Sequential machine structure
Sequential machine uses registers to control temporal behavior of combinational logic.
Clock signal controls register.
Combinational logic:
  Inputs present state, primary inputs.
  Outputs next state, primary outputs.

## Slide 6: Sequential machine functional models
input | present state | next state | output
0 | 00 | 00 | 0
1 | 00 | 01 | 0
0 | 01 | 01 | 0
1 | 01 | 10 | 0
0 | 10 | 10 | 0
1 | 10 | 00 | 1

## Slide 7: Unspecified states
Symbolic states are encoded in binary.
Not all possible binary codes may be mapped to valid symbolic states.
Unspecified states may be entered via noise, etc.
Unspecified states result in permanent faults.

## Slide 8: Registers
Registers hold state values.
  Controlled by clock input.
Several types of registers:
  How is the value stored?
    Dynamic vs. static.
  How does the register react to the clock?
    Latch vs. flip-flop.
Dynamic vs. static:
  Dynamic value stored on capacitance.
  Static value stored using feedback.
Latch vs. flip-flop:
  Latch is transparent.
  Flip-flop is not transparent.

## Slide 9: Dynamic latch
Dynamic latch stores value on gate input.
Access transistor is controlled by clock.
  When clock is active, D input drives capacitance at inverter input.
Latch is transparent---output follows input when clock is active.

## Slide 10: Static latch
Value is stored on cross-coupled inverters.
When clock is active:
  Access transistor is on, allows forward inverter to be driven.
  Feedback capacitor is off, allowing value to be easily changed.
Latch is still transparent.
D
Q’
f
f’

## Slide 11: Master-slave flip-flop
Master-slave is one type of flip-flop.
  Edge-triggered by clock transition.
  Built from two latches.
When clock is active, first latch is on and transparently reads input.
  Second latch is not transparent, guards output.
When clock goes inactive, second latch transparently feeds output.
  Value is provided by non-transparent first latch.
D
Q
D
Q
f
D
Q

## Slide 12: Register timing characteristics
Register must meet two timing requirements:
  Setup time: data input must be stable before clock edge.
  Hold time: data input must be stable after clock edge.
Violating setup, hold times can cause bad value to be stored.
Setup and hold times may be given as a single parameter defined around the clock edge.
data
clock
ts
th

## Slide 13: Register performance analysis
Register performance depends on gain of the feedback gates.
Internal voltages .
Voltages at capacitors:
Register time constant
Vx
Vy
R
R
C
C

## Slide 14: Clocking
Clock controls behavior of synchronous machine.
  Worst-case combinational logic delay .
Clock, logic must obey timing constraints.
Clock period is most basic property:
time
clock
T
Combinational logic
f
PS
NS

## Slide 15: One-sided timing constraint
Clock period must be longer than worst-case combinational delay:
  .
If clock arrives too soon, register will not be enabled when data arrives.
One-sided constraint means there exists a clock frequency at which the machine will work.
time
0
T
D
f
T1
T2
T1
PS
NS
T1

## Slide 16: Clocking overhead
Setup and hold times must be subtracted from the available clock period:
Signals must be stable before start of setup period, stable until end of hold period.

## Slide 17: Pipelining
Registers can be added to reduce clock period---pipelining.
Pipelining does not change latency, only period.
New clock period , minus setup/hold times.
Combinational logic
D
Combinational logic 1
D/2
Combinational logic 2
D/2
pipeline register rank

## Slide 18: The trouble with latches
Latches require additional constraints for proper operation.
Short paths cause next state outputs to change more than once.
Requires a two-sided timing constraint:
combinational logic
f
short path

## Slide 19: Two-phase clocking
Latch-based systems can be reduced to one-sided timing constraint using two-phase clocking.
  Phases are non-overlapping.
combinational logic 1
combinational logic 2
D
Q
D
Q
f1
f2
T1
T2
f1
f2
time

## Slide 20: Clock skew
Clock does not arrive everywhere at the same time.
Clock skew: relative delays in arrival time of clock.
Example:
  Reg 1 releases values at time
  Reg 2 expects values at time
  Effective clock period is .
D
Q
D
Q
d
f
effective clock period T-d
reg 1
reg 2

## Slide 21: Clock skew timing
time
reg 1
reg 2
T
time
reg 1
reg 2
T-d
no skew
Bad skew

## Slide 22: Clock skew timing, cont’d.
time
f
reg1
no skew
reg2
T
reg1
with skew
T-d

## Slide 23: Example: clock skew
Combinational logic delay of 5 ps.
Clock period of 5 ps.
1 ps clock skew.
Effective clock period is 4 ps---errors.

## Slide 24: Metastability
Intermediate values may be captured and stored in registers for extended periods.
  Indeterminate values.
  Indeterminate settling times.
Metastability is a fundamental physical phenomenon:
  Result of using energy barriers to separate states.
  Metastability can be reduced but not eliminated.
Metastability occurs in real machines and can cause reliability problems if not properly managed.

## Slide 25: Cross-coupled inverters
Transfer curves of cross-coupled inverters have been superimposed.
Cross-coupled inverters have two stable states at the ends of their operating ranges.
Intersection in middle is metastable point.
x
y
v
v
-v
-v
x
y

## Slide 26: Metastability and potential energy
Energy of cross-coupled inverters depends on their state.
Stable points at 0, 1 values minimize potential energy.
The midpoint of the potential energy is the metastable point.
  An electron at the top of the hill may stay there for a long time before rolling down.
  Electron may end up on either side of the hill.
V1 + V2
potential
energy

## Slide 27: Metastability in practice
Metastable states can be captured when the register input is near the middle during the clock event.
Metastability can be observed on an oscilloscope.
  Overlay behavior over many clock cycles.
Final value may go to 0 or 1.
Settling time can vary widely.
time
Vout
alternative
behaviors
variable
timing

## Slide 28: Metastability model
Probability of metastability failure:
  .
  Probability of entering metastable state .
  Probability of not resolving metastable state in time .

## Slide 29: The vulnerable interval
A mid-level voltage may be captured if the register input changes during the setup/hold interval.
Assume that changes to the register input are uniformly distributed over the clock period:
time
tSH
T
D

## Slide 30: The stabilization window
Register has a settling time window S after the setup/hold window.
If metastable value does not settle in time S, the register output is invalid.
Settling time can be modeled by a Poisson process:
Settling failure can also be analyzed using cross-coupled amplifier analysis:
time
tSH
S
Q

## Slide 31: Metastability probability model
Probability of metastability failure:
Dominated by exponential term.

## Slide 32: Example: metastability failure.
Clock frequency of 1 GHz.
Setup/hold time of 10 ps.
Assume , .
.
Probability of failure over 1 second of operation

## Slide 33: Metastability countermeasures
Probability of metastability failure can be reduced by increasing the settling time.
A dual-register synchronizer greatly increases S:
  First register reads value which may be metastable.
  Value is allowed to settle for a full clock cycle before being passed to the second register.
This is not a master-slave flip-flop---both registers clocked at same polarity.
Extra clock cycle must be accounted for in design.
D
Q
D
Q