## Slide 1: Heat Transfer
The Physics of Computing
Chapter 5: Processors and Systems

## Slide 2: Topics
Heat transfer basics.
Thermal analysis:
  Steady-state.
  Transient.
Heat and reliability.

## Slide 3: Heat transfer mechanisms
Conduction:
  Results from molecular motion.
Convection:
  Caused by bulk transfer of fluids (gas or liquid).
Radiation:
  Electromagnetism.

## Slide 4: Example: server operating temperatures
DellPowerEdge R710:
  Operating temperature range .
  Relative humidity levels 20% - 80%.
  Power-to-cool ratio 2.0% (server operating power/power required for cooling).

## Slide 5: Key thermal ratings
Transistor junctions must be kept below maximum junction temperature:
  Temperature at which heat damages the transistor structures.
Chip specifies thermal design power (TDP).
  Amount of operating heat that its cooling system must be able to dissipate.

## Slide 6: Physical properties
Specific heat:
  Relationship between heat input/output and temperature.
  Measured in Joules/kilogram-Kelvin.
Thermal conductivity:
  Relationship between temperature difference and heat flow per unit time.
  Measured in Watts/meter-Kelvin.
material | specific heat (J/kg K) | thermal conductivity (W/m K) | density (kg/m3)
silicon | 710 | 149 | 2.3x10-3
ceramic (aluminum nitride) | 740 | 150 | 3.3x10-3
carbon steel | 620 | 41 | 7.9x10-3

## Slide 7: Thermal properties of objects
Thermal resistance R:
  Thermal conductivity for a specific shape and size of material.
  , length , area , thermal conductivity .
Thermal capacitance C:
  Specific heat for a specific shape and size of material.
  , mass , specific heat .

## Slide 8: Thermal/electrical analogy
electrical | thermal
charge Q | thermal energy Q
current I | heat flow P
voltage V | voltage V
resistance R | thermal resistance R
capacitance C | thermal capacitance C

## Slide 9: Physical laws of thermal behavior
Fourier’s Law of Heat Conduction:
Newton’s Law of Cooling:

## Slide 10: Example: heat transfer of coffee
Added cream cools coffee slightly.
Hypothesis: does coffee with cream cool more slowly than does black coffee?
Chart: time
| 0 | 2 | 3 | 5 | 8 | 10 | 12 | 15 | 17 | 20
black | 161 | 153 | 150 | 146 | 138 | 138 | 134.5 | 131 | 126 | 123.5
cream | 159 | 147 | 147 | 143 | 135 | 134.5 | 131 | 128 | 124 | 123.5

## Slide 11: Heat sink structure
chip
heat
sink
air flow
ambient

## Slide 12: Heat sink example

## Slide 13: Steady-state temperature
Use thermal resistance to determine steady-state temperature.
  Calculate temperature difference from ambient to junctions.
Thermal circuit has a heat source P, thermal resistance R.
Output temperature is measured across thermal resistance.

## Slide 14: Example: heat sink performance
Computer power
Ambient temperature .
Case 1---no heat sink:
Case 2---heat sink:

## Slide 15: Thermal transient analysis
P
R
C
TC
+
-
TA
+
Chip and heat sink form a thermal RC circuit.
  Measure chip temperature relative to ambient.
Temperature as a function of time:
  Temperature above ambient at is .

## Slide 16: Example: thermal RC model of chip temperature
parameter | value
parameter | value
Thermal time constant .
Steady-state temperature .
Chart: time (s)
| 0 | 5.0000000000000001E-3 | 0.01 | 1.4999999999999999E-2 | 0.02 | 2.5000000000000001E-2 | 0.03 | 3.5000000000000003E-2 | 0.04 | 4.4999999999999998E-2 | 0.05 | 5.5E-2 | 0.06
T(t) | 300 | 307.0867 | 312.1646 | 315.803 | 318.4101 | 320.2781 | 321.6166 | 322.5757 | 323.2629 | 323.7553 | 324.1082 | 324.361 | 324.5421

## Slide 17: Thermal square wave
Chip runs periodically:
Chart: time (s)
time
P
-P
Kt
S=2Kt

## Slide 18: Dual-core processor
Two processors alternate between run, stop.
Cores are connected by thermal resistance.
P1
R1
C1
R12
R2
C2
P2

## Slide 19: Dual-core thermal analysis
Can borrow a result from electrical circuits:
  Assume 50% duty cycle, period .
Upward and downward temperature waveforms:
Temperature cycles between :
So

## Slide 20: Dual-core thermal behavior
Chart: time (s)

## Slide 21: Heat and reliability
Heat contributes to aging.
  Higher temperatures cause chips to fail earlier.
Arrhenius’ equation describes the relationship between energy and the rate of physical processes:
  Activation energy is determined by energy required to promote electrons to high orbits.
  Arrhenius prefactor is measured experimentally.

## Slide 22: Example: activation energies for failure mechanisms [Pan09]
failure mechanism | Activation energy
oxide film defect | 0.3 to 1.1 eV
iconicity drift (Na ions in oxide film) | 0.7 to 1.8 eV
slow trap | 0.8 to 1.2 eV
electromigration disconnect | Aluminum: 0.5 to 0.7 eV Copper: 0.8 to 1.0 eV
aluminum corrosion | 0.7 to 0.9 eV
failure mechanism | 
oxide film defect | 0.3 to 1.1 eV
iconicity drift (Na ions in oxide film) | 0.7 to 1.8 eV
slow trap | 0.8 to 1.2 eV
electromigration disconnect | Aluminum: 0.5 to 0.7 eV Copper: 0.8 to 1.0 eV
aluminum corrosion | 0.7 to 0.9 eV

## Slide 23: Electromigration
Electromigration is a common temperature-related failure mechanism.
  Heat causes some molecules in wire to release free atoms.
  Current flowing through wire causes free atoms to move.
  Destructive feedback---thinner wire segments heat more, causing more rapid failure.
Failure rate modeled using Black’s equation:
  , .

## Slide 24: Lifetime analysis
Chip temperature often varies over time based on use case and computing activity.
We can model aging as a function of temperature:
Chip-level reliability engineering:
  Minimize hot spots.
  Use operating system to spread workload across cores.

## Slide 25: Thermal management
A combination of hardware and software is used to manage thermal behavior.
On-chip temperature measured using band gap reference circuit.
Processor may provide a software interface to on-chip temperature sensors.
  Intel Thermal Monitor 1 turns the clocks off and on at a duty cycle chosen for the processor type, typically 30%-50%.
  Intel Thermal Monitor 2 uses dynamic voltage and frequency scaling mechanisms to reduce both the clock speed and power supply voltage of the processor.