## Slide 1: Memory
The Physics of Computing
Chapter 5: Processors and Systems

## Slide 2: Topics
Memory trends.
Memory structures.
Memory system performance.
DRAM systems.
DRAM reliability.

## Slide 3: Memory trends
 | 2011 | 2014 | 2017 | 2020 | 2023
capacity (GBits) | 68.72 | 137.44 | 137.44 | 549.76 | 549.76
generation | 64G | 128G | 128G | 512G | 512G
 | data rate (MTransactions/sec) | CAS latency (ns)
DDR3 | 1066-1866 | 13.1-13.91
DDR4 | 1866-3200 | 13.32-15
memory capacity (ITRS)
memory speeds

## Slide 4: Memory structures
Memory is a 2-D array.
  Cannot access all bits simultaneously.
  Random access.
Interface:
  Read/write and other control.
  Address (input).
  Data (bidirectional).

## Slide 5: Memory organization
Address is divided into row, column bits:
  Row logic decodes row address bits.
  Column logic decodes column address bits.
Memory height, width is chosen by the memory designer.

## Slide 6: Dynamic RAM (DRAM)
Cell includes:
  access transistor;
  storage capacitor (requires refresh).
Addressing lines:
  Horizontal word line.
  Vertical bit line.
Write:
  Put desired bit on bit line.
  Address word line to turn on access transistor.
Read:
  Put bit line at mid voltage.
  Use word line to turn on access transistor.
  Bit line voltage may change depending on storage capacitor value.
  Destructive read---reading a 0 destroys the value on the storage capacitor. Value must be written after read.

## Slide 7: DRAM analysis
DRAM gets bigger but not faster.
Two states:
  Access transistor off, each capacitor has its own value.
  Access transistor on, capacitors store charge.
Access transistor off:
  .
Access transistor on:
  .
  If , .

## Slide 8: SRAM cell
Cell includes:
  Two access transistors.
  Four storage transistors as cross-coupled inverters.
Interface:
  Horizontal word line.
  Vertical bit, bit’ lines.
Write:
  Set bit, bit’ to desired (complementary values).
  Turn on access transistors.
Read:
  Set bit, bit’ to mid-level voltage.
  Turn on access transistors.

## Slide 9: DRAM vs. SRAM
 | DRAM | SRAM
density | very dense | less dense
performance | slower | faster
energy | less energy | more energy

## Slide 10: Memory system performance
Clock speeds have increased much faster than DRAM access times.
Memory wall: memory system performance loses ground to CPU performance.
Comparison:
  1980, VAX-11/780 clock rate 10 MHz, memory access time .
  2016, 4 GHz clock frequency, 80 ns memory access time.

## Slide 11: Caches
Caches provide an intermediate level of memory:
  Faster than DRAM, slower than CPU registers.
  Smaller than DRAM, larger than register file.
Most caches are built from SRAM.

## Slide 12: Memory system performance
Average memory access time .
  Prefetching width of words, perfect prefetching gives .
  Random locations (pointers) gives .
Metrics:
  DRAM/cache ratio .
  Cache/clock ratio .
Average access time in terms of DRAM/cache ratio:
  .

## Slide 13: DRAM system architecture
DRAM is organized into banks to limit size of memory array.
  Accesses can be parallelized across the banks.
Modern DRAM is synchronous to allow pipelining of accesses.
Stacked memory uses through-silicon vias with reduced interconnect impedance.

## Slide 14: DRAM reliability
Typical charge on DRAM:
Alpha particles (protons) generate electrons when they strike the chip.
  Alpha particle loses energy at
  Promoting an electron to conduction band requires .
  Tens of thousands of electrons can be generated by one alpha particle strike.
Alpha particles may come from environment or from packaging.
Error correction codes can be used to detect, correct errors.