## Slide 1: Processors
The Physics of Computing
Chapter 5: Processors and Systems

## Slide 2: Topics
Microprocessor characteristics.
Busses and interconnect.
Global communication.
Clocking.

## Slide 3: Microprocessor characteristics (ITRS)
 | 2011 | 2014 | 2017 | 2020 | 2023
Power (W) | 161 | 152 | 130 | 130 | 130
I/O count | 728-3061 | 800-4075 | 960-5423 | 1050-7218 | 1212-8754
Performance (GHz) | 3.744 | 4.211 | 4.737 | 5.329 | 5.994
 | 2011 | 2014 | 2017 | 2020 | 2023
Power (W) | 161 | 152 | 130 | 130 | N/A
I/O count | 5094 | 5896 | 6826 | 7902 | 9148
Performance (GHz) | 3.744 | 4.211 | 4.737 | 5.329 | 5.994
cost-performance chips
high-performance chips

## Slide 4: Relative access times
L1 cache
L2 cache
L3 cache
DRAM
magnetic disk
solid-state drive
reg
CPU
256 B
1 ns
32 KB
5 ns
64 KB
10 ns
8 MB
40 ns
8 GB
80 ns
128 GB
80 ms
6 TB
8000 ms

## Slide 5: Chip floorplan
Floorplan is a geometric plan for the chip.
  Created during initial chip planning, updated during design.
Shows sizes, positions of major blocks.
  May also show sizes of wiring areas.

## Slide 6: Busses and interconnect
Global wiring delay is a large component of total delay.
Buffers can be added to long wires to improve delay.
  Buffer restores signal.
  Buffer also adds its own delay.
How many buffers for long wires?

## Slide 7: Two segments
Consider dividing a wire into two segments.
Delay components:
  Driver .
  Wire section .
  Termination .

## Slide 8: Delay vs. number of sections
Buffered wire delay:
For small number of sections, additional buffers reduce delay.
For large number of sections, buffer delay dominates and adding buffers increases delay.
Chart: # buffers
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 20 | 30 | 40
 | 5.2002e-10 | 2.8004e-10 | 2.0672e-10 | 1.7508e-10 | 1.601e-10 | 1.5344e-10 | 1.5156e-10 | 1.5266e-10 | 1.5573e-10 | 1.602e-10 | 2.354e-10 | 3.2726e-10 | 4.233e-10

## Slide 9: Busses
Bus includes long wire, multiple drivers, multiple loads.
  Loads add significant capacitance to the bus.
Model bus length relative to number of cores .
.

## Slide 10: Example: velocity of data
Ideal case: signals travel at speed of light in a vacuum.
Assume
Distance traveled in one clock cycle:
RC transmission line gives much slower propagation.
Assume wire width , length .
Distance traveled in one clock cycle:

## Slide 11: Example: planet-scale computer
Mean radius | 
Volume | 
Total area | 
Land area | 
Mean radius | 
Volume | 
Total area | 
Land area | 
NASA

## Slide 12: Planet-scale computer analysis
Assume Earth-sized planet is filled with computers to a depth of 10 km.
  Machine room volume .
Computer size .
Data center holds computers.
At 100 W/computer, planet-scale system consumes .
1 GB RAM/computer gives bytes.
1 TB mass storage gives bytes of disk storage.
  Equivalent to HD movies.

## Slide 13: Performance
Earth-scale computer:
  Delay between poles at speed of light is .
Intel 4004 (1971):
  Clock period .

## Slide 14: Use cases for planet-scale computer
Planetary-scale delay is less important if workload is many small, loosely-coupled jobs.
Amdahl’s Law:
  Speedup depends on proportion of job that is parallelizable vs. serial.

## Slide 15: Clocking
Clock must be distributed everywhere at once with minimum skew.
Clock rise, fall times also reduce useful clock period.
  Rise and fall times may be 10% of clock period.
Clock distribution may consume 30% of chip power.

## Slide 16: Example: capacitive loads on clock network
Assume:
  10,000 registers;
  .
Assume clock signal swing of 1V.
  For 1 ps rise time,

## Slide 17: Clock distribution networks
Topology of clock wiring is important to delay.
  Linear clock network is worst case.
Tree is simple to analyze.
  H-tree is a regular tree.
  Unbalanced trees are used when register density varies.
Some networks are meshes.
  Harder to analyze, better performance.

## Slide 18: Buffered clock tree
As with global wiring, buffers help to improve clock delay.
Simple case: buffer at each tree node, branching factor of .
Similar to driving large loads but load is distributed over the leaves.

## Slide 19: Clock domains
Large chips cannot be clocked at high speeds.
  Clock signal requires more than one clock period to cross the chip.
Chip can be divided into clock domains.
  Synchronizers required between domains.
Globally asynchronous locally synchronous (GALS).

## Slide 20: Clock generation
High speed clocks cannot be easily injected onto the chip.
Generate off-chip clock at lower frequency, use clock multiplier circuit to increase frequency.
Crystal uses piezoelectric effect.
  Pressure on crystal induces charge.
Pierce oscillator uses crystal R, L to generate clock signal.
crystal equivalent
crystal oscillator