## Slide 1: System Power
The Physics of Computing
Chapter 5: Processors and Systems

## Slide 2: Topics
Data center power.
Mobile system power.

## Slide 3: Transaction volumes
Wal-Mart averaged $1.3 billion in sales per day in 2015.
Amazon sales totaled $107 billion in 2015.
Delta operated 15,000 flights per day in 2016.
  180 million passengers per year.

## Slide 4: Computer system energy consumption
CPU dominates but other components are significant.
Component | Power (W)
CPU | 100-200
Memory | 25
Disk | 10-15
Board | 40-50
Power/fans | 30-40
Total | 200-350

## Slide 5: Current requirements
Intel Xeon E7-8800:
  Operating voltage of 1.3V
Craftsman Arc Welder:
  Operating voltage of 120V.
Welder draws higher power but CPU has impressively high current density.

## Slide 6: Data center power consumption
Large data center:
  Over 10,000 servers.
  Consumes > 10 MW power, 100X more than a typical office building.
  Total cost of electricity is 10% of total cost of ownership of the data center.

## Slide 7: Example: server power density
Typical rack holds 50 servers.
Assume 50W per server:
  Rack consumes 2.5 kW.
  Monthly power consumption 1,800 kW-hours per month.
Compare to home utilization:
  Georgia (US) 1,152 kWh per month.
  Colorado (US) 687 kWh per month.

## Slide 8: Example: data center power distribution
Data distribution system for small data center.
Design goals:
  No single point of failure.
  Use single-phase electrical power.
Three power sources: utility, two backup generators.
  Transfer switch manages switchovers.
UPSs interface external power to the server system.
  Each UPS has 16 kVA capacity.
Each rack gets redundant power from both UPSs.
Power delivery unit (PDU) manages power from UPSs to devices on the rack.
Critical devices have dual power supplies, non-critical devices have only one.

## Slide 9
Gen 1
Gen 2
xfer switch
utility
UPS A
UPS B
PDU A leg 1
PDU A leg 2
PDU B leg 1
PDU B leg 2
PDU switch A1, B1
PDU switch A2, B2
singlet power supply
dual power supply
rack

## Slide 10: Mobile systems
Typically battery-operated.
Battery characteristics must be taken into account in system design.

## Slide 11: Example: cell phone power requirements
TI OMAP 4460 processor:
  Two 32-bit CPUs, special-purpose processors, I/O devices, on-board memory.
  Power supply voltage of 1.5V, 2.3A current.
TFT display 240 x 320 pixels consumes 0.5 W.

## Slide 12: Example: Cell phone power utilization
Sample cell phone power consumption:
  Total power.
  Subsystem and application power.
Screen is typically largest power draw on cell phone.

## Slide 13: Batteries and cells
A battery is a connected set of electrochemical cells.
Cell terminals:
  Negative terminal is anode.
  Positive terminal is cathode.
Electrolyte stores energy in chemical form.
anode
-
cathode
+
electrolyte

## Slide 14: Battery characteristics
Nominal voltage and current.
Total energy.
Energy density.
Shelf life.
Number of charging cycles.
Internal resistance.
Performance vs. temperature.
Different applications may require very different combinations of battery characteristics.

## Slide 15: Battery chemistries
Chemistry | Nominal voltage (V) | Capacity (A-hr) | Usable cycles | Watt hr/kg
Lithium ion | 3.6 | 0.75 | 600 | 135
NiCD | 1.2 | 1 | 1000 | 46
Alkaline | 1 | 1.6 | 100 | 80

## Slide 16: Energy densities
material | specific energy (megajoules/kg)
U-235 | 1.5 x 109
hydrogen | 123
gasoline | 46
TNT | 4.6
lithium battery | 1.8
lithium-ion battery | 0.72
!!!

## Slide 17: Dischage characteristics
voltage
time
Modern batteries have fairly flat voltage characteristics.
  Voltage may fall off slowly as battery discharges.
At end of charge, voltage drops off steeply with use.

## Slide 18: Example: Smart Battery System (SBS)
SBS specifies interfaces and features for smart batteries.
System management bus based on I2C.
Provides information on battery voltage, current, temperature.
Smart battery charger manages charging.

## Slide 19
a node
c a t h o d e
x
Species
concentration

## Slide 20: Peukert effect
a node
c a t h o d e
x
species
concentration
GAME
OVER
Battery capacity depends on its discharge rate:
Electrolyte species are depleted fastest at cathode end.
When species concentration drops below certain level, battery stops operating.
Pausing battery use allows species to diffuse and even out concentration across battery.

## Slide 21: Power management
Dynamic voltage and frequency scaling (DVFS) most effective in low-leakage system.
  Identify slowest allowable execution rate.
  Reduce power supply voltage, clock frequency to achieve that rate.
Race-to-dark (RTD) used in high-leakage systems.
  Run as fast as possible, then go to idle.

## Slide 22: DVFS vs. RTD
Clock period , power supply voltage
Execution time for cycle job. Job deadline .
Power supply voltage vs. gate delay and clock period .
DVFS energy:
  Minimized at .
RTD energy:
  Minimized at fastest clock speed.