## Slide 1: Input and output
The Physics of Computing
Chapter 6: Input and Output

## Slide 2: Topics
Displays
Image sensors
Touch sensors
Microphones
Accelerometers and inertial sensors

## Slide 3: LEDs
Semiconductor diode optimized for photon emission.
Electron-hole recombination causes release of energy.
  Released as photon under proper energies and band gaps.
Junction promotes electron-hole recombination.
Quantum efficiency : proportion of photon-creating recombination events.
  Decreases with temperature.

## Slide 4: LED color
Human eye sensitive in range .
Energies in range produce visible light.
Material properties determine color of emitted photons.
  Red and green LEDs are built from .
  Blue LEDs require specialized materials.

## Slide 5: Liquid crystal display
Liquid crystals can be oriented by an electric field.
Modern LCDs are light valves---control the transmission of light through the display.
Twisted nematic liquid crystal twists with electric field.
nematic
isotropic
E

## Slide 6: LCD display architecture
Display is backlit.
Isotropic crystals block the light.
Nematic crystals align with polarizer, allow light through.
LCD contrast is limited by transmission.
polarizer
liquid crystals
backlight
light
E field

## Slide 7: Pixel control
Early displays used passive matrix with capacitor to hold pixel value.
  Addressed using row and column of capacitor.
Modern displays use active matrix with access transistor and capacitor.
passive matrix
active matrix

## Slide 8: Organic LEDs
Organic materials can act as semiconductors.
Amorphous organic LEDs (AMOLEDs) are very bright but deteriorate over time.
Pixel circuit must compensate for time-varying LED characteristics.

## Slide 9: Digital light processor
Hinged mirror is controlled electrostatically.
  Mirror either reflects out of projector or inside projector.
Brightness is controlled by frequency of flips.
Truly digital output---light pulses are integrated in the visual system.
dark
bright

## Slide 10: Electronic ink
Pixel represented by bi-tone electric ball.
Ball is electrostatically flipped between black and white.
Reflective display---very high contrast in bright light.
Gray scale and color are difficult.

## Slide 11: Inkjet
MEMS nozzle is used to spit out ink.
  Microbubbles caused by superheating ink.
  Bubble size is highly precise.
Nozzle is moved by printhead to scan page.
Wolf

## Slide 12: Image sensors
Absorbing a photon creates an electron-hole pair.
Responsiveness to light determined by cutoff wavelength:
Junction promotes capture of photons and electron-hole pair creation.
  Photodiode uses single junction.
  Phototransistor uses one pn junction of transistor. Transistor amplifies current.
Junctions are not equally sensitive to all frequencies.

## Slide 13: Pixel architecture
Photodetector and pixel circuit reside in substrate.
Lens focuses light onto photodetector to maximize efficiency.
Filter allows selective color sensing.
substrate
photodetector
pixel circuit
filter
lens

## Slide 14: Bayer pattern
Bayer pattern captures colors in regular 2 X 2 pattern.
  Two greens because a eye is most sensitive to green.
Other colors can be interpolated from nearby pixels.
Bayer pattern

## Slide 15: Image sensor architectures
Two approaches to reading out pixels.
  CCD is highly efficient.
  CMOS active pixel sensor (APS) is more compatible with CMOS processes.
    Photodetectors benefit from somewhat different processing.

## Slide 16: CCD
MOS capacitors form a bucket brigade.
Electrode voltages are used to manipulate band structures.
Proper coordination of electrode phases moves all pixels as an analog shift register.
E1
E2
charge

## Slide 17: CMOS active pixel sensor
Sensor architecture similar to memory.
  Row and column address lines.
Analog shift register along bottom shifts out pixels in a row.
pixel
pixel
pixel
…
Analog register
pixel
pixel
pixel
…
Analog register
pixel
pixel
pixel
…
Analog register
…
…
A/D
convert
word0
word1
wordh-1
bit0
bit1
bitw-1

## Slide 18: APS pixel
Photogate captures electrons.
Pixel value is stored on transistor gate capacitance.
Row select sends value to row line.
Reset signal resets the pixel value for next image.
+
p
n
n
p+
pinned diode
photogate
reset
row select
transfer gate
row

## Slide 19: Theremin
Theremin was early electronic musical instrument.
  Capacitive sensor, does not require touch.
Resonant circuit frequency:
Body capacitance is added to circuit:
L1
antenna
C2
C1
Vout
+
-
Cant

## Slide 20: Resistive touch screen
2D voltmeter:
  Alternates between x and y measurements.
  Touch creates contact between membrane and screen.
  Voltmeter measures voltage drop from edge of screen to touch point.
screen
+
y+
x+

## Slide 21: Microphones
Can be based on resistance, capacitance, or inductance.
Edison carbon microphone was widely used for a century.
  Contact is made to a carbon button.
  Sound pressure on diaphragm causes varying pressure on contact, varying resistance.
Electret microphone is modern inexpensive microphone.
  Ferroelectric material that is permanently charged.
  Sound moves capacitor plate.

## Slide 22: Accelerometer
MEMS inertial sensor based on Hooke’s Law .
Motion moves plate of measurement capacitor:
proof
mass
spring
VS
VB
+
-
+
-
measurement
capacitor
x