## Slide 1: Internet-of-Things (IoT) Systems Chapter 1: The IoT Landscape
Dimitrios Serpanos
Marilyn Wolf

## Slide 2: Outline
What is IoT?
Applications
Architectures
Wireless networks
Devices
Security and privacy
Event-driven systems

## Slide 3: What is IoT?
IoT system vs. the Internet-of-Things:
Many IoT systems operate primarily within their own boundaries.
Many IoT devices do not use the IoT protocol.
IoT system:
Built to provide a set of applications.
Sensor network, perhaps some actuation.
Wireless networks of embedded computing devices.
Network configuration is long-lived and evolving.

## Slide 4: IoT system enablers
VLSI technology:
  Low-cost digital and analog.
  Low power.
  Simple devices do not need to rely on state-of-the-art processes.
MEMS (microelectromechanical) sensors.

## Slide 5: IoT applications
Industrial systems:
  Monitor industrial processes and product quality.
  Monitor state of equipment.
Smart buildings:
  State of building.
  Activity tracking.
  Control of lighting, heating/ventilation/air conditioning.
  Structural health.
Smart communities:
  Pedestrian and vehicular traffic.
Networked sensors and devices in vehicles.
Medical systems:
  Implanted devices.
  External patient monitoring.
  Emergency vehicles, hospitals, medical offices.

## Slide 6: IoT application requirements
Event latency:
  Time to read an event.
Event throughput:
  Number of events per second.
Event loss rate:
  Related to buffer capacity.
Service latency and throughput:
  Notifications and actions caused by an event.
Reliability and availability.
Service lifetime.

## Slide 7: IoT architectures
Event-driven:
  Aperiodic changes in system state.
Transmission of data consumes a great deal of power.
  Periodic transmission of samples consumes too much power.
Local processing of events reduces power consumption.
Non-local computing:
  Fog computing is near edge of network.
  Cloud computing is at center of network.
Fog and cloud computing can be used to combine sensors to perform more sophisticated analysis.

## Slide 8: Wireless networks
Wireless networks reduce cost of IoT devices.
Wireless consumes significant amount of power.
  Wireless network should be optimized for event-driven operation.
Not all devices at the edge use the Internet Protocol (IP).
IoT networks typically run by non-experts.
  Should be easy to install, largely self-managing.

## Slide 9: IoT devices
VLSI IoT devices operate at the edge of the network.
Small chips provide low manufacturing cost.
  A few mm2 can be enough for useful sensing, memory, computation, and communication.

## Slide 10: Security and privacy
IoT systems present security vulnerabilities:
  Devices can be physically accessed by attackers.
Many IoT devices are poorly designed for security:
  Inadequate hardware security support.
  Poorly designed, vulnerable software.
  Default passwords and other sloppy deployment.
Long installed life of IoT devices increases risk of insecure devices.
Dyn attack of 2016 illustrates

## Slide 11: Event-driven systems
Event (time/value pair) is a fundamental datatype.
  Time is a first-class element.
  Physical behavior is expressed as event sets.
Many traditional Internet systems are designed for transactions.