## Slide 1: Internet-of-Things (IoT) Systems Chapter 2: IoT System Architectures
Dimitrios Serpanos
Marilyn Wolf

## Slide 2: Outline
IoT system organization and terminology.
Application protocol concepts.
IoT-oriented protocols.
Databases.
Time bases.
Security.

## Slide 3: IoT system terminology
Plant or environment:
  Physical system with which IoT computational system interacts.
Devices:
  Leaf devices on the network.
Hub:
  First-level connectivity device.
Fog processor:
  Local computational node.
Cloud server:
  Remote computational system.
Database:
  Stores IoT system data.

## Slide 4: Application protocol concepts
IoT systems require multi-hop service for end-to-end communication, specialized services, efficient operation.
IoT service protocols can provide high-level models for IoT operation.
Many IoT protocols are event-oriented.

## Slide 5: Request/response design pattern
The Internet HTTP protocol, used for Web service, uses a request/response design pattern.
  Client issues a request for a hypertext object.
  Server replies with object.

## Slide 6: Publish/subscribe design pattern
Publish/subscribe requires less coupling between client and server.
Server is publisher:
  Classifies messages into categories or topics.
Clients subscribe to message categories.
Brokers mediate message delivery.
  Bridge allows indirect publication of messages.

## Slide 7: Publish/subscribe servcies
DDS (Data Distribution Service):
  Pub/sub software architecture.
  DDS domain maintains a logical global data space.
  Publishers can specify quality-of-service parameters.
RTPS (Real-Time Publish-Subscribe) Protocol defines communication with DDS and other pub/sub systems.
  Provides QoS properties, fault tolerance, and type-safety.
MQTT designed for low overhead pub/sub with QoS parameters.
Esposito et al. scalable architecture for time-sensitive publish/subscribe system.
  Network layer for domains, nodes and clusters, coordinator layer.
Kang et al. used state space estimators at publisher and subscriber to maintain sensor value continuity over QoS variations.
Choi et al. combined DDS and OpenFlow for QoS.
Google Cloud Pub/Sub.

## Slide 8: IoT communication protocols
Some wireless protocols are tied to a particular physical layer, others can be used over more than one physical layer.

## Slide 9: Zigbee
Tied to 802.15.4 PHY and MAC standards.
Mesh network.
Designed for low-power operation.
NWK layer provides data and management services.
APL layer provides application support.
Two types of security: centralized and distributed.

## Slide 10: Bluetooth Low Energy (BLE)
BLE is part of Bluetooth standard designed for coin cell battery-style operation.
Device can operate as receiver, transmitter, or both.
BLE is stateless; classic Bluetooth is stateful.
Link layer provides advertising service.

## Slide 11: LoRa
Designed for wide-area IoT applications.
  Base station may cover hundreds of square kilometers.
Gateways communicate with end devices.
Data rates range over 0.3-50 kbps.

## Slide 12: Web-style protocols
XMPP streaming XML protocol.
  Provides security, authentication, availability information, client rosters.
  XMPP-IoT designed for IoT.
REST provides stateless HTTP transfers.
  COAP is REST-based protocol for IoT.
Amazon Web Services (AWS) provides managed cloud service.
  IoT devices known as things.
  Cloud model of a thing is a thing shadow.
  Rule engine transforms messages based on rules and routes to AWS services.
  Message broker based on MQTT.
Microsoft Azure provides middleware Service Fabric and microservices.

## Slide 13: Databases for IoT
Used for both short-term and long-term storage.
Unstructured databases (noSQL):
  Often structured as key-value pairs.
  Lack of schema simplifies deployment but complicates maintenance.
Time-series data may require specialized handling.
Dynamic time warping (DTW) can be used to compare time-series data.

## Slide 14: Time Bases
Time base provides a time reference for devices and the system.
Many algorithms and applications require a global notion of time.
  Allows comparison of events across nodes.
Network Time Protocol (RFC1305) provides distributed time synchronization on Internet.

## Slide 15: Security
Security is a system property.
  System is only as secure as its weakest component.
Security features can be provided at several layers: devices, physical networks, middleware.
Lightweight block cyphers: SIMON, SPECK.
Several network provide security services: BLE, Zigbee, LoRA.
MQTT may be operated with several different security standards.
  See MQTT and the NIST Framework for Improving Critical Infrastructure Cybersecurity.