## Slide 1: Internet-of-Things (IoT) Systems Chapter 3: IoT Devices
Dimitrios Serpanos
Marilyn Wolf

## Slide 2: Outline
IoT device design space.
Cost of ownership and power consumption.
Cost per transistor and chip size.
Duty cycle and power consumption.
Platform design.

## Slide 3: IoT design space
IoT requires extremely low power levels.
IoT nodes often operate at low rates or intermittently.
IoT node typically includes CPU, memory/storage, communicatin, sensors.
Some IoT devices produced in extremely high volumes.
Total cost of ownership:
  Installation cost dominates manufacturing cost.
Trillion sensor world:
  5.4 million 200mm wafers per month in 2018.
  Provides 678 billion chips of size .

## Slide 4: Lifetime cost of ownership
Components:
  Silicon.
  Packaging.
  System and assembly.
  Distribution and marketing.
  Installation.
Cost of cable drop in U. S. is approx. $150.
  Eliminating wiring requires both wireless communication and ultra low power operation.
Replaceable batteries entail maintenance cost.
  If node lasts longer than batteries, maintenance operation must replace batteries.
Energy scavenging or harvesting collects energy from environment.

## Slide 5: Energy scavenging
Sources (Paradiso/Starner):
  Radio frequency energy.
  Ambient light.
  Thermoelectric.
  Heel strikes.
Efficiency (Sudevalayam/Kulkarni):
  Daylight .
  Wind .
  Footfalls
Power conversion and management (Romani et al.):
  Transducer extracts power with efficiency .
  Efficiency limited by power control circuitry, storage element leakage, monitor circuits.

## Slide 6: Cost per transistor and chip size
Chip cost depends on both chip area and wafer processing cost.
Advanced technologies require more steps, higher wafer processing cost.
  More manufacturing steps.
  Double/triple/quadruple patterning.
Cost per transistor vs. wafer cost:

## Slide 7: Low-cost VLSI processes
High wafer processing costs can negate benefits of die shrink.
Many observers believe that 28 nm manufacturing node provides historically lowest cost-per-transistor.
Today’s small chips provide useful functionality:
  Intel 8088 contained 4,000 transistors running at 4.77 MHz.
Low-cost packaging is important to total manufacturing cost.
DARPA SHIELD:
  CMOS module on 14 nm finFET technology.
  Includes digital CPU, communication, one-time programmable memory, physically-unclonable function, analog/digital converter, power conversion and management.
  RF pickup coil, thin-film temperature sensor.

## Slide 8: Duty cycle and power consumption
Duty cycle is percentage of time for which device is on:
Power consumption is lower when device is not operating (may be limited by leakage).
Average power consumption:
Duty cycle as a function of power:

## Slide 9: IoT device power consumption
Communication consumes large fraction of power in many devices.
Power to transmit one bit is limiting metric for communication power.
Dementyev et al. measured power consumption to determine optimal period for IoT protocols:
  14.3 sec for Zigbee.
  10.0 sec for BLE.

## Slide 10: Platform design
Mobile devices operate continuously for extended periods.
IoT devices operate intermittently.
  Device often needs to save internal state.
Persistent-state devices promise improved performance and enhanced capabilities.