## Slide 1: Internet-of-Things (IoT) Systems Chapter 6: Security and Safety
Dimitrios Serpanos
Marilyn Wolf

## Slide 2: Outline
Security and safety in control.
Systems security.
Network security.
Generic application security.
Application process security and safety.
Reliable-and-secure-by-design IoT applications.
Run-time monitoring.
ARMET.
Privacy and dependability.

## Slide 3: IoT system models
IoT system model:
  Sense device state.
  Perform control/decision tasks.
  Command actuators.
Control Center
(C)
Device
(D)
Sensors
Actuators
Data acquisition
Control commands
Control
actions
Measurements

## Slide 4: SCADA
Supervisory control and data acquisition (SCADA) is hierarchical control.
  Network connects multiple PLCs.
  SCADA coordinates devices.
Supervisory Control
and Data Acquisition
(SCADA)
PLC
PLC
PLC
Network
Network
Pump
Valve

## Slide 5: Safety and security requirements
Safety properties:
  Maintain well-defined state that corresponds to safe operation.
Safety typically expressed as requirements on control loop.
Security is related to safety:
  Data integrity.
Security:
  Confidentiality.
  Integrity.
  Authentication.
  Access control.
  Non-repudiation.
  Dependability.
  Safety.
  Privacy.

## Slide 6: Security property layers
Security and dependability are mechanisms.
Privacy and safety are system properties.
  Requirements for processes, applications, services.
Privacy and safety depend on security.
Threats:
  Computational.
  Data.
Privacy
Safety
Security
Dependability
Layer 1: Mechanisms
Layer 2: Properties

## Slide 7: Systems security
System architecture:
  Processor, memory, I/O, power.
Components must be protected.
Overall system must be protected.
Anti-tamper prevents physical interference with device.
Side-channel attacks infer computer operation from power, etc.
Processor
Memory
I/O
Power (Battery)
Bus

## Slide 8: Network security
Secure communication requires encryption, authorization.
Traditional encryption algorithms are too resource-intensive for embedded systems.
New lightweight encryption algorithms are designed for embedded systems.
Crypto keys must be managed to avoid disclosure.
Network communications must be authorized.
  Ad-hoc networks require node protection.
  Centralized networks can use network-level protection.
Distributed denial-of-service (DDoS) overload CPU, memory, network resources.
  Mirai botnet attack used IoT to attack Internet services.

## Slide 9: Generic application security
Generic application security:
  DDoS defense.
  Secure upgrading.
Upgrading is a challenge:
  Code can be attacked during transport.
  Upgrades may be limited on some critical devices.
  Access control mechanisms protect less-critical devices.

## Slide 10: Application process security and safety
Safety properties are application-dependent.
Security is a prerequisite for safety.
Dual approach:
  Verification at design time.
  Monitoring at run time.

## Slide 11: Reliable-and-secure-by-design IoT applications
Ur/Web for secure Web apps:
  Ensures app does not have code vulnerabilities.
  Ensures app will not crash.
Based on enriched type system.
ROSCoq framework:
  Uses Coq proof assistant to model robot cyber/physical resources.
  Uses extended logic of events to prove properties.
VeriDrone ensures security at multiple independent levels of abstraction.

## Slide 12: Run-time monitoring
Monitoring methods:
  Behavior description as profile-based or model-based.
  Behavior comparison as match to bad behavior or deviation from good behavior.
Class 1, 3 uses machine learning.
  Learning good behavior more robust than learning attacks.
Class 2, 4 systems used in highly secure environments.
Class 1
Class 2
Class 3
Class 4
Behavioral description
Profile based
Model based
Behavioral
comparison
Bad behavior
matching
Good behavior
deviation

## Slide 13: ARMET
Application
specification
Application
code
Run-time security monitor
(RSM)
Diagnosis
Recovery
Adaptive method selection
Trust model
Backup

## Slide 14: ARMET methodology
Create secure-by-design systems.
  Executable specifications.
Monitor systems at run time to detect attacks and failures.
  First formally-proven sound/complete run-time security monitor (RSM).
  Observes application behavior, executes specification to identify good behavior, some known bad behavior.
  Identify deviations from good behavior.
During attack/failure, make use of recovery plans.
  Diagnosis makes use of available information.

## Slide 15: ARMET example
Water management system:
  Pour water into or drain water from tank.
Actions: fill, drain, nothing.
wh
in_pump
out_pump
h

## Slide 16: Water tank executable specification
«Enumeration» Action
FILL DRAIN NOTHING
«StereoType» WaterTankSpec
water_level : Integer :=0 SENSOR_ACCURACY : Real := 0.01 FILL_RATE : Integer := 1 DRAIN_RATE : Integer := 1 TANK_MAX : Integer := 10
+ readValue (reading : Integer) : void + doAction (water_level : Integer ) : Action context WaterTankSpec ::readValue(reading : Integer) + pre: reading – self_water > SENSOR_ACCURACY + post: self_water = reading context WaterTankSpec :: doAction(water_level : Integer) : Action + pre: forall( a : Action ¦ (a = FILL implies water_level + FILL_RATE <= TANK_MAX) and (a = DRAIN implies water_level - DRAIN_RATE >= 0)) + post: result = FILL implies self.water_level= old(self.water_level)+ FILL_RATE and result = DRAIN implies self.water_level= old(self.water_level) - DRAIN_RATE

## Slide 17: Privacy and dependability
Privacy protection may be legally required in some applications.
  Health, smart grids, home, etc.
Privacy protections can be expressed as pre-conditions, post-conditions, or invariants.