## Slide 1: Internet-of-Things (IoT) Systems Chapter 7: Security Testing IoT Systems
Dimitrios Serpanos
Marilyn Wolf

## Slide 2: Outline
IoT security testing.
Fuzz testing.
White-box fuzzing.
Black-box fuzzing.
Fuzzing industrial control systems.
Fuzzing Modbus.

## Slide 3: Verification and validation for IoT
IoT verification and validation (V&V) often limited:
  Complexity grows exponentially with system size.
  Long supply chains limit comprehensive models.
Communication systems are difficult to test:
  Different vendors provide different implementations with different implementation-dependent parameters.

## Slide 4: Fuzz testing for security
Generates representative inputs.
Applies tests, observes behavior of system under test (SUT).
Faults identified by system crash.
Advantages:
  Does not require source code.
  Independent of code size.
  Faults associated with user input.
Disadvantages:
  Large input space.
  Must identify representative input values.
System-Under-Test
(SUT)
-Tester/
Fuzzer
Fuzzed inputs
Outputs

## Slide 5: White-box fuzzing
Based on availability of source code.
Symbolic execution:
  Replaces symbolic values in source code or program flow.
  Can combine symbolic, concrete execution.
Taint analysis:
  Tracing tainted values.
  Fuzz inputs to attack points.

## Slide 6: Black-box fuzzing
No information about system under test.
Methods to generate input:
  Data generation.
  Data mutation.
Coupled with techniques to choose seed values:
  Random.
  Block-based.
  Grammar-based.
  Heuristic-based.

## Slide 7: Fuzz testing for industrial control
Supported by many commercial tools.
Black-box mutation fuzzing used for SCADA.

## Slide 8: Fuzzing Modbus
Application protocol for ICS.
  (a), (b) interface directly to layer 1 and layer 2 protocols.
  © itnerfaces to TCP.
Client/server or master/slave protocol between control center and field devices (SCADA or PLC).
Modbus Application
Protocol
Serial Master/Slave
Physical Protocol
(RS-232/RS-485)
Modbus Application
Protocol
HDLC
Physical Protocol
(RS-485)
TCP
IP
Ethernet Data Link and
Physical Protocols
Modbus Messaging
(Mapping) on TCP
Modbus Application
Protocol
(a)
(b)
(c)

## Slide 9: Modbus application packet
Requests send function code to execute and related data.
Client responds with function code executed and related data.
Three classes of function codes:
  Public.
  User-defined.
  Reserved.
Application packets are encapsulated in lower-layer protocol packets.
Function code
(FC)
Data

## Slide 10: Modbus TCP fuzzer
MTF tool:
  Automated, provides good coverage, does not require physical access to system-under-test.
Three phases:
  Reconnaissance.
  Attack.
  Failure detection.
Reconnaissance identifies operation performed by system and important parameters.
  For example, ask device for identification information.
  Identify boundary memory addresses for each type of memory.
Legitimate packets are generated and fuzzed.
Results of test application are recorded, errors identified.