## Slide 1: Smart Camera Design Chapter 2: Light, Optics, and Imaging
Marilyn Wolf

## Slide 2: Outline
Image formation
The human visual system.
Color science.
Lenses.
Geometry and the camera model.
Image display.
Practical image capture.

## Slide 3: Light and images
Throwing an image onto a surface requires control of light.
Light is reflected from the subject to the image surface.
Controlling light:
  Pinhole.
  Lens.
Position and orientation of lens and image surface determine point of view (POV).

## Slide 4: Pinhole image formation
A pinhole is sufficient to control the light reaching the image surface.
Size of pinhole determines circle of confusion.
  Smaller pinholes give smaller circle of confusion, sharper image.
Size of pinhole determines brightness of image.
  Smaller pinhole gives dimmer image.

## Slide 5: Illumination to luminance
Subjects are illuminated by both direct and indirect light.
The subject reflects the light.
Light captured at the image surface produces a luminance value at each point in the image.

## Slide 6: Spatial frequency
Fourier introduced frequency analysis.
  Complex waveforms can be expressed as a weighted sum of sinusoids.
We can use sinusoids over the image surface to analyze the image.
  Spatial frequency describes distance over which sinusoid repeats itself.

## Slide 7: Color
Visual system responds to visible spectrum of light.
Frequency of light is perceived as color.
Other frequency bands behave similarly to visible light:
  Ultraviolet.
  Infrared (near, far).

## Slide 8: The Golden Hour
Sunlight is composed of light of many colors.
The atmosphere filters light.
Sunlight passes through the thickest slice of atmosphere at sunrise and sunset.
  Sunlight is most heavily filtered.
Golden hour:
  Sun’s illumination includes greater portion of yellow, gold.
  Visual system perceives greatest contrast over orange/teal.

## Slide 9: The physics of light
Light is a form of electromagnetic radiation.
  Propages as waves.
Wavelength and frequency of light are related:
Visible spectrum lies over wavelengths.

## Slide 10: Sensitivity of eye vs. wavelength
Human eye is not equally sensitive to all colors/wavelengths.
CIE describes sensitivity of eye under daylight.
  Peaks at .

## Slide 11: Intensity of light
Basic intensity is a physical measurement.
Luminous intensity is weighted to the sensitivity of the eye.
Candela () approximates illumination of one candle:
  Light at .
  Given power in Watts.
  Given solid angle.
Nits: candela per square meter
Lux () measures intensity falling on a surface.
  Depends on angle at which light strikes surface.
  Also depends on intensity and distance from source.
  Highest when source is normal to surface.
  Falls off as .
Lumen () measures total light emitted from source in all directions.
  incandescent bulb puts out about .

## Slide 12: Color temperature
Color of light can be described using thermal emissions.
Black body reflects no light.
  All light from black body is emissive.
  Wavelength of black body radiation depends on its temperature.
Color temperature measured in Kelvin ().
White light is a mixture of light at several frequencies.
Visual system adjusts for color of light source.

## Slide 13: Fermat’s principle
Light takes the path that requires the shortest time.
  Governs reflection.
Specular reflection:
  Angle of incidence is equal to angle of reflection.
Reflection produced by reflection and reabsorption.
  Ray optics models reflection as a bounce.

## Slide 14: Light and surfaces
Light can be absorbed or reflected by subject.
  Most surfaces combine absorption and reflection.
Absorpton generally depends on frequencies.
Reflection may be specular or diffuse.

## Slide 15: Refraction and diffraction
Refraction allows focusing of light.
Diffraction has practical advantages, causes some limitations in optical systems.
Snell’s Law and refractive index :
Refractive index is a function of wavelength.

## Slide 16: Diffraction
A small aperture acts as a radiator.
Light falling on an image surface from a diffractive forms wavefronts.
Interference among wavefronts causes intensity variation.
Fraunhofer diffraction formula:

## Slide 17: Diffraction grating
A regular pattern of slits forms a diffraction grating.
Huygens-Fresnel principle:
  Intensity at image surface is a superposition of the interference patterns of the slits.
Airy diffraction pattern is produced by diffraction through a circular aperture.

## Slide 18: Polarization
Light waves have an orientation.
Natural lighting includes light from many orientations.
A polarizing filter selects light of certain orientations.
  Reduces glare.
  Darkens sky in color photographs.

## Slide 19: Human visual system
The visual system is more than a camera.
The visual system processes images over many stages:
  Within the eye.
  On the way to the visual cortex.
  Within the visual cortex.

## Slide 20: The human eye
The eye has an aperture (iris) but no shutter.
Lens is focused by flexing its shape.
Eye filled with vitreous humor.
Retina has two types of photoreceptors:
  Cones for color and fine detail.
  Rods for low light levels.
Cones are concentrated near the fovea.

## Slide 21: Visual acuity
Resolution of the visual system.
Visual system can resolve two lines about 1 arc minute apart.
Visual acuity limited primarily by the lens.

## Slide 22: Visual processing
Eye resolves only a small part of the scene at high resolution. The visual system moves the eye to scan the scene and build up a view.
Retina uses lateral inhibition to increase contrast.
Optic chiasm reorganizes neural pathways:
  Left half of both visual fields goes to the right.
Superior colliculus helps to control eye movement.
Lateral geniculate nucleus controls vergence and focus of eyes, analyzes position of major objects.
Visual cortex analyzes the scene:
  Visual field mapped onto cortex.
  Depth roughly corresponds to complexity.

## Slide 23: Visual system response to light
Visual system does not respond proportionately to light intensity.
  Allows visual system to function over a wide range of illumination levels.
Over moderate luminance ranges, visual system responds logarithmically.
  Weber-Fechner Law.
Over large ranges of illumination, power law is more accurate.

## Slide 24: Visual scanning and constancy
The eye constantly moves to scan the scene.
  Iris and retina are adjusted during movement.
Constancy:
  Visual system sees objects with constant properties despite variations in intensity and color temperature, angle of view, etc.
Constancy is a complex phenomenon.
  Ratio of luminances at edges provides cues.
  Anchoring heuristic assigns white and black values at extremes of luminance.
Saliency---some scene characteristics draw more attention than others.
  Edges and detail are usually salient.

## Slide 25: Real and apparent motion
Continuous physical motion of an object is real motion.
Video presents apparent motion.
  Moving image consists of a sequence of still images.
  Beta effect produces continuous motion of a light that alternates between two positions at 10 frames/sec.
  Persistence of vision has been disproven.
Frame rates:
  Cinema is traditionally 24 frames/sec.
  Video is traditionally 30 frames/sec.
  Flicker fusion occurs at 60 frames/sec.
  Gaming and virtual reality may employ higher frame rates.

## Slide 26: Color science
Three types of cones respond to different wavelength bands:
  Red, green, blue.
  Some evidence that some women have a fourth color receptor.
Color depends on the relative stimulation of cones in these three colors.
Eye is most sensitive to green.

## Slide 27: Additive and subtractive color
Additive color models reflected light.
  Primary colors red, green, blue (RGB).
Subtractive color models elimination of some wavelengths.
  Secondary colors yellow, cyan, magenta.
  CYMK: cyan, yellow, magenta, plus black.

## Slide 28: Color combinations
Visual system cannot distinguish all color combinations.
Opponent process theory:
  Processing reduces information for later stages.
Pairs of opposites:
  Green/Red.
  Blue/Yellow.
Opposite processing:
  Can perceive green/blue, blue/red.
  Cannot see green/red or blue/yellow.

## Slide 29: Perceived color
Perceived color depends on:
  Color of illuminating light.
  Reflectance of object.
  Response of visual system.
Color references:
  Munsell Book of Color includes 1600 paint chips with controlled colors.
  Pantone is a widely used color standard.

## Slide 30: Retinex theory
Mondrian:
  Visual target with rectangular shapes of varying size, colors, values.
Visual system:
  Finds ratio of reflectances on two sides of edge.
  Analyzes chains of ratios to compare reflectances.
  Allows for color constancy.

## Slide 31: CIE chromaticity diagram
Mathematical color specification (1931).
Color sample represented by XYZ tristimulus value:
  Light source .
  Spectral reflectance .
  Standard Observer model .
XYZ:
Chromaticity diagram eliminates value, concentrates on hue and saturation.

## Slide 32: Other color models
Just-noticeable-difference (JND) model.
  Original CIE model doesn’t match JND measurements.
  Updated models CIELAB, , CIEDE2000.
HSV color space:
  Hue is color or dominant wavelength.
  Saturation is purity.
  Value or lightness ranges from black to white.
YUV model from analog TV (YCrCb is digital terminology):

## Slide 33: Lenses and ray tracing
Ray tracing models the effect of a lens on light.
Light refracts at each lens surface.

## Slide 34: Focus
Parallel beams converge to a focal point.
Set of focal points form a focal plane.
Focal length of lens :
  Subject at infinity.
  Distance from lens to focal plane.
Focal point of an object varies with its distance to the lens.
Lens is moved mechanically to select a focal plane for the image surface.

## Slide 35: Circle of confusion and depth-of-field
Rays form circle of confusion in both directions from the focal plane.
Acceptable circle of confusion is a design parameter.
Depth-of-field:
  Range of planes with acceptable circle of confusion for a subject.
Bokeh: rendering of highly defocused elements.
  Influenced by lens abberations.
  Described by lens impulse response.

## Slide 36: Focal length and image circle
Focal length determines size of image circle:
  Longer lens produces larger image circle.
For a given imager size:
  Longer focal length gives smaller angle of view.
  Shorter focal length gives wider angle of view.

## Slide 37: Focal length and image surface
For a given focal length, different image surface sizes capture different portions of the image circle and field-of-view.
  Smaller image surface size captures a narrower field-of-view.
  Larger image surface captures a wider field-of-view.
Normal lens approximates field-of-view of human eye.
  is normal for full frame, image surface.

## Slide 38: Lenses
A lens is a single element.
Spherical lenses are easiest to analyze.
  Modern lens systems include aspherical elements to improve lens system performance.

## Slide 39: Lensmaker’s formula
  closest to light source.
  furthest from light source.
  Diopter is reciprocal of focal length.
Refractive index .
Lens thickness .
Single thin lens:
Series of lenses in contact:
Two lenses separated by distance :
Subject at finite distance:

## Slide 40: Lens characteristics
Nodal point:
  Point through which rays travel such that entry angle equals exit angle.
  Forward and backward nodal points.
Hyperfocal distance:
  Object from hyperfocal distance to infinity will be in focus.
  , circle of confusion diameter c.
For subject distance , region of acceptable sharpness:

## Slide 41: Iris
Iris is built into lens to control aperture.
Vanes allow diameter to vary while maintaining approximate circular shape.
  Number of vanes contributes to bokeh.
Lens is characterized by its maximum aperture, defined relative to focal length, e. g. .

## Slide 42: Real and virtual images
Light impinges on a real image at the image plane.
A virtual image appears at a spot through which rays do not travel.
Examples:
  Magnifying lenses.
  Mirrors.

## Slide 43: Lens design
Lens systems are engineered to meet design criteria:
  Focal length.
  Maximum aperture.
  Optical quality.
  Size and weight.
  Cost.

## Slide 44: Abberations
Spherical aberrations.
Coma.
Astigmatism.
Oblique spherical aberrations.
Distortion.
Chromatic aberrations.

## Slide 45: Spherical aberration and coma
spherical abberation
coma

## Slide 46: Astigmatism and barrel/pincushion
astigmatism
barrel and pincushion

## Slide 47: Chromatic abberations
Lens behavior depends on wavelength.
  Refraction depends on wavelength.
Lateral chromatic abberations cause wavelengths to focus at different points on image plane.
Longitudinal chromatic abberations cause wavelengths to focus at different planes.
Combines lens elements of different materials to reduce chromatic abberations.
  Achromatic lens.
Relative dispersions of lens elements:
Element focal lengths:

## Slide 48: Flare
Flare caused by reflections internal to lens.
Coated lens elements reduces flare.
North Carolina

## Slide 49: Telephoto and zoom
A telephoto lens has a back focus point shorter than lens’s focal length.
  Used generically for long focal length.
Zoom lens can range through focal lengths.
  Harder to correct for abberations over zoom range.
Prime lens: fixed focal length.

## Slide 50: Anamorphic lenses
Anamorphic lenses used in cinema for widescreen.
Anamorphic element is not spherical:
  Squeezes lens in one dimension.
Anamorphic element is used during display to re-establish image.

## Slide 51: Lens system design
Lens designers use multiple elements to improve image quality.
Petzval field curvature:
  Flat object produces curved-focus image.
Petzval sum for set of lenses:
Cooke triplet has Petzval sum of 1, giving flat field of focus.

## Slide 52: Panoramas
Panoramas can be captured in several ways:
  Single, fixed lens.
  Single, moving lens.
  Stitched images.
Mapping of image onto the image surface determines how objects are represented in the image.

## Slide 53: Cropped and scanned panoramas
cropped
scanned

## Slide 54: Fisheye panorama

## Slide 55: Cylindrical and anamorphic
cylindrical
anamorphic

## Slide 56: Stitched panorama
Glacier National Park

## Slide 57: Lens assessment
Resolution: ability to distinguish fine detail.
Acutance: perceptual sense of sharpness.

## Slide 58: Rayleigh’s criterion
Minimum resolvable distance between two slits:
  Peak of one slit coincides with first minimum of second slit.
Suggests using line pairs as a measure of resolution.
Air Force Resolution Test Chart widely used for resolution tests.
IEEE resolution chart developed for analog television.

## Slide 59: Intensity modulation

## Slide 60: Modulation transfer function (MTF)
Measure lens response to a target with white and black bars.
Peak/trough ratio describes sharpness of bar images.
  High MTF corresponds to high sharpness.

## Slide 61: Modulation and spatial frequency

## Slide 62: Camera model
Ray tracing is too complex for some applications.
Camera model is purely geometric.
  Describes relationships between the scene and the model.
  Abstract, simplified model of camera optics.

## Slide 63: Projective geometry
2D image point:
3D Euclidean space point:
Homogeneous coordinates:
  4 dimensions for 3D.
  Allows for perspective transformations.
3D homogeneous points:
  represents 3D point
  3D point corresponds to line in 4D space.
2D homogeneous points:

## Slide 64: Transformation matrix
Translation in :
  Upper-left matrix performs linear transformation.
  Rightmost top three values perform perspective.
  Bottommost left three values perform translation.
Perspective for distance :

## Slide 65: Mapping 3D object onto 2D image
Given focal length :

## Slide 66: 2D geometric transformations
Isometric rigid transformations:
Similarity with transformation and scaling:
Affine preserves parallel lines:
Projective is most general:

## Slide 67: Fundamental matrix
2D homography:
  Three points in source iamge lie on the same line iff collinear in the transformed image.
Nine parameters for system, eight degrees of freedom in mapping.
  Commonly assume that homography parameters are related by a multiplicative constant.

## Slide 68: Camera model
Use pinhole model to map 3D scene onto 2D image surface.
Center of projection:
  Located distance from image surface.
  Used only for geometric construction.
Projection ray:
Viewing matrix:

## Slide 69: Intrinsic camera parameters
Model for camera characteristics:
  Offsets from optical axis to image sensor.
  Skew models analog video capture.
  Scale factor for pixel spacing.
Lefthand submatrix is calibration matrix .

## Slide 70: Camera and world coordinates
Extrinsic camera parameters describe camera’s relationship to the scene.
Rotation matrix , translation matrix , projection matrix .

## Slide 71: Camera calibration
Externally determine intrinsic and extrinsic camera parameters.
Tsai’s method:
  Capture images of calibration target.
  Single target version takes multiple images at different target positions.
  Two-target version puts targets at right angle.

## Slide 72: Tsai calibration
Two types of parameters:
  Group I require nonlinear estimation.
  Group II requires only projective geometry.
First compute Group II, then Group I.
  First estimate rotation and translation.
  Next estimate focal length and transformation.
Frame rate must be estimated for video.
  Frame rate can vary within a camera over time.
  Frame rate varies widely between cameras.

## Slide 73: Image display
Display affects perception of the image.
Most displays are 2D renderings.
Display may be reflective (ink jet) or radiative (monitor).

## Slide 74: Electronic displays
LCD: light valve.
OLED: emissive LED elements.
DLP: reflective elements.
3D display:
  Early display used different colors at each eye to create monochrome 3D.
  Most modern 3D systems use polarized images.
Display type | Dynamic range | Gamut | Persistence
LCD | medium | medium | medium
OLED | high | large | medium
DLP | high | large | low

## Slide 75: Gamuts
Gamut: range of colors produced by a display.
Without adjusting for gamut, an image may change appearance on different displays.

## Slide 76: Color management
Color management systems keep track of display system parameters separate from the images being displayed.
  Device profile describes device.
  Color management module translates between devices.
Filmmakers often create custom lookup tables (LUTs) to control rendering of color.

## Slide 77: Practical image capture
Photographer chooses parameters to define the image:
  Exposure.
  Color temperature.
  Composition.

## Slide 78: ISO
ISO number describes sensitivity of image sensor.
  High ISO value is more sensitive.
Speed = ISO value.
Doubling/halving of ISO values corresponds to 1 increment of aperture or shutter.
Many image sensors provide electronic adjustment of ISO through internal amplification.

## Slide 79: Exposure control
Traditional cameras use iris, shutter to control exposure.
Typical shutter speeds: , etc.
Standard f-stops: , etc.
Many smartphones use variable ISO to substitute for iris.

## Slide 80: Reciprocity
Aperture and shutter speed can be traded off to control exposure:
  Smaller aperture, longer shutter speed.
Reciprocity:
  Aperture/shutter pairs give equivalent exposure.
  Film displays reciprocity failure at exposures longer than several seconds.
Reciprocity trade-offs:
  Depth-of-field.
  Motion blur.
Exposure value EV describes luminosity.
  Used to capture an exposure level without specifying aperture, shutter speed.

## Slide 81: Exposure and image tones
+1EV
nominal exposure
-1EV

## Slide 82: Measuring light in the scene
Light meter measures light on the meter sensor.
Metering positions:
  Incident at the subject.
  Reflective at the camera.

## Slide 83: Meter readings and rendering
Light meter reading is generally given as EV or aperture/shutter speed.
Reading calibrated to produce mid-level gray.
  Gray value may vary from one meter manufacturer to another.
Placing a value in the scene at a different gray level requires adjusting the exposure.
  White paper is rendered as mid-level gray.
Gray card can be used as a reference for reflective metering.

## Slide 84: Lighting for the subject
Limited dynamic range means that not all parts of the image can be kept at reasonable exposures.
Indoor subject, outdoor background:
  Face-weighted exposure blows out the outdoor background.
  Reducing exposure saves the background but person goes dark.
face-weighted exposure -2EV
Silver Skillet Restaurant, Atlanta

## Slide 85: Zone System
Defined by Ansel Adams.
Eleven Zones:
  0 for black.
  X for white.
Zones are one f-stop apart.
11 Zones correspond to dynamic range of film.
Use Zones to describe scene during previsualization, map it onto a rendering.

## Slide 86: Tonal range adjustment
Visual system adjusts exposure dynamically while camera captures image at one exposure.
Photo tools can be used to adjust the tonal mapping of an image.
Adams: previsualize image to include strong black, strong white.
  Provide anchors for visual system.
before
after

## Slide 87: Color temperature
Color temperature of light source affects how colors are rendered.
  Visual system cannot correct for color temperature in the original scene---it only sees the reproduced image.
Common color temperature descriptions:
  Daylight.
  Tungsten.
  Fluorescent.
Algorithms can compensate for color temperature.

## Slide 88: Image composition
The placement of scenic elements in the image is an important aspect of imaging.
  The image frame helps to define the image.
Placing elements of interest around the image encourages the eye to scan over the image.
Subjects are rarely in the center of interesting photographs.
  Counterexample: Mad Max Fury Road placed nose of drivers at the center of the frame; George Miller didn’t want viewers to search for the subject.

## Slide 89: Compositional placement rules
Rule of Threes
Golden Ratio

## Slide 90: Depth-of-field and composition
1/200 sec, f/7.1
1/40 sec, f/16

## Slide 91: Vanishing point
Perspective creates vanishing points for parallel lines.
Vanishing point may be created horizontally or vertically.
Vanishing points draw the eye.

## Slide 92: Horizontal and vertical perspective
Utah
Washington DC

## Slide 93: View cameras and depth-of-field
View cameras provide camera motions for lens, image surface.
  Image surface does not have to be along optical axis or perpendicular to the optical axis.
Camera motions can be used to manage perspective, depth-of-field.
Scheimpflug rule:
  Maximum depth-of-field when image surface, lens plane, and subject plane meet at a single point.

## Slide 94: Composition for moving pictures
Framing described relative to people:
  Establishing shot shows the entire scene.
  Two-shot shows two people.
  Medium shot shows upper torso of one person.
  Close-up shows face of one person.
Cinematic tradition holds that D. W. Griffith invented the close-up on Birth of a Nation.
Panning changes the position of camera relative to the scene.
  Hitchcock shot Rope in 10-minute shots without cuts.
Zooming adjusts framing, zooming action provides emphasis.

## Slide 95: Framing dialog
180 degree rule
alternating shots for dialog

## Slide 96: Relationships between shots
Transitions:
  Cuts.
  Fades.
  Dissolves.
  Wipes.
Montage was developed by Soviet filmmakers in the 1920s.
Kuleshov effect:
  Images juxtaposed by transitions affect the interpretation of nearby images.
Cut identical sequence of expressionless, sitting actor against:
  Plate of soup.
  Girl in coffin.
  Woman in divan.
Audience believed that actor had different expression in each case.

## Slide 97: Image quality assessment
Image quality depends on many characteristics:
  Image type.
  Display.
  Visual system.
  Individual viewer.
Physics-based measurements are not always sufficient to describe image quality.

## Slide 98: Sharpness and resolution
Katz’s formula for combining resolutions of system components:
Higgins and Jones found that resolving power does not correlate well with subjective experience of sharpness.

## Slide 99: Acutance
Acutance: picture contrast.
Measure using light/dark strips.
Each strip has density , density slope .
Acutance:
Combination of acutance and resolving power:

## Slide 100: Subjective quality factor (SQF)
Compares image metrics to subjective quality.
  Used panel of viewers to evaluate quality of a set of images.
Outer integral over line pair separation, inner integral is over polar coordinates.