## Slide 1: Smart Camera Design Chapter 3: Image Capture Systems and Algorithms
Marilyn Wolf

## Slide 2: Outline
Camera architecture.
The camera design space.
Image sensors.
Pre-exposure operations.
Post-exposure operations.
Image and video compression.
Computing platforms.
Image characteristics and image capture.
Stereo and multicamera systems.
Trade-offs.

## Slide 3: Generic camera architecture
Image sensor.
On-the-fly filtering.
  Bayer pattern interpolation.
Image processing unit.
  Sharpening.
Image compression engine.
  JPEG, H.264.
Host processor.
  Camera control, user interface.
Storage system.
Display and user interface.

## Slide 4: Imaging chain efficiency characteristics
Execution time.
  End-to-end latency from capture to generation of final file.
Energy and power consumption.
  Battery life.
Memory bandwidth and capacity.
  Limits size of image, frame rate.

## Slide 5: Camera design trade-offs
Image quality.
Physical size.
Cost.
Power consumption and battery life.

## Slide 6: Image sensor size and camera size
Small image sensor has small normal focal length.
Small image size also gives shorter optical system depth.
Small image sensor in smartphone reduces phone thickness.

## Slide 7: Camera use cases
Still or video snapshots.
Portraiture.
Landscape or architectural photography.
Electronic news gathering (ENG).
Studio videography.
Technical and scientific.

## Slide 8: Web cam, surveillance camera
Low cost, small size.
Simplified operation.
Only moderate demands on image quality.
User interface provided by host.
Inexpensive optics.
Fixed focal length.
Small aperture to avoid focus.

## Slide 9: Smartphone camera
Very small physical size.
Low power consumption.
Still and video capture.
Moderate to high image quality.
Rich processing platform.
Very small optical system.
Very small image sensor.

## Slide 10: Mirrorless and SLR cameras
Larger handheld size.
Larger battery, higher power consumption.
High to professional-grade image quality.
Still and video capture.
Complex optics, interchangeable lenses.
Large image sensors.
Processors designed for camera operation.

## Slide 11: Camcorders
Optimized for video.
Video features such as zebra stripes.
Moderate-sized image sensor.
Complex lenses, may or may not be interchangeable.

## Slide 12: Image sensors
Image sensor design parameters:
  Sensor size.
  Pixel size and pixel count.
Two major technologies.
  Charge-coupled device (CCD).
  CMOS APS.

## Slide 13: Color image sensors
Single-sensor color uses color filter array puts filters on top of each pixel.
  Some video cameras use three separate RGB sensors.
Bayer pattern:
  pattern.
  Two greens because eye is most sensitive to green.
  Missing colors are interpolated separately.
Foveon sensor used wavelength-dependent light penetration to sense RGB at each pixel site.

## Slide 14: Pixel vertical structure
Color filter fabricated on top of color filter.
Microlens concentrates light on photosensor.
  Some of pixel is occupied by other circuitry.
  Fill factor: percentage of pixel area occupied by photosensor.

## Slide 15: Video formats
Interlacing introduced in analog television to improve brightness uniformity.
  Two fields per frame, displayed sequentially.
HDTV specifies multiple formats, including , .
4K UHDTV .
8K UHDTV
Video signal is often encoded as luminance + chrominance.
  YCrCb.
n:n:n describes spatial subsampling:
  4:4:4 samples luminance, chrominance at full resolution.
  4:2:2 samples chrominance at half resolution.
  4:2:0 samples chrominance at half resolution, alternates Cr, Cb.

## Slide 16: Silicon as a light detector
Silicon is most sensitive to red end of spectrum.
  Red, IR penetrate deepest into silicon.
Absorbed photons create electron-hole pairs.
  Quantum efficiency is proportion of carriers generated by photons.

## Slide 17: Photocurrent
Photocurrent:
  Carrier mobility .
  Carrier lifetime .
  Optical power input .
  Planck’s constant .
Primary photo current.
Photocurrent gain:
  Carrier transit time
  Recombination rate .
Photodetector response time depends on transit time:
  Distance traveled.
  Electric field.

## Slide 18: Photodetector noise
Thermal noise (Johnson noise):
Shot noise.
  Due to discrete carriers.
noise.
  Poorly understood physical mechanism.
  Highly correlated in successive samples.
Dark current:
  Current produced under zero illumination.
  Primarily from recombination generation processes due to traps in silicon.
Bulk recombination generation current proportional to :
  Intrinsic carrier concentration .
  Depletion region width .
  Minority carrier lifetime .

## Slide 19: Photodetector structures
Photodiode uses a pn or pin junction.
Phototransistor uses the transistor depletion region to collect photons.
  Gate absorbes blue, limiting color response.
  Transistor used to amplify photocurrent.

## Slide 20: Charge coupled device
Image sensors vary in how they move photodetector charge off-chip.
CCD uses array of MOS capacitors as a bit bucket chain.
CCDs are extremely efficient---lose very little charge.
Require non-standard processing, more expensive to manufacture.

## Slide 21: APS CMOS image sensor
CMOS image sensor uses slightly modified manufacturing line used for DRAM.
  Lower manufacturing cost than CCD.
Column of pixels connected to bit line.
Columns read out a row at a time.
Analog shift register reads out each row.

## Slide 22: APS pixel
Photodiode transforms photons into charge.
Charge is stored in capacitor .
provides current gain.
connects pixel to bit line.
resets pixel.

## Slide 23: Column sample-and-hold
Each column must sample pixel value.
  Sampling capacitor .
  Sampling transistor .
Double-sampling may be used to reduce noise.

## Slide 24: Readout noise
Ideal noise model of sample-and-hold:
Fixed pattern noise caused by mismatches between transistor threshold voltages on the bit line.
  Results in luminance pattern on the image.
Reset noise due to incomplete reset of the pixel.
  Image lag: value of pixel depends on its value in previous image.

## Slide 25: Extended dynamic range
Standard pixel has linear dynamic range of .
Logarithmic sensors provide logarithmic response similar to eye.
Can vary reset transistor voltage during capture to dump charge from .

## Slide 26: Advanced image sensors
Put analog/digital converter on each pixel.
Time-of-flight sensor times return of laser pulse.
Far infrared sensors:
  Microbolometer.
  Quantum-well sensor.
Stacked sensors use back-side illumination:
  High-bandwidth interconnect.
  Stacked memory, processor.

## Slide 27: Image sensor characteristics
Pixel depth:
  Number of bits per pixel value.
Pixel count:
  Number of pixels in image.
Pixel pitch:
  Physical size of pixel.
Image sensor size:
  Physical size of complete image sensor.

## Slide 28: Quantization noise
Analog/digital conversion produces quantized digital value.
Assume uniform distribution over .
RMS noise:
10-bit dynamic range similar to film.
12-bit and 14-bit sensors are common.
Small pixel depths result in posterization.
Kell factor: limit image bandwidth to avoid beat frequencies near Nyquist limit.

## Slide 29: Pixelization
Pixel dimensions quantize spatially.
RMS pixelization noise:
  Pixel count per dimension .
  Pixel pitch .
  RMS error
smaller pixel
larger pixel

## Slide 30: Image noise vs. pixel pitch
Competing noise mechanisms:
  Pixelization noise goes down with smaller pixels.
  Photodiode noise goes up with smaller pixels.
Imager reset noise:
  Pixel pitch related to capacitor size.
  Decreasing pixel size increases reset noise.
Pixels have an optimal size to balance photodiode, pixelization noise.

## Slide 31: Sensitometry
Experimental evaluation of image sensor characteristics.
Characteristic curve shows log exposure over pixel value.
Film look comes in part from goes of the characteristic curve.
electronic image sensor
film

## Slide 32: Sensor ISO and amplification
ISO 12232:2006 describes standard for determining digital native ISO.
Logarithmic sensors put ISO amplifiers in logarithmic control circuitry.
  Most noise in amplifier chain comes from first stage.
Expose-to-the-right:
  Higher illumination at the pixel increases spread between signal and shot noise.
ISO invariance:
  Noise independent of ISO setting.
  Some image sensors are less ISO invariant than others.

## Slide 33: Motion blur
Rolling shutter moves over the image sensor.
Moving image is captured at different positions over different positions.
Tilted speeding object has become a visual motif.

## Slide 34: Shutters
High-end cameras often use mechanical shutters.
  May cause shake and vibration.
  Global shutter vs. rolling shutter.
Mechanical shutter types:
  Leaf shutter within lens.
  Focal plane shutter at focal plane.
  Rotating shutter for moving image camera.
Electronic shutter pulls charge off pixels.
  Not as effective as mechanical shutter.
Many cameras combine electronic, mechanical shutters.

## Slide 35: Pre-exposure operations
Must determine focus, exposure.
  Where in the image?
  At what value.
Must be fast.
Can combine image sensor data with other sensors.

## Slide 36: Histogram
Histogram provides a summary of luminance values.
  Pixel values are binned.
Ends of histogram provide under/overexposure information.
Shape of histogram provides information on image structure.
luminance histogram
RGB histogram
Atlanta

## Slide 37: Autofocus
Active autofocus illuminates the image.
  Infrared, ultrasound, visible.
Infrared autofocus uses triangulation.
  IR pulses sent to subject.
  Linear array of photodetectors gives estimate of angle to subject and therefore distance.
Ultrasound autofocus uses time-of-flight to measure distance.

## Slide 38: Phase-detection autofocus
Passive autofocus system.
Beam splitter directs fraction of light to pair of line sensors.
  Line sensor gives profile of intensity along one dimension.
Comparing line sensors gives both direction and amount of defocus:
  In focus gives known separation between profiles.
  Front focus puts intensity profiles farther apart.
  Back focus puts intensity profiles closer together.
Modified lenses on pixels can provide ranging information.

## Slide 39: Contrast detection
Measure contrast between adjacent pixels.
  Focus gives high contrast edge.
Does not require specialized hardware.
Does not provide focus direction.
  Focus mechanism must hunt.
Contrast must be measured at multiple angles to allow for varying line orientations.
Focus evaluation algorithms:
  Sum-modulus-difference forms the sum-of-difference of adjacent pixels.
  Histogram entropy is defined as for the bins of the histogram .
  Histogram of local variations finds the best-fit line through the logarithms of the histogram bins.
  Fast Fourier transform evaluates the FFT of the image region.

## Slide 40: Exposure
Early autoexposure systems used a small number of photodiodes.
Exposure zones were measured separately, weighted to provide overall exposure.
  Center-weighting.
Digital cameras can measure exposure at multiple points, weight values.
Histogram extremes can be used as a check.

## Slide 41: Image stabilization
Mechanical image stabilization moves the image sensor.
  MEMS accelerometers measure movement, transducers move the sensor.
Optical image stabilization moves the optics.

## Slide 42: Face detection
Face detection can guide both exposure and focus.
Basic structure of face provides a small set of useful features.

## Slide 43: Viola and Jones face detector
Prune search space quickly using simple features.
Haar-like features identify small features.
Integral image provides intermediate representation:
Adaboost used to train classifiers.
Haar-like features
integral image

## Slide 44: Post-exposure operations
Generate complete image.
  Color filter array interpolation.
Improve image characteristics.
  Sharpening.

## Slide 45: Color filter array interpolation
CFA interpolation provides missing images from filter array.
Bilinear interpolation (given green pixel):
Bicubic interpolation averages over a larger area.

## Slide 46: Interpolation artifacts
A white picket fence produces separate RGB lines at each picket edge.
Interpolation estimates the edge at different positions for different colors.

## Slide 47: Subsampling and color rendition example
Nikon D810, no pixel shift
Olympus OM-D E-M1 Mk II w. pixel shift

## Slide 48: Subsampling and color rendition
Fabric contains a small proportion of blue threads.
Two different sensor configurations:
  Pixel shift captures RGB samples at each pixel position.
  Normal Bayer pattern sensor.
Bayer pattern captures blue threads as weak color.
Pixel shift captures strong blue.

## Slide 49: White balance
Gray world assumption: average color is gray.
  Example photo violates gray world assumption.
Find average value of pixels, then adjust color components:
Cleveland OH

## Slide 50: White balance, cont’d.
More sophisticated algorithm applies gray world model only for a limited band of colors:

## Slide 51: Sharpening
People prefer images to which sharpening has been applied.
To sharpen edges of any orientation, use an approximation of the Laplacian:
Compute weighted sum of pixels in region:
Filtering window has value 9 in center, -1 elsewhere.

## Slide 52: Image and video compression
Reduce file size while maintaining acceptable image quality.
Lossy coding---information is removed from the image.
Perceptually-aware coding---remove image features less likely to be noticed.

## Slide 53: JPEG
Image is divided into blocks.
Discrete cosine transform analyzes spatial frequencies of block.
Quantization modifies DCT coefficients---lossy.
Entropy coding encodes coefficients---lossless.

## Slide 54: Discrete cosine transform (DCT)
Given values :
Inverse DCT:

## Slide 55: DCT computation
DCT can be computed efficiently using butterfly a la Cooley-Tukey.
Butterfly form:

## Slide 56: 2D DCT
Two-dimensional DCT can be formed from row and column DCTs:
Separability of dimensions improves efficiency.

## Slide 57: DCT quantization
DCT quantization modifies DCT coefficients to improve its ability to be losslessly compressed.
  Zeroes, strings of zeroes are easy to compress.
Quantization modifies image, throws away image information.
Perceptual coding---change values at higher spatial frequencies.
Apply quantization matrix:
Image quality parameter controls degree of quantization.
52 | 55 | 61 | 66 | 70 | 61 | 64 | 73
63 | 59 | 55 | 90 | 109 | 85 | 69 | 72
62 | 59 | 68 | 113 | 144 | 104 | 66 | 73
63 | 58 | 71 | 122 | 154 | 106 | 70 | 69
67 | 61 | 68 | 104 | 126 | 88 | 68 | 70
79 | 65 | 60 | 70 | 77 | 68 | 58 | 75
85 | 71 | 64 | 59 | 55 | 61 | 65 | 83
87 | 79 | 69 | 68 | 65 | 76 | 78 | 94
example quantization matrix

## Slide 58: Entropy coding
Entropy coding reduces size of coefficient representation using loss length coding.
Standard allows for several different coding algorithms:
  Huffman, run-length, arithmetic, combinations.
Read out coefficients in zig-zag order:
  Low spatial frequencies to high spatial frequencies.
  Increases lengths of zero strings.

## Slide 59: Coding quality
high quality
low quality
high - low
Black Rock Mountain GA

## Slide 60: JPEG features
Image may be converted to YCrCb, chroma components subsampled.
Profile: set of features.
JFIF file format standard describes how to represent JPEG data as file.
EXIF standard provides metadata, compatible with JPEG and other file formats.

## Slide 61: H.264/AVC video coding
Video coding leverages still coding techniques.
High video data rates require additional encoding mechanisms.
  Motion estimation and compensation.
Interframe coding:
  Code one frame in terms of another.

## Slide 62: Block motion estimation
Divide frame into macroblocks.
Search for macroblock from one frame in other frames.
Encode displacement as motion vector.
Compute error signal to compensate for movement within the macroblock, regions that could mot be matched.
Frame types:
  Infraframe (I) frame is not predicted.
  Predicted (P) frame is predicted by past frames.
  Bidirectional (B) frame is predicted by past and future frames.

## Slide 63: Generic video encoder

## Slide 64: Generic video decoder

## Slide 65: Block motion estimation algorithm
Compare blocks using sum-of-absolute difference of pixels:
Compare blocks at various offsets, choose best match.
Search is limited to a region defined by the standard.
Full search is expensive.
Heuristic search algorithms compare a small number of offsets.

## Slide 66: Three-step and four-step search
three-step
four-step

## Slide 67: Diamond search

## Slide 68: Subpixel motion estimation
Interpolate intermediate pixel values:

## Slide 69: Bit rate
Variable bit rate:
  Output bit rate depends on video content.
Constant bit rate:
  Encoding is adapted to maintain roughly constant bit rate.
Lagrange multiplier method:
  Rate , distortion for bit allocation .
  Langrange multiplier controls relative importance of rate, distortion.

## Slide 70: H.264 encoder

## Slide 71: H.264 features
Flexible block motion estimation algorithms:
  Multiple block sizes.
  Lagrangian rate-distortion control.
YCrCb color space, 4:2:0 sampling.
Intra prediction predicts pixels from neighboring pixels.
Deblocking filter smooths block boundaries.

## Slide 72: Compressed image quality assessment
Peak SNR does not take into account perceptual characteristics:
Structural Similarity Index Model (SSIM) is easy to compute, takes into account perceptual characteristics.
Given image patches :

## Slide 73: Camera computing platform
Computing platform determines:
  Rate at which images can be generated.
  Image/video compression features.
  Battery life.
Cameras are heterogeneous multiprocessors.
  Multiple CPUs, DSPs.
  Hardwired accelerators, particularly for video.
  GPUs.
Smartphone, SLR cameras often use different processor architectures.

## Slide 74: Buffering
Processing at different rates requires buffering between stages.
Buffering may limit frame rate for still images.
Video buffering must take into account worst-case rate.

## Slide 75: Camera displays
A good camera requires low latency from image sensor to display.
Image sensor may be subsampled during preview to reduce latency.

## Slide 76: Storage
Flash storage devices provide large data capacity, high data rates.
File system format determines compatibility.
Image file formats:
  TIFF typically used for lossless compression.
  JPEG/JFIF is widely used.
  EXIF defines metadata to supplement image data.
  DCF standard describes relationship between storage media, writers, and readers.
  RAW image formats are usually proprietary.

## Slide 77: Stereo
Disparity between subject position in stereo images gives distance to subject.
Heuristic search algorithms can be used to speed up disparity search.

## Slide 78: Trade-offs revisited
Image sensor size:
  Small sensor gives small optics, small camera.
  Large sensor gives higher image quality.
Resolution-frame rate product limited by pixilation, sensor noise.
Some characteristics can be compensated by post-processing.