## Slide 1: Smart Camera Design Chapter 5: Image and Video Analysis
Marilyn Wolf

## Slide 2: Outline
Building block algorithms.
Image and video characteristics.
Scene analysis.
Tracking.
Multicamera systems.
Use cases and workflows.

## Slide 3: Mahalanobis distance
Compares multidimensional data to a distribution:
  Measurement .
  Mean vector .
  Covariance matrix .

## Slide 4: Harris detector
Identifies corner features:
  Window function .
  Shift range .

## Slide 5: SIFT
Extracts features with invariance to scale, orientation.
Extracted from k-scaled difference-of-Gaussian images:

## Slide 6: SIFT, cont’d.
Extremal position estimated using Taylor expansion
  Reject low values of
Reject features with high curvature across edge but small curvature in perpendicular:
  Hessian matrix of second-order derivatives of .
  .
Reference orientation determined at local maximum of local image gradient orientations:

## Slide 7: Feature extractors
SURF requires less computational effort than SURF.
  Uses box filter as approximation for Gaussian.
  Haar wavelet values are processed to provide descriptor.
Mikolajczyk et al. compared region detectors.

## Slide 8: Model fitting
RANSAC used to fit models to data with some large discrepancies.
  Iteratively refines a set of candidate points, based on an error tolerance.
Particle filtering used for data with non-standard models.
  Sequential importance sampling generates samples based on their relative importance.
  Resampling generates new samples from previously estimated distribution.

## Slide 9: Image statistics
Huang et al. proposed statistics for range images:
  distribution of single pixels.
  Bivariate distribution.
  Range patches are grouped into small clusters.
Zontak and Irani used Parzen estimator for density of image patch in neighborhood :
  Search radius grows exponentially with patch gradient

## Slide 10: Saliency
Relates image characteristics to behavior of human visual system.
Itti et al. developed a feature-based saliency map of an image.
Hou and Zhang created saliency map from spectral residue.
Goferman et al. developed context-aware saliency:
  Global features, visual organization rules, priors on object location.
Liu et al. created saliency map using supervised learning.
[Itt98]

## Slide 11: Key frame selection
Key frame is a still image used to represent a shot.
  Used to create storyboards for live action.
  Used to define animation sequence.
Identify key frames at local minimum of motion:
  Handles subject motion, camera motion, zooming in a single framework.
Compute motion as sum of magnitudes of optical flow vectors:

## Slide 12: Key frames from Nixon resignation speech

## Slide 13: Visual search
QBIC system:
  Images and videos analyzed as they were loaded.
  Query system extended for image and video characteristics.
Object characteristics:
  Texture.
  Color.
  Location.
  Shape.
Scene characteristics:
  Texture.
  Color.
  Texture/color as a function of position.
  Sketches.
Video keyframes characterized by object and camera motion.
Sivic and Zisserman developed image descriptors for video that could be used in text retrieval systems.
  An ellipse around an interest point.
  Region whose area is steady as the intensity gradient isotropy is maximized.
  Features represented as 128-D SIFT.
  Mahalanobis distance between regions.
Philbin et al.:
  Identified affine-invariant Hessian regions, represented with 128-D SIFT descriptors.
  Cluster descriptors with k-means, represented by k-dimensional trees.
  Used RANSAC to generate spatial transformations between regions.

## Slide 14: Face detection and recognition
Tasks:
  Detection = a face.
  Recognition = which face.
Leung et al. model-based approach:
  Image pyramid.
  Match against local feature template vectors.
  Build a graph model for constellations of features.
Zhu et al. used wavelet features.
Eigenface method performs both detection and recognition:
  Facebook of images .
  Image is -dimension vector.
  Fit image using principal component analysis to find orthonormal vector and engenvector.
  Any face is a linear combination of the facebook faces.

## Slide 15: Tracking
Tracking:
  Target model.
  Path model.
Camera setup:
  Single camera.
  Multiple cameras.
  Moving camera.
  Multiple bands (visible, IR, etc.)
target
track
observation

## Slide 16: Background elimination
In video, background = items not of interest.
In many scenes, target moves, background does not move much.
Background subtraction:

## Slide 17: Mixture-of-Gaussians
Stauffer and Grimson: model each pixels with a set of Gaussians.
  Allows multiple appearances for a pixel.
  A given pixel may match any of the models to be classified as background.
Probability of observing pixel :
Weight update:
Mean, variance update:

## Slide 18: Tracking from a fixed camera
Model linear track using Kalman filter.
  Frame .
  Observation .
  Target state
  System state:
  State transition matrix:
Propagate step:
Update step:

## Slide 19: Multi-target tracking
Multiple targets must be distinguished and assigned to proper tracks.
  Several different assignments of observations to tracks may be possible.
Reid used Kalman filter for each target.
Probability of new target configuration:

## Slide 20: Multi-target tracking, cont’d.
Fortmann et al.: build hypotheses to assign observations to targets.
  Each observation assigned to at most one event.
Measurement PDF:
Probability of a set of target identifications given observations:

## Slide 21: Target appearance
Object appearance is influenced by scene lighting.
Target may be occluded.
Mixed indoor-outdoor lighting exhibits high contrast ratios.

## Slide 22: Appearance models
Bounding box:
Ratio of bounding boxes:
Use Bhattacharyya distance to compare color or luminance histograms:
Jepson et al.: multi-component appearance mixture model:
  Stable features.
  Outliers.
  Short time constant set to account for motion.
  Expectation maximization over observation classification:

## Slide 23: Appearance models, cont’d.
Comaniciu et al.: mean-shift target model.
  Compare using generalized Bhattacharyya coefficient.
  Target represented as an ellipse with normalized size.
  Kernel profile weights pixels relative to distance from center, covex and monotonic decreasing.
Distance between candidate distributions:
Kernel position estimate in new frame:

## Slide 24: Activity analysis
Pfinder used statistical models of Gaussian blobs.
  Pixels classified into blob/non-blob.
  Blob update:
Likelihood of pixel’s membership in blob, background:
Use heuristics for shadows.
Update blob statistics using new pixel members:

## Slide 25: Gesture analysis
Wolf et al gesture analysis:
  Background elimination.
  Blob identification.
  Ellipse matching.
  Graph model classification into pose.
  HMM for gesture from sequences of poses.

## Slide 26: Gesture analysis, cont’d.
Stauffer and Grimson classified motion using codebook.
  Observation
  Does not directly model time or sequence.
  Activity is a multiset of observations.
Co-occurrence matrix:
Update:

## Slide 27: Tracking from a moving camera
Egomotion: motion of camera relative to scene.
Tracking methodology:
  Extract feature points.
  Identify corresponding features between frames.
  Estimate egomotion from feature point correspondences.
  Estimate 3D structure, identify region of interest.
  Find target in region of interest.
[Lin12]

## Slide 28: Tracking from a moving camera, cont’d.
Egomotion estimated using motion vectors:
Foregrond/background test:
Classify motion using belief propagation.
[Lin12]

## Slide 29: Multicamera systems
Occlusion caused by other objects in the scene.
Pixels-on-target:
  Some cameras more likely to be near target.
Depth analysis for 3D.
Coverage of large spaces.
Multicamera systems enabled by semiconductor imaging, system-on-chip, IP cameras.

## Slide 30: Distributed algorithms
Practical systems require distributed algorithms:
  Raw video requires large bandwidth.
  Centralized analysis of features does not scale well.
Need calibration algorithms for camera parameters, time.
Lin et al:
  Identify features locally.
  Camera with token fuses features across cameras.
  Token moves with subject.

## Slide 31: Spatial calibration

## Slide 32: Spatial calibration algorithm
Devarajan et al distributed algorithm.
  Perspective model
  Projection of scene points onto camera :
Each camera calibrates locally using structure-from-motion.
Solve for projective depth:

## Slide 33: Temporal calibration
Cameras must be synchronized.
Velipasalar and Wolf:
  Perform local search to identify corresponding frames.
  Use frame offset to synchronize.
  May be performed periodically to correct for drift.
i
target
j

## Slide 34: Multicamera tracking
Two cases:
  Overlapping fields-of-view.
  Nonoverlapping fields-of-view.
Velipasalar et al.: cooperating trackers share track estimates.
  Camera can anticipate the appearance of a target not currently visible.
Kokiopoulou and Frossard used consensus algorithm.
Chang and Gong used Bayesian network to fuse tracking results.

## Slide 35: Tracking over path graphs
Used to model camera networks with non-overlapping fields-of-view.
  Entry/exit node.
  Nodes for camera locations.
  Directed edges identify possible paths.
Use supernode to model direction of movement through the node.

## Slide 36: Tracking using hidden Markov model
Bayesian models:
  Target .
  Obsevation .
Probability of observations of target on a track:
Kettnaker and Zabih track model:
  Duration and location of transit from one camera to another .
  Probability of a track of a given length.
  Probability of new targets entering the system.
Path probability:
Take logarithm, solve as weighted assignment problem.

## Slide 37: HMM tracking, cont’d.
Oh et al.:
  Consecutive observations .
  Track probability
  Set of tracks .
Solve using Metropolis-Hastings algorithm:
  Randomly select move from birth, split, extend, update, switch.
  Randomly accept with probability

## Slide 38: Person reidentification
Pose, lighting may cause same person to be identified as different people by different cameras in the network.
Gheissari et al.:
  Break person image into regions based on edges, hue/saturation.
  Identify over a series of frames to minimize effect of fabric movement.
  Cluster features.
  Identify correspondences between regions.
  Map onto body parts using model.
Zheng et al. used learning algorithms based on relative distance between sets of features.

## Slide 39: Use cases and workflows
Monitoring of scenes to detect activity, certain types of activity.
Identification of people and vehicles.
Autonomous and driver-assisted vehicles.
Monitoring of large groups of people.
Important concepts:
  Image capture to maximize information on region of interest.
  Calibration.
  Feature extraction.