## Slide 1: Architectures
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: Processor security
Root-of-trust provides trusted execution environment.
Secure boot validates executable using digital signature.
Other programs can trace their provenance to the root.
Side channel attacks identify or alter communication:
  Differential power analysis.
  Electromagnetic radiation.
  Sound.
  etc.
CPU side channel attacks:
  Meltdown leverages out-of-order execution.
  Spectre attacks branch prediction and speculative execution.

## Slide 3: Model-based design
Abstract model provides higher-level representation than programming language.
Domain-specific modeling language (DSML) (Karsai et al.):
  UML plus Object Constraint Language as metamodeling language.
  DSML allows abstraction, modularization, interfaces, aspects, and references.
  Can capture access rights using partition construct.
DSML for irrigation networks (Tariq et al.):
  Based on Generic Modeling Language.
  Included both atoms and higher-level models.
  Used MATLAB to solve Saint Venant’s equation.
AADL is model-based design language for avionics and other domains.

## Slide 4: Architectural threat modeling
Privilege escalation attacks can allow processes to access/manipulate data for which they do not have privileges.
  Many operating systems do not transitively check access rights.
  Demonstrated on Android.
Quality-of-service (QoS) attacks compromise system timing.
  Delaying data may be sufficient to compromise system function.

## Slide 5: System-level vulnerabilities
System-level vulnerability | Attack goals
Improper data read. | Privacy.
Improper data write. | System malfunction.
Man-in-the-middle. | Privacy, system malfunction.
Timing vulnerability | 
Missed deadline. | System malfunction.
Network-on-chip quality-of-service. | System malfunction.

## Slide 6: Attack model
Attack model = threat model and design-under-test (DUT) model.
  Architecture graph N, E.
  Storage set S.
  Access capability function K.
  Access zones L.
  Task set T.
  Transaction set M.

## Slide 7: Valid and attack computations
Valid computation:
  Initiating task must have access capability for all required storage locations.
  Both initiating and target tasks must have compatible access capabilities.
  Transactions must complete by deadline.
  Link bandwidth cannot be exceeded.
Varieties of attacks:
  Compromised computation modifies a valid computation.
  Crafted attack is custom built.

## Slide 8: Inferred threats

## Slide 9: QoS-aware service-oriented architecture
Service-oriented widely used in Web systems.
  Transaction-oriented, no quality-of-service.
Networked control requires QoS.
Service description language:
  Messages at the service interface.
  Computation performed by service.
  Modes such as fault-handling.