## Slide 1: False Data Injection Attacks
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: False data injection
Attack, for example, sensors.
  Change data sent from sensors to controller.
  False data results in inappropriate actions.
Example: suppress temperature readings in a fire control system.
Stuxnet employed false data injection.

## Slide 3: Vulnerability analysis
Example: HVAC system with temperature sensor.
Example attack: apply heat to sensor to initiate air conditioning.
Countermeasures:
  Multiple sensors.
  Filter sensor data.
Data monitors are plant-specific and application-specific.
  Operational plant parameter ranges should be known.

## Slide 4: Power grid vulnerability example
Power grid:
  Network of busses () interconnected with transmission lines ().
  System state represented by voltage and phase angle .
  Active power injection measurement .
  Reactive power injection measurement

## Slide 5: Power grid model
Power flow:
  Zpij= hpij(vi, vj, θi, θj)
  Zqij= hqij(vi, vj, θi, θj)
  hpij(vi, vj, θi, θj)= v2i gij – vi vj gij cos(θi – θj) -vi vj bij sin(θi – θj)
  hqij(vi, vj, θi, θj)= - v2i bij – vi vj bij cos(θi–θj) -vi vj gij sin(θi– θj)
Power injection:
  Zpii= hpii (vi, θi, vi1,…, vik, θi1, …, θik)
  Zqii= hqii (vi, θi, vi1,…, vik, θi1, …, θik)
  hpii(v, θ)= vi vj (-gij cos(θi – θj) – bij sin(θi – θj))
  hqii(v, θ)= vi vj (-gij sin(θi – θj) – bij cos(θi – θj))

## Slide 6: State estimation
State estimator estimates state variables to satisfy power equations and measurements.
Measurement error residue R= Z- h(X) captures difference between expected and actual measurements.

## Slide 7: Vulnerability analysis as satisfiability
Does there exist a combination of input data that is accepted by the monitor even though it is not correct?
Can be modeled as a satisfiability problem with real values.

## Slide 8: Dynamic monitoring
Condition monitoring:
  Model-based.
  Model-free (neural networks, etc.).
Credibility of condition monitor depends on:
  Accuracy of model.
  Accuracy of estimation method.
  Accuracy of statistical decision-making.
Kalman filter provides minimum-variance estimates.
  Recursing provides good computational performance.
Confidence intervals can be used to detect deviations of operation.

## Slide 9: Kalman filter as virtual sensor
Kalman filter emulates fault-free plant.
Statistical deviation criteria are used to detect attacks.
  The square of this residuals vector, weighted by the inverse of the associated covariance matrix, constitutes a random variable that follows the χ2 distribution.

## Slide 10: Kalman filter operation
Predict Step:
Prediction of the apriori state estimation:
where … state transition and control input model
Prediction of the apriori error covariance:
where is the noise covariance
Update Step:
Measurement Residual:
Residual Covariance: where is the observation noise covariance
Optimal Kalman Gain:
State Estimation update:
Covariance Estimation Update:
Measurement Residual:

## Slide 11: False data injection attack
False data injection attack can be expressed as a linear combination for random vector .
False data injection attack:
State estimate residuals:
Residuals are unaffected by attack vector.
Can be countered by adding sparsity and low rank constraints to the state estimator objective.