## Slide 1: Safety and Security Design Processes
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: Definitions
Functional safety: risks resulting from faults or design flaws.
Reliability: probability of a system being able to perform its intended function.
Availability: percentage of time over which system is capable of performing its intended function.
Certification: legal or regulatory process in which a system is deemed to meet certain criteria, such as safety.

## Slide 3: Risk management
Risk: potential for loss or injury.
Risk can be minimized but not avoided.
  Risk management may require trade-offs.
Risk management approaches:
  Design for minimum risk.
  Incorporate safety devices.
  Provide warning devices.
  Develop procedures and training.

## Slide 4: Safety management
Risk planning provides an organized, managed process for the identification and mitigation of risks.
Risk assessment identifies potential risks through system engineering documents and lessons learned.
Risk analysis assesses the likelihood of risks and their potential consequences.

## Slide 5: Risk model
Controlled or eliminated risk can be managed through design process.
Residual risk cannot be controlled or eliminated.
  May come from identified or unidentified sources.
Unacceptable risk cannot be tolerated.

## Slide 6: Failure modes and effects analysis
A hazard is a precondition for a mishap.
Failure modes and effects analysis (FEMA) identifies likelihood and severity of hazards.
  Results can be used for risk modeling and management.

## Slide 7: Hazard risk index matrix

## Slide 8: Risk priority number
Product of three factors:
  The severity of the risk.
  The likelihood of occurrence of the risk.
  The system’s ability to detect the failure mode or its cause.
Risk priority number .

## Slide 9: Dependability
Avizienis and Laprie: dependability of computer system is justified reliance on its ability to provide its intended service.
A fault may cause a system failure expressed as an error.
Faults may be physical or human-made.
Faults may be permanent or transient.

## Slide 10: Safety
Safety used for physical safety in this book.
Related to absence or minimization of hazards that may harm life or property.
Leveson argues that reliability is a property of components, safety is an emergent property.

## Slide 11: Fault models
Digital fault models are widely used for digital hardware.
  Stuck-at 0/1 model models fault as output always stuck at a given value.
  Stuck-at open/short models provide different behavior.
  Transient models include bit flips, glitches.

## Slide 12: System failure analysis
Failures often occur because of a cascade of conditions and events.
Common methods:
  Functional Hazard Assessment (FHA).
  Fault Tree Analysis (FTA).
  Failure Mode Effects Analysis (FMEA).

## Slide 13: Functional Hazard Analysis worksheet
Hazard ID | Life cycle phase | Activity | State/Mode | Function
Identifier | Phase analyzed by risk assessment | Actions performed within life cycle phase | System state or mode for the hazard | System function
Functional failure | Hazard Description | System Item(s) | Causal Factor Description | Mishap
Detailed description of failure mode | Detailed description of failure conditions | Portion of the system | Causes of failure | Description of failure
Effect(s) | Existing Mitigations | Software Control Category | Initial MRI | Software Criticality Index
Effects on life, limb, property | Existing means to mitigate failure | Degree of autonomy of software function | Initial risk assessment | Criticality
Target MRI | Causal Factor Risk Level | Recommended Mitigations | Comments | Follow-On Actions
Projected risk after mitigation | Potential for causal factors to occur | Methods to reduce risk | Relevant additional information | Further work to better understand risk

## Slide 14: FHA methodology
System architecture data is analyzed to create a functional hierarchy, block diagrams, and a function/item matrix.
The impact of the failure of each system function is analyzed for hazards.
Safety-significant subsystems and interfaces are identified.
Existing and recommended mitigations are identified.
Safety-significant functions are decomposed to components. Component failures are related to subsystem hazards.
Risk levels and software criticality indexes are identified and assigned. Follow-on actions are specified.
A final FHA report is prepared.

## Slide 15: Fault Tree Analysis
Originally developed at Bell Labs.
Typically proceeds from undesired event backward.
  Precondition events can be combined to create successor event.

## Slide 16: FTA symbols

## Slide 17: Event tree

## Slide 18: Failure Mode Effects Analysis worksheet
Function | Potential Failure Mode | Potential Effect(s) of Failure | S | Potential Cause(s) of Failure
Function being analyzed | Detailed description of failure conditions | Results of failure | Severity | Causes of failure
O | Current Process Controls | D | RPN | CRIT
Probability of failure due to occurrence of this failure | Existing means to mitigate failure | Ability to detect cause or failure mode | Risk Priority Number = | Initial criticality assessment
O | Current Process Controls | D | RPN | CRIT
Probability of failure due to occurrence of this failure | Existing means to mitigate failure | Ability to detect cause or failure mode |  | Initial criticality assessment
Recommended Action(s) | Responsible Party and Target Completion Date
Actions to take | Who is responsible, when task should be finished
Action Taken | S | O | D | RPN | CRIT
How issue was resolved | Final severity | Final occurrency probability | Final detection ability | Final Risk Priority Number | Final risk assessment

## Slide 19: Attack tree
Introduced by Schneier.
Branches are OR-combination by default but may be marked as AND.
Nodes can be labeled for likelihood, cost of attack, special equipment, etc.

## Slide 20: Howard’s model of computer and network attacks

## Slide 21: Microsoft STRIDE model
Part of Security Development Lifecycle.
Threats:
  Spoofing.
  Tampering.
  Repudiation.
  Information Disclosure.
  Denial of Service.
  Elevation of Privilege

## Slide 22: NIST
NIST Framework for Improving Critical Infrastructure Cybersecurity defines activities for managing cybersecurity goals and processes.
  Asset vulnerabilities are identified and documented.
  Threat and vulnerability information is collected from a variety of sources.
  Internal and external threats are identified and documented.
  Potential impacts on business and the likelihood of those events are identified.
  Risk is assessed based on threats, vulnerabilities, likelihoods, and impacts.
  Risk responses are formulated and prioritized.
NIST Guide to Industrial Control Systems (ICS) Security proposes risk management operating at organization, business process, and IT/ICS levels.

## Slide 23: Intrusion kill chain (Hutchins et al.)
Reconnaissance identifies targets.
Weaponization makes use of a Trojan to deliver a payload.
Delivery sends the weapon to the target.
Exploitation triggers the intrusion code on the target.
Installation provides a persistent presence of the adversary on the target.
Command and control (C2) provide remote information on and control over the attack code.
Actions on objectives perform the desired operations on the target.

## Slide 24: Cyber kill chain
Gartner defined cyber kill chain.
Modified cyber kill chain for industrial control systems (Armando and Compagna).
  Stage 1 prepares and executes a cyber intrusion.
  Stage 2 develops and executes attack on industrial control system:
    Attack development and tuning, validation, and the attack proper.
  Constituent actions for attack phases: enabling includes triggering and delivering; initiating the attack includes modifying and injecting; supporting the attack includes hiding and amplifying

## Slide 25: Certification
May be provided by:
  Companies (Underwriters Laboratory).
  Professional societies (IEEE, SAE).
  Other organizations (ISO).
  Government agencies (FAA).

## Slide 26: Aircraft certification
U. S. certification based on FAR Part 21.
Aircraft certification:
  Type certificate for design.
  Production certificate for production.
  Airworthiness certificate for production and maintenance of the aircraft.
Type certification:
  Design information, inspection and maintenance plans, flight tests.
  Supplemental type certificates can certify post-manufacture modifications.
SAE ARP4761 provides guidelines for safety assessment of civil aircraft.
FAR Part 23 governs maintenance and alteration.
  Any item permanently attached to the aircraft must be certified.
  Airframe and Powerplant Mechanic is certified to sign off maintenance.

## Slide 27: Certification and systems analysis
FAR 25.1309 requires that airplane systems and associated components must be designed so that a failure that would prevent continued safe flight and landing is extremely improbable and that the occurrence of any other failure conditions that would reduce the capability of the airplane or ability of the crew to cope with adverse operating conditions is improbable.

## Slide 28: Fail-safe design
Designed integrity and quality including life limits.
Redundancy or backup systems.
Isolation of systems, components, and elements.
Proven reliability so that multiple, independent failures are unlikely to occur during the same flight.
Failure warning or indication.
Flight crew procedures for use after failure detection.
Checkability or the ability to check a component’s condition.
Designed failure effects limits to limit the safety effects of a failure.
Designed failure path to control and direct the effects of a failure so as to limit its safety impact.
Margins or factors of safety.
Error tolerance.

## Slide 29: DO-178C
Used for avionics software certification in U. S., Canada, Europe.
Modified V process:
  Functional requirements, hazard and safety analysis, and functional allocations identify the functions allocated to software and their development assurance level.
  Software is refined from planning, through requirements, design, coding and integration.
  The products of software development at various stages are fed into a system safety assessment that may update the system functional and hazard/safety analysis.
  Software is verified, then the system is verified, with the results of software verification feeding into the system safety assessment.
Design Assurance Level (DAL):
Level A is catastrophic, generally with airplane loss and possible deaths.
Level B is hazardous, reducing system performance or the ability of the crew to operate the aircraft.
C is major, significantly reducing the safety margin or increasing crew workload.
D is minor, slightly reducing the safety margin or increasing crew workload.
E is anomalous behavior that has no safety effect on the aircraft or pilot workload.

## Slide 30: ASTM F3269-17
Defines best practices for certification of UAVs with complex functions (machine learning, etc.).
  Run-time assurance architecture includes recovery control functions.

## Slide 31: Medical devices
Software components of medical devices or software-as-a-medical device must be validated.
Software used in device production or manufacturing quality systems must be validated.
Recalls between 1992-1998:
  3140 total.
  242 attributable to software, 192 due to software defects introduced by changes after the initial release.

## Slide 32: ISO 9000
Family of quality standards.
Principles:
  Customer focus to understand the needs of customers and align organizational objectives accordingly.
  Leadership to establish a vision and challenging goals.
  Engagement of people to use their abilities and make them accountable.
  A process approach to activities.
  Continual improvement of organizational capabilities.
  Evidence-based decision making.
  Manage relationships with suppliers.
ISO/IEC 15504 Automotive SPICE is process assessment model for automotive embedded computing systems:
  Primary life cycle processes for supplier/customer interface.
  Organizational life cycle processes.
  Supporting life cycle processes.

## Slide 33: Safety design processes
Software System Safety Handbook (Joint Services Computer Resources Management Group).
  Safety planning by customer is an iterative process.
  Alternates between requirements/safety policy and software safety plans.
ISO 26262 is for functional safety of automotive E/E systems.
  Guidelines only.
  Subsystem’s hazards are identified and safety goals are specified.
  QM for goals that can be achieved using a standard quality management system, levels A-D otherwise, with A least critical.
ASTM F3153 describes system-level test process for avionics systems safety.

## Slide 34: Software safety processes (Tighlman et al.)
The software critical index of each safety-significant function is determined.
Software requirements hazard analysis derives the software requirements necessary to provide a safe implementation and mitigate hazards.
Software architectural hazard analysis is conducted on architectural documents and requirements. It is performed before the preliminary design review.
Software design hazard analysis expands the analysis to consider the planned implementation; it reviews each identified hazard and looks for new hazards. This step is performed before the critical design review.
Code level hazard analysis analyzes safety-significant variables, typing, code flow analysis, and error processing.
Operator documentation safety review reviews user documents for adequacy and to identify additional hazards introduced by the documents.
Software safety testing verifies and validates all software safety requirements.
Formal review gives evidence for the process and resultant risk level of the design.

## Slide 35: Safety case
Alternate safety analysis methodology.
  Goal-based or evidence-based.
  Part of burden-of-proof on designers and managers.
The aim of the safety case.
The audience for the safety case and why it is being written.
The scope of the document.
A description of the system and its environment.
If created for a modification the system, a justification for the change.
A safety argument.
Supporting safety evidence.
Caveats, assumptions, and limitations.
Conclusions.

## Slide 36: MISRA
Coding-level guidelines for automotive software.
MISRA Generic Modeling Design and Style Guidelines for directory names, file names, etc.
MISRA C guideline examples:
  No unreachable code.
  A typedef name should be unique.
  Macro and identifier names should be unique.
  All if…else if constructs are terminated with an else clause.

## Slide 37: V methodology (MISRA, ISO 26262)

## Slide 38: Security design processes
Attack surface is set of interfaces (attack vectors) or locations where an attacker may extract or inject data.
Bell and LaPadula analyzed security using set theory.

## Slide 39: Security design principles (Saltzer)
Economy of mechanism reduces chances of flaws and faults that could compromise a security mechanism.
Fail-safe defaults require that permission should be explicit and exclusion the default.
Complete mediation ensures that every object access must be checked to ensure that the access is allowable.
Open design forbids reliance on what is now known as security-through-security.
Separation of privilege requires multiple keys for privilege.
Least privilege causes programs and users to operate under the least set of privileges required to complete the task.
Least common mechanism minimizes the commonality of mechanisms among users.
Psychological acceptability promotes ease of use.
Work factor identifies the amount of effort required for a hacker to subvert a mechanism.
Compromise recording creates audit trails.

## Slide 40: MULTICS ring policy
Concentrates on direct modification of information, not indirect modification.
Each information subject (module) and object (repository) is given an integrity level that does not change during its lifetime.
A subject may modify only an object whose integrity level is less than or equal to its own.

## Slide 41: NIST Platform Firmware Resliency Guidelines
Security mechanisms are based on roots of trust or rooted chains of trust.
Changeable firmware shall rely on root of trust update.
Devices with intrusion detection shall make use of root of trust for the detection services.
Recovery shall rely on root of trust.
The update mechanism will be the only mechanism for updating device firmware.
Flash shall be protected to be unmodifiable outside of an authenticated/secire update mechanism.
Protection mechanisms cannot be bypassed.
Write protection of field non-upgradeable memory shall not be modifiable.
Critical data shall be modifiable only through the device or defined interfaces.
A successful attack on firmware shall not compromise the device’s detection capability.
The device shall perform integrity checks on critical data before use.
Firmware recovery mechanisms shall resist attacks against critical data or primary firmware image.
Critical data recovery mechanisms shall resist attacks.

## Slide 42: NIST guidelines
Incident response recommendations:
  Creating a policy and plan for incident response.
  Developing procedures to handle and report incidents.
  The development of guidelines for communicating about incidents with outside parties.
  Creation of a team structure and staffing model.
  Establishing relationships with other parts of the organization.
  Determining the services to be provided by the incident response team.
  Staffing the response team and providing training.
Guidelines for Smart Grid Cybersecurity identifies seven domains, logical interfaces are categorized based on their security characteristics.
NIST SP 800-53 provides U. S. Federal organizations with guidance on the management of information security risk.
  Based on a muti-tier model including organizations, mission/business processes, and information systems
ICS security:
  develop the security business case; build and train a cross-functional team; identify charter and scope of team; define ICS policies and procedures; implement an ICS security risk management framework; provide training for ICS staff

## Slide 43: Zero-day vulnerability
A zero-day vulnerability is not known to those who are interested in mitigating the vulnerability.
Once known, referred to as zero-day exploit.
Possible detection methods:
  Statistical analysis of attack profiles.
  Signatures of known exploits.
  Analysis of exploit’s behavior relative to the target.

## Slide 44: Compare and contrast
Safety risk analysis is driven by requirements and is concentrated on the requirement phase.
Security vulnerability analysis is driven by the system structure and concentrated at the architecture phase and, to some extent, at coding.

## Slide 45: Compare and contrast, cont’d.
Many existing, installed devices are insecure, creating long-term problems.
Traditional IT applications are often transaction-oriented. CPS and IoT systems may not be easily modeled as transactions.
Physical plant attacks:
  Timing attacks.
  Replay attacks.
Safety design often assumes that system designers control characteristics of their components, may not be true for embedded software.

## Slide 46: Incident reporting
Safety incident reporting is widely practiced, may be mandated by law or regulation.
Computer security violations may be collected by several different organizations:
  U. S. CERT.
  Internet Crime Complaint Center.
  DHS National Infrastructure Coordinating Center.
Private organizations may not always report security breaches.
V methodology assumes that risks are known early in the design process.