## Slide 1: Security Testing and Runtime Monitoring
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: Security testing
Challenges:
  Exponential growth in complexity.
  Long supply chains with limited visibility.
Testing provides evaluation of correctness, security, and performance.

## Slide 3: Fuzz testimg
Traditional software code testing:
  Static analysis typically gives high false positive rates, limited effectiveness for specific instruction sequences.
  Dynamic analysis often inserts code into system-under-test.
Fuzz testing methods:
  White-box, full implementation.
  Black-box, no implementation.
  Gray-box, some system info.

## Slide 4: Fuzzing methods
Traditional white-box fuzzers use symbolic execution or taint analysis.
  Symbolic execution inserts symbolic values to analyze execution sequence.
  Taint analysis traces tainted values to identify test points for further exercise.
  AFL combines compile-time instrumentation and genetic algorithms.
Black-box testing popular in systems that implement standards---leverages well-defined interface.
Network fuzzing:
  Data generation creates input packets using random + targeted values.
  Mutation changes legal packets.

## Slide 5: Fuzzing for Modbus
Well-known industrial networking standard:
  Application-level protocol.
  Interfaces to serial and HDLC protocols or TCP.
  Client-server model.

## Slide 6: Modbus packets
Packet includes function code and data.
Models device data with tables of 64K entries.
Tables may have 1-bit or 64-bit entries.
Allows file access.

## Slide 7: Modbus fuzzing tool
Three phase testing:
  Reconnaissance to identify memory model and function codes.
  Fuzzing.
  Fault detection.
Reconnaissance methods:
  Request identification methods.
  Send valid requests and determine if they are executed.
  Monitor device traffic.
  Identify memory bounds by observing traffic, probing specific addresses.
Fuzzing tests values of MBAP header fields, violation of protocol packet, values of PDU fields.

## Slide 8: Run-time monitoring
Detect violations:
  Deviation from good behavior.
  Match fo bad behavior.
Behaviors can be described as profiles or models.
  Profiles can be built using statistical and machine learning methods.
  Model-based methods make use of reference system model.

## Slide 9: ARMET
Features:
  Secure-by-design.
  Run-time monitoring.
  Recovery from detected attacks and failures.
Uses Fiat proof system to prove properties of system specification.
Run-time security monitor runs as middleware.
Detects all attacks as inconsistencies between observations and predictions.