## Slide 1: The Safety and Security Landscape
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: Safety and security
We can no longer treat safety and security as separate disciplines.
Combination of real-time embedded systems and physical plants intertwines safety and security.
  Cyber-physical systems (CPS).
  Internet-of-Things systems (IoT).

## Slide 3: Traditional definitions
Physical safety is the result of the absence or minimization of hazards that may harm life or property.
Security prevents attackers from achieving objectives through unauthorized access or unauthorized use of computers and networks (Howard).

## Slide 4: Safety and security interactions
Safety practices run counter to security updates.
  Physical systems cannot be arbitrarily stopped.
  Stopping and restarting may impose significant costs.
Security practices run counter to safety practices.
  Security provides a changing threat surface.
  Design requirements change as threats evolve.

## Slide 5: Themes
Safety and security are inseparable in CPS and IoT systems.
Neither safety nor security disciplines offer all the answers.
Safety and security vary in their use of short-term vs. long-term approaches and in the use of prevention vs. remediation. The new field of safe and secure systems should operate at all time scales and from the earliest stages of design to updates.
System designers must accept the fact that there is no end to design process due to evolving Internet threats. Systems must be designed to be adaptable to counter evolving threats.
Suites of standardized design templates help to reduce design risks.
Modern systems must combine design time analysis and architected safety+security features along with run-time monitoring.
Safety and security should be assessed in part by probabilistic assertions of the health of the system.

## Slide 6: Example threats
An Airbus A400M crashed after takeoff at Sevilla Airport in Spain. Later analysis determined that the aircraft’s engine control software had been incorrectly installed during its final assembly. That improper installation led to engine failure [Keo15].
Analysis of the design of Toyota automobiles [Koo14] identified failures to apply well-known engineering techniques in several areas, including protection from cosmic ray-induced data errors and application of software engineering principles.
Dieselgate [Dav15] was the result of a decision by Volkswagen management to design software in many of their diesel vehicles to provide inaccurate testing data that incorrectly gave the appearance of satisfying emissions regulations in several companies.

## Slide 7: Cyber-physical systems are shockingly easy to attack
Examples:
  Tire pressure monitoring system (TPMS) provides access to car electronic control units.
  Checkoway et al. identified car vulnerabilities including CD player, OBD-II port, telematics, Bluetooth.

## Slide 8: Cyber-physical systems can kill people
Leveson and Turner analyzed Therac-25 radiation device accidents.
  Multiple radiation overdoses, some fatal.
  Multiple contributing factors include lack of procedures to report incidents, overconfidence in software, poor software engineering, unrealistic risk assessments.
HatMan attack targets Triconex safety controllers.
  Allows read/modify memory, executing arbitrary code.

## Slide 9: Cyber-physical system disruptions require extensive and lengthy repairs
Stuxnet attack on Iranian nuclear facilities:
  Attacked Siemens Step 7 PLC.
  Stuxnet 0.5 manipulated valves to damage centrifuges.
  W32.Stuxnet damaged centrifuges by overspinning.
Dragonfly group has targeted energy companies, petroleum pipeline operators, energy industry equipment providers.
Ukraine power grid attacked in 2016.
  Attack conducted using CrashOverride.

## Slide 10: Patch and pray considered harmful
Information security practices encourage prompt installation of upgrades.
Upgrade testing does not take into account effects on physical plant.
Operating schedule of physical plant may restrict timing of upgrade application.

## Slide 11: Folk wisdom is untrustworthy
Open source software is not more reliable:
  Heartbleed security vulnerability affected critical software for several years before being discovered.
Air gaps cannot be maintained (Chatham House):
  Stuxnet attacks was propagated by portable USB drives.
  Some nuclear facilities use virtual private networks.
  Some nuclear facilities retain undocumented or forgotten Internet connections left over from maintenance operations.

## Slide 12: The IT/OT boundary is soft
Information technology and operational technology are not separate:
  Ukraine power grid attack included a denial-of-service attack on call centers to prevent reporting of outages.
  IT failures at three U. S. airlines caused service disruptions.

## Slide 13: Design processes cannot be trusted
Dieselgate:
  Senior executives ordered design changes to subvert emissions testing.
  Management decisions resulted in violations of laws in several countries.

## Slide 14: V model is inadequate
ISO 26262 uses V model for development:
  Top-down design.
  Bottom-up verification.
Internet-enabled systems are exposed to a changing threat environment.
  Requirements for security change even after deployment.
  System requirements are a moving target.

## Slide 15: Privacy is a critical requirement
Operational behavior may expose user characteristics and intent.
  Car position and routes.
  Medical information.
Non-functional characteristics may need to be protected:
  Timing.
  Power consumption.
Trade secrets are a form of private information.