## Slide 1: Threats and Threat Analysis
Marilyn Wolf and Dimitrios Serpanos
Safe and Secure Cyber-Physical Systems and Internet-of-Things Systems

## Slide 2: Vulnerabilities
Vulnerability in safety: design flaw or improper use of a system.
May result in a safety hazard, security threat, or both.

## Slide 3: Security threats
Hierarchy of security concerns:
  A vulnerability is a system security weakness.
  A threat is a possible means to exploit a vulnerability.
  An exploit is software that can be used by an attacker to take advantage of a vulnerability.
  An attack is an implementation of a threat.

## Slide 4: Compound threats
A compound threat includes both security and safety threats.
Allow attackers to extend their attacks into the physical world.
Threat tree for malicious exercise of an unstable mode.

## Slide 5: Threat analysis models
Find cutsets of threat trees:
  Combination of safety and security.
  All-safety or all-security.
Generalize risk priority number:
  for safety, occurrence, and detection factors.
  Vulnerability priority number
  Threat priority number
Functional Hazard Analysis Worksheet:
  The security vulnerability.
  Tools and methods used for the attack.
  Access mode for the attack.
  Results of the attack.
  Relationship of the attack to safety.

## Slide 6: Functional Hazard Analysis Worksheet
Threat ID | Life cycle phase | Activity | State/Mode | Function
Identifier | Phase analyzed by risk assessment | Actions performed within life cycle phase | System state or mode for the hazard | System function
Vulnerability | Attack Tools | Access Mode | Results of Attack | Relationship to Safety
Security vulnerability | Tools and methods used for attack | Unauthorized access, use, etc. | System compromise | How security violation results in safety failure
Functional failure | Threat Description | System Item(s) | Causal Factor Description | Mishap
Detailed description of failure mode | Detailed description of threat conditions | Portion of the system | Causes of failure | Description of failure
Effect(s) | Existing Mitigations | Software Control Category | Initial TPN | Software Criticality Index
Effects on life, limb, property | Existing means to mitigate failure | Degree of autonomy of software function | Initial threat assessment | Criticality
Target TPN | Causal Factor Risk Level | Recommended Mitigations | Comments | Follow-On Actions
Projected threat after mitigation | Potential for causal factors to occur | Methods to reduce threat | Relevant additional information | Further work to better understand threat

## Slide 7: Failure Mode Effects Analysis worksheet for threats
Function | Potential Failure Mode | Potential Effect(s) of Failure | Sf, Sv | Potential Cause(s) of Failure
Function being analyzed | Detailed description of failure conditions | Results of failure | Severity of failure, vulnerability | Causes of failure
Vulnerability | Attack Tools | Access Mode | Results of Attack | Relationship to Safety
Security vulnerability | Tools and methods used for attack | Unauthorized access, use, etc. | System compromise | How security violation results in safety failure
Of, Ov | Current Process Controls | Df, Dv | TPN | CRIT
Probability of failure due to occurrence of this failure/vulnerability | Existing means to mitigate failure | Ability to detect cause or failure mode/attack | Threat Priority | Initial criticality assessment
Of, Ov | Current Process Controls | Df, Dv | TPN | CRIT
Probability of failure due to occurrence of this failure/vulnerability | Existing means to mitigate failure | Ability to detect cause or failure mode/attack |  | Initial criticality assessment
Recommended Action(s) | Responsible Party and Target Completion Date
Actions to take | Who is responsible, when task should be finished
Action Taken | Sf, Sv | Of, Ov | Df, Dv | TPN | CRIT
How issue was resolved | Final failure, vulnerability severity | Final occurrency probabilities | Final detection abilities | Final Threat Priority Number | Final threat assessment

## Slide 8: Cyber-physical kill chain
Reconnaissance identifies both physical and cyber targets. Attack development can take into account safety risks that could be exploited.
Weaponization may in some cases make use of physical properties of the system to deliver an attack.
Delivery may or may not depend on physical access. In some cases, delivery may involve interfering with physical objects (attempted theft of a BMW automobile proceeded over two days [Roo18]).
Exploitation may make use of a combination of cyber and physical methods.
Installation may provide a persistent presence or a presence over a limited time span. Installation may also include methods, such as replay, to hide the attack.
Command and control may allow the attacker to remotely assess physical damage and update the direction of the attack.
Actions related to safety and security include the security actions of detect, deny, disrupt, degrade, deceive, destroy as well as the safety actions of detect, mitigate.

## Slide 9: Safety accident reporting
The Department of Energy maintains several databases, including Safety Basis Information System (SBIS). The Department operates a process to identify Suspect/Counterfeit and Defective Items.
The Federal Aviation Administration maintains an accident and incident database (https://www.faa.gov/data_research/accident_incident/).
The National Transportation Safety Board (NTSB) provides a database on accident reports on various transportation modes (https://www.ntsb.gov/investigations/AccidentReports/Pages/AccidentReports.aspx) and a database specific to aviation accidents (https://www.ntsb.gov/_layouts/ntsb.aviation/index.aspx).

## Slide 10: Example NTSB crash report
An executive summary provides a short description.
A factual information section describes the crash narrative, injuries, emergency response, motorcoach, highway and grade crossing, railroad operations, motor carrier operations, motorcoach driver, weather and roadway conditions.
An analysis section considers the motorcoach driver and train crew, the grade crossing, and emergency egress and extrication.
A conclusions section describes finding and probable cause.
A recommendations section provides new recommendations as well as recommendations reiterated and reclassified in the report.
An appendix describes the investigators and parties to the investigation.
A list of references is provided, as is a list of figures and tables as well as acronyms and abbreviations.

## Slide 11: Software vulnerability databases
The NIST National Vulnerability Database (NVD) (https://nvd.nist.gov/) is the U. S. government repository of vulnerability management data.
Common Vulnerabilities and Exposures CVE® (https://cve.mitre.org) is a database of publicly known vulnerabilities. CVE data is used in NVD.
The CERT Vulnerability Notes Database (https://www.kb.cert.org/vuls/) provides a set of Vulnerability Notes that include technical descriptions, remediation notes, and affected vendors.
The Common Vulnerability Scoring System (CVSS) defines metrics for IT-oriented vulnerabilities.

## Slide 12: Example CVE entry
The current description provides a summary.
Impact describes severity and metrics for CVS versions 3.0 and 2.0.
References to advisories, solutions, and tools are provided.
Vulnerability type is identified.
Vulnerable software and versions are provided.

## Slide 13: Improper authorization threats
Authorization domain governs access to data.
  Domain size should balance efficiency vs. protection.
  Domains should be designed considering both safety and security.
Software safety threats:
  Poor numerical algorithms.
  Hardware flaws.
  Cosmic rays and other externally-induced faults.

## Slide 14: Iterative threat analysis
Safety typically operates over long time scales while security reacts quickly.
Revisit threat analysis:
  Several times during design.
  Post-deployment.
Requirements safety/security:
  define a post-deploy schedule for vulnerability analysis;
  develop a plan to handle zero-day vulnerabilities;
  develop critieria under which these plans are revisited both during later design phases and after deployment.

## Slide 15: Architecture phase
Architectural design:
  Uses threat analysis.
  Updates threat analysis to include architectural information.
Newly-identified vulnerability possibilities:
  The new vulnerability may be a variation of one that was previously considered in the design process.
  The new vulnerability may present new threat cases.

## Slide 16: Threat mitigation
Pre-deployment:
  McGraw identifies static analysis, risk analysis, penetration testing for security, risk-based software testing.
Post-deployment:
  Emphasize resilience of safety-critical systems to both security and safety threats.
  Test software updates for physical plant issues