## Slide 1: Computing platforms
Design methodology.
Consumer electronics architectures.
System-level performance and power analysis.
Platform security.

## Slide 2: Evaluation boards
Designed by CPU manufacturer or others.
Includes CPU, memory, some I/O devices.
May include prototyping section.
CPU manufacturer often gives out reference design---can be used as starting point for your custom board design.

## Slide 3: ARM evaluation module
ARM processor.
Display, serial port, etc.
Prototyping area.

## Slide 4: BeagleBoard
OMAP processor.
Audio input and output.
Video output.
SD card.

## Slide 5: Choosing a platform
CPU: choice of instruction sets, features, etc.
Bus determines available I/O devices, system performance.
Memory size, speed.
I/O devices vary in performance, cost.

## Slide 6: Intellectual property
Hardware designs, source or object code, netlists, etc.
Used at all levels of design:
  Schematics for hardware reference design.
  Drivers and run-time libraries.
  Software development environments.

## Slide 7: BeagleBoard IP
PCB schematics and artwork files.
Bill of materials for components.
Compiler.
Linux.

## Slide 8: Debugging embedded systems
Challenges:
  target system may be hard to observe;
  target may be hard to control;
  may be hard to generate realistic inputs;
  setup sequence may be complex.

## Slide 9: Host/target design
Use a host system to prepare software for target system:
target
system
host system
serial line

## Slide 10: Host-based tools
Cross compiler:
  compiles code on host for target system.
Cross debugger:
  displays target state, allows target system to be controlled.

## Slide 11: Software debuggers
A monitor program residing on the target provides basic debugger functions.
Debugger should have a minimal footprint in memory.
User program must be careful not to destroy debugger program, but , should be able to recover from some damage caused by user code.

## Slide 12: Breakpoints
A breakpoint allows the user to stop execution, examine system state, and change state.
Replace the breakpointed instruction with a subroutine call to the monitor program.

## Slide 13: ARM breakpoints
0x400 MUL r4,r6,r6
0x404 ADD r2,r2,r4
0x408 ADD r0,r0,#1
0x40c B loop
uninstrumented code
0x400 MUL r4,r6,r6
0x404 ADD r2,r2,r4
0x408 ADD r0,r0,#1
0x40c BL bkpoint
code with breakpoint

## Slide 14: Breakpoint handler actions
Save registers.
Allow user to examine machine.
Before returning, restore system state.
  Safest way to execute the instruction is to replace it and execute in place.
  Put another breakpoint after the replaced breakpoint to allow restoring the original breakpoint.

## Slide 15: In-circuit emulators
A microprocessor in-circuit emulator is a specially-instrumented microprocessor.
Allows you to stop execution, examine CPU state, modify registers.

## Slide 16: Logic analyzers
A logic analyzer is an array of low-grade oscilloscopes:

## Slide 17: Logic analyzer architecture
UUT
sample
memory
microprocessor
controller
system clock
clock
gen
state or
timing mode
vector
address
display
keypad

## Slide 18: Boundary scan
Simplifies testing of multiple chips on a board.
  Registers on pins can be configured as a scan chain.
  Used for debuggers, in-circuit emulators.

## Slide 19: How to exercise code
Run on host system.
Run on target system.
Run in instruction-level simulator.
Run on cycle-accurate simulator.
Run in hardware/software co-simulation environment.

## Slide 20: Debugging real-time code
Bugs in drivers can cause non-deterministic behavior in the foreground problem.
Bugs may be timing-dependent.

## Slide 21: Consumer electronics use cases
Multimedia: stored in compressed form, uncompressed on viewing.
Data storage and management: keep track of your multimedia, etc.
Communication: download, upload, chat.

## Slide 22: Non-functional requirements for CE
Often battery-operated, strict power budget.,
Very inexpensive.
User interface must be capable but inexpensive.

## Slide 23: CE devices and hosts
Many devices talk to host system.
  PC host does things that are hard to do on the device.
Increasingly, CE devices communicate directly over the network, avoiding the host for access.

## Slide 24: Platforms and operating systems
Many CE devices use a DSP for signal processing and a RISC CPU for other tasks.
I/O devices include buttons, screen, USB.

## Slide 25: Flash file systems
Flash is widely used for mass storage.
Flash wears out on writing (up to 1 million cycles).
  Directory is most often written, wears out first.
Flash file system has layer that moves contents to levelize wear.
  Hides wear leveling from API.

## Slide 26: Cell phones
Most popular CE device in history; most widely used computing device.
  1 billion sold per year.
Handset talks to cell.
Cells hand off handset as it moves.

## Slide 27: Cell phone platforms
Today’s cell phones use analog front end, digital baseband processing.
  Future cell phones will perform IF processing with DSP.
Baseband processing in DSP:
  Voice compression.
  Network protocol.
Other processing:
  Multimedia functions.
  User interface.
  File system.
  Applications (contacts, etc.)

## Slide 28: System-level performance analysis
Performance depends on all the elements of the system:
  CPU.
  Cache.
  Bus.
  Main memory.
  I/O device.
memory
CPU
cache

## Slide 29: Bandwidth as performance
Bandwidth applies to several components:
  Memory.
  Bus.
  CPU fetches.
Different parts of the system run at different clock rates.
Different components may have different widths (bus, memory).

## Slide 30: Bandwidth and data transfers
Video frame: 1920 x 1080 x 3 = 6.2 MBytes.
  Transfer in 1/30 sec = 0.033 sec,
100 MHz 8-bit wide bus requires 0.062 sec/frame---too slow.
Increase bus width to 32 bits, transfer time reduced to 0.015 sec/frame.
Increase bus speed to 200 MHz, transfer time is 0.031 frame/sec for8-bit wide bus.

## Slide 31: Bus bandwidth modeling
T: # bus cycles.
P: bus cycle period.
Total time for transfer:
  t = TP.
D: data transfer

## Slide 32: Bus bandwidth
Assume one word per transfer, compute time for N word transfer.
Data transfer time D (may include wait states).
Overhead O1 + O2 = O.
O1
D
O2

## Slide 33: Bus burst transfer bandwidth
B: transfers per burst.
  N words.
D clock cycles per transfer.
O cycles overhead per burst.
B
OB
2
1
…

## Slide 34: Memory aspect ratios
64 M
16 M
8 M
8

## Slide 35: Bus performance bottlenecks
Transfer 1920 x 1080 video frame @ 30 frames/sec = 6.2 MBytes/sec.
Is performance bottleneck bus or memory?
memory
CPU

## Slide 36: Bus performance bottlenecks, cont’d.
Bus: assume 100 MHz bus, D=1, O=3:
Memory: try burst mode B=4, two bytes wide.

## Slide 37: Bus performance spreadsheet

## Slide 38: Parallelism
Speed things up by running several units at once.
DMA provides parallelism if CPU doesn’t need the bus:
  DMA + bus.
  CPU.

## Slide 39: ACPI
Standard power management mechanism for PC.
  OS determines actions, ACPI provides services.
States:
  G3, mechanical off.
  G2, soft off.
  G1, sleep.
  G0, working.

## Slide 40: Cryptography
Cryptography is the science of hiding information.
Secret-key cryptography allows messages to be encoded and decoded.
  Key must be kept secret or the message will not be secure.
Public-key cryptography gives secret messages with an easier-to-use approach:
  Sender uses secret key to encrypt message. Also provides a public key to others.
  Receiver can decrypt message using public key. The sender’s identity is established by the ability to use their public key.

## Slide 41: Cryptographic hash and digital signature
Cryptographic hash function generates a message digest.
  Short version of the message.
  Two different messages are unlikely to generate the same key.
Digital signature:
  Sender signs the message or message digest using private key.
  Receiver decrypts with public key.
Digital signature plus encryption:
  Sender signs the message or message digest with private key.
  Sender encrypts the message with the receiver’s public key.
  Receiver decrypts with private key, then verifies signature using sender’s public key.

## Slide 42: Attestation
Allows Bill to check whether Alice has been compromised before sharing secure information with Alice.
For example, hash certain code or data that will be known to Bill.
  If that important information was changed, the hash sent by Alice will not match what Bill expects.