## Slide 1: Introduction
What are embedded computing systems?
Challenges in embedded computing system design.
Design methodologies.

## Slide 2: Definition
Embedded computing system: any device that includes a programmable computer but is not itself a general-purpose computer.
Take advantage of application characteristics to optimize the design:
  don’t need all the general-purpose bells and whistles.

## Slide 3: Embedding a computer
CPU
mem
input
output
analog
analog
embedded
computer

## Slide 4: Examples
Cell phone.
Printer.
Automobile: engine, brakes, dash, etc.
Airplane: engine, flight controls, nav/comm.
Digital television.
Household appliances.

## Slide 5: Early history
Late 1940’s: MIT Whirlwind computer was designed for real-time operations.
  Originally designed to control an aircraft simulator.
First microprocessor was Intel 4004 in early 1970’s.
HP-35 calculator used several chips to implement a microprocessor in 1972.

## Slide 6: Early history, cont’d.
Automobiles used microprocessor-based engine controllers starting in 1980.
  Control fuel/air mixture, engine timing, etc.
  Multiple modes of operation: warm-up, cruise, hill climbing, etc.
  Provides lower emissions, better fuel efficiency.

## Slide 7: Microprocessor varieties
Microcontroller: includes I/O devices, on-board memory.
Digital signal processor (DSP): microprocessor optimized for digital signal processing.
Typical embedded word sizes: 8-bit, 16-bit, 32-bit.

## Slide 8: Application examples
Simple control: front panel of microwave oven, etc.
Canon EOS 3 has three microprocessors.
  32-bit RISC CPU runs autofocus and eye control systems.
Digital TV: programmable CPUs + hardwired logic.

## Slide 9: Automotive embedded systems
Today’s high-end automobile may have 100 microprocessors:
  4-bit microcontroller checks seat belt;
  microcontrollers run dashboard devices;
  16/32-bit microprocessor controls engine.
Low-end cars use 20+ microprocessors.

## Slide 10: BMW 850i brake and stability control system
Anti-lock brake system (ABS): pumps brakes to reduce skidding.
Automatic stability control (ASC+T): controls engine to improve stability.
ABS and ASC+T communicate.
  ABS was introduced first---needed to interface to existing ABS module.

## Slide 11: BMW 850i, cont’d.
brake
sensor
brake
sensor
brake
sensor
brake
sensor
ABS
hydraulic
pump

## Slide 12: Characteristics of embedded systems
Sophisticated functionality.
Real-time operation.
Low manufacturing cost.
Low power.
Designed to tight deadlines by small teams.

## Slide 13: Functional complexity
Often have to run sophisticated algorithms or multiple algorithms.
  Cell phone, laser printer.
Often provide sophisticated user interfaces.

## Slide 14: Real-time operation
Must finish operations by deadlines.
  Hard real time: missing deadline causes failure.
  Soft real time: missing deadline results in degraded performance.
Many systems are multi-rate: must handle operations at widely varying rates.

## Slide 15: Non-functional requirements
Many embedded systems are mass-market items that must have low manufacturing costs.
  Limited memory, microprocessor power, etc.
Power consumption is critical in battery-powered devices.
  Excessive power consumption increases system cost even in wall-powered devices.

## Slide 16: Design teams
Often designed by a small team of designers.
Often must meet tight deadlines.
  6 month market window is common.
  Can’t miss back-to-school window for calculator.

## Slide 17: Why use microprocessors?
Alternatives: field-programmable gate arrays (FPGAs), custom logic, etc.
Microprocessors are often very efficient: can use same logic to perform many different functions.
Microprocessors simplify the design of families of products.

## Slide 18: The performance paradox
Microprocessors use much more logic to implement a function than does custom logic.
But microprocessors are often at least as fast:
  heavily pipelined;
  large design teams;
  aggressive VLSI technology.

## Slide 19: Power
Custom logic uses less power, but CPUs have advantages:
  Modern microprocessors offer features to help control power consumption.
  Software design techniques can help reduce power consumption.
Heterogeneous systems: some custom logic for well-defined functions, CPUs+software for everything else.

## Slide 20: Platforms
Embedded computing platform: hardware architecture + associated software.
Many platforms are multiprocessors.
Examples:
  Single-chip multiprocessors for cell phone baseband.
  Automotive network + processors.

## Slide 21: The physics of software
Computing is a physical act.
  Software doesn’t do anything without hardware.
Executing software consumes energy, requires time.
To understand the dynamics of software (time, energy), we need to characterize the platform on which the software runs.

## Slide 22: Internet-of-Things (IoT) system
Combines sensing, actuating, computing, communication.
  Some links in the network are often wireless.
Example: manufacturing plant.

## Slide 23: Cyber-physical systems
A physical system that tightly interacts with a computer system.
Computers replace mechanical controllers:
  More accurate.
  More sophisticated control.
Engine controllers replace distributor, carburetor, etc.
  Complex algorithms allow both greater fuel efficiency and lower emissions.

## Slide 24: IoT and CPS
IoT often lower sample rate, larger physical plant.
CPS often more tightly coupled, higher sample rate.

## Slide 25: Edge computing
Systems that must respond to the physical world often can’t wait for answers from a remote data center.
Edge computing:
  Responsive.
  Energy efficient.
  Connected to other devices.

## Slide 26: What does “performance” mean?
In general-purpose computing, performance often means average-case, may not be well-defined.
In real-time systems, performance means meeting deadlines.
  Missing the deadline by even a little is bad.
  Finishing ahead of the deadline may not help.

## Slide 27: Characterizing performance
We need to analyze the system at several levels of abstraction to understand performance:
  CPU.
  Platform.
  Program.
  Task.
  Multiprocessor.

## Slide 28: Security, safety
Security: system’s ability to prevent malicious attacks.
Integrity: maintenance of proper data values.
Privacy: no unauthorized releases of data.
Safety: no harmful releases of energy.
  No crashes, accidents, etc.

## Slide 29: Safe, secure systems
Traditional security is oriented to IT and data security.
But insecure embedded computers can create unsafe cyber-physical systems.
We need to combine safety and security:
  Identify security breaches that compromise safety.
Safety and security can’t be bolted on---they must be baked in.

## Slide 30: Safe and secure systems technologies
Cryptography enables encryption and its follow-ons such as digital signatures.
Security protocols use cryptography to authenticate, check integrity, etc.
Safe and secure hardware architectures limit ability of adversaries to interfere with cryptographic operations.

## Slide 31: Challenges in embedded system design
How much hardware do we need?
  How big is the CPU? Memory?
How do we meet our deadlines?
  Faster hardware or cleverer software?
How do we minimize power?
  Turn off unnecessary logic? Reduce memory accesses?

## Slide 32: Challenges, etc.
Does it really work?
  Is the specification correct?
  Does the implementation meet the spec?
  How do we test for real-time characteristics?
  How do we test on real data?
How do we work on the system?
  Observability, controllability?
  What is our development platform?

## Slide 33: Design methodologies
A procedure for designing a system.
Understanding your methodology helps you ensure you didn’t skip anything.
Compilers, software engineering tools, computer-aided design (CAD) tools, etc., can be used to:
  help automate methodology steps;
  keep track of the methodology itself.

## Slide 34: Design goals
Performance.
  Overall speed, deadlines.
Functionality and user interface.
Manufacturing cost.
Power consumption.
Other requirements (physical size, etc.)

## Slide 35: Levels of abstraction
requirements
specification
architecture
component
design
system
integration

## Slide 36: Top-down vs. bottom-up
Top-down design:
  start from most abstract description;
  work to most detailed.
Bottom-up design:
  work from small components to big system.
Real design uses both techniques.

## Slide 37: Stepwise refinement
At each level of abstraction, we must:
  analyze the design to determine characteristics of the current state of the design;
  refine the design to add detail.

## Slide 38: Requirements
Plain language description of what the user wants and expects to get.
May be developed in several ways:
  talking directly to customers;
  talking to marketing representatives;
  providing prototypes to users for comment.

## Slide 39: Functional vs. non-functional requirements
Functional requirements:
  output as a function of input.
Non-functional requirements:
  time required to compute output;
  size, weight, etc.;
  power consumption;
  reliability;
  etc.

## Slide 40: Our requirements form

## Slide 41: Example: GPS moving map requirements
Moving map obtains position from GPS, paints map from local database.
lat: 40 13 lon: 32 19
I-78
Scotch Road

## Slide 42: GPS moving map needs
Functionality: For automotive use. Show major roads and landmarks.
User interface: At least 400 x 600 pixel screen. Three buttons max. Pop-up menu.
Performance: Map should scroll smoothly. No more than 1 sec power-up. Lock onto GPS within 15 seconds.
Cost: $120 street price = approx. $30 cost of goods sold.

## Slide 43: GPS moving map needs, cont’d.
Physical size/weight: Should fit in hand.
Power consumption: Should run for 8 hours on four AA batteries.

## Slide 44: GPS moving map requirements form

## Slide 45: Specification
A more precise description of the system:
  should not imply a particular architecture;
  provides input to the architecture design process.
May include functional and non-functional elements.
May be executable or may be in mathematical form for proofs.

## Slide 46: GPS specification
Should include:
  What is received from GPS;
  map data;
  user interface;
  operations required to satisfy user requests;
  background operations needed to keep the system running.

## Slide 47: Architecture design
What major components go satisfying the specification?
Hardware components:
  CPUs, peripherals, etc.
Software components:
  major programs and their operations.
Must take into account functional and non-functional specifications.

## Slide 48: GPS moving map block diagram
GPS
receiver
search
engine
renderer
user
interface
database
display

## Slide 49: GPS moving map hardware architecture
GPS
receiver
CPU
panel I/O
display
frame
buffer
memory

## Slide 50: GPS moving map software architecture
position
database
search
renderer
timer
user
interface
pixels

## Slide 51: Designing hardware and software components
Must spend time architecting the system before you start coding.
Some components are ready-made, some can be modified from existing designs, others must be designed from scratch.

## Slide 52: System integration
Put together the components.
  Many bugs appear only at this stage.
Have a plan for integrating components to uncover bugs quickly, test as much functionality as early as possible.

## Slide 53: Summary
Embedded computers are all around us.
  Many systems have complex embedded hardware and software.
Embedded systems pose many design challenges: design time, deadlines, power, etc.
Design methodologies help us manage the design process.