## Slide 1: Networks and Multiprocessors
Why networks and multiprocessors?
Categories of multiprocessors.
MPSoCs and shared memory multiprocessors.

## Slide 2: Why multiprocessors?
Better cost/performance.
  Match each CPU to its tasks or use custom logic (smaller, cheaper).
  CPU cost is a non-linear function of performance.
cost
performance

## Slide 3: Why multiprocessors? cont’d.
Better real-time performance.
  Put time-critical functions on less-loaded processing elements.
  Remember RMS utilization---extra CPU cycles must be reserved to meet deadlines.
cost
performance
deadline
deadline w.
RMS overhead

## Slide 4: Why multiprocessors? cont’d.
Using specialized processors or custom logic saves power.
Desktop uniprocessors are not power-efficient enough for battery-powered applications.
[Aus04] © 2004 IEEE Computer Society

## Slide 5: Why multiprocessors? cont’d.
Good for processing I/O in real-time.
May consume less energy.
May be better at streaming data.
May not be able to do all the work on even the largest single CPU.

## Slide 6: Categories of multiprocessors

## Slide 7: Multiprocessor taxonomy
PE: processing element.
PEs and memory connected by interconnection network.
Shared memory: all PEs talk to a pool of memory.
Message passing: each PE has its own memory, communicates with messages.
Shared memory and message passing are equivalent.

## Slide 8: Varieties of multiprocessor
System-on-chip is complete system, usually a multiprocessor, with I/O and memory.
A distributed system has multiple chips and significant communication delay.

## Slide 9: ARM MPCore
Up to four CPUs.
Distributed interrupt system.
Snooping cache controller.

## Slide 10: Why distributed?
Higher performance at lower cost.
Physically distributed activities---time constants may not allow transmission to central site.
Improved debugging---use one CPU in network to debug others.
May buy subsystems that have embedded processors.

## Slide 11: Shared memory multiprocessors
Multi-core systems are symmetric multiprocessors with identical PEs.
Many embedded multiprocessors are heterogeneous:
  Multiple programmable CPU types.
  Hardwired accelerators.
Heterogeneous multiprocessors use less energy, are less expensive.

## Slide 12: TI TMS320DM816x DaVinci
ARM Cortex A8 plus C674x VLIW DSP.
HD video coprocessor accelerates H.264, MPEG-4, etc.
HD video processing susystem provides additional video processing.
Graphics unit performs 3D graphics.

## Slide 13: Accelerated systems
Use additional computational unit dedicated to some functions?
  Hardwired logic.
  Extra CPU.
Hardware/software co-design: joint design of hardware and software architectures.

## Slide 14: Accelerated system architecture
CPU
accelerator
memory
I/O
request
data
result
data

## Slide 15: Accelerator vs. co-processor
A co-processor executes instructions.
  Instructions are dispatched by the CPU.
An accelerator appears as a device on the bus.
  The accelerator is controlled by registers.

## Slide 16: Accelerator implementations
Application-specific integrated circuit.
Field-programmable gate array (FPGA).
Standard component.
  Example: graphics processor.

## Slide 17: Xilinx Zynq UltraScale+
Quad-core ARM Cortex-A53 and dual-core ARM Cortex-R5.
Mali graphics unit.
FPGA fabric and block RAM.
PCI3, SATA, USB, CAN, SPI, GPIO.

## Slide 18: System design tasks
Design a heterogeneous multiprocessor architecture.
  Processing element (PE): CPU, accelerator, etc.
Program the system.

## Slide 19: Accelerated system design
First, determine that the system really needs to be accelerated.
  How much faster is the accelerator on the core function?
  How much data transfer overhead?
Design the accelerator itself.
Design CPU interface to accelerator.

## Slide 20: Accelerated system platforms
Several off-the-shelf boards are available for acceleration in PCs:
  FPGA-based core;
  PC bus interface.

## Slide 21: Accelerator/CPU interface
Accelerator registers provide control registers for CPU.
Data registers can be used for small data objects.
Accelerator may include special-purpose read/write logic.
  Especially valuable for large data transfers.

## Slide 22: System integration and debugging
Try to debug the CPU/accelerator interface separately from the accelerator core.
Build scaffolding to test the accelerator.
Hardware/software co-simulation can be useful.

## Slide 23: Caching problems
Main memory provides the primary data transfer mechanism to the accelerator.
Programs must ensure that caching does not invalidate main memory data.
  CPU reads location S.
  Accelerator writes location S.
  CPU writes location S.
BAD

## Slide 24: Synchronization
As with cache, main memory writes to shared memory may cause invalidation:
  CPU reads S.
  Accelerator writes S.
  CPU reads S.

## Slide 25: Multiprocessor performance analysis
Effects of parallelism (and lack of it):
  Processes.
  CPU and bus.
  Multiple processors.

## Slide 26: Accelerator speedup
Critical parameter is speedup: how much faster is the system with the accelerator?
Must take into account:
  Accelerator execution time.
  Data transfer time.
  Synchronization with the master CPU.

## Slide 27: Accelerator execution time
Total accelerator execution time:
  taccel = tin + tx + tout
Data input
Accelerated
computation
Data output

## Slide 28: Accelerator speedup
Assume loop is executed n times.
Compare accelerated system to non-accelerated system:
  S = n(tCPU - taccel)
  = n[tCPU - (tin + tx + tout)]
Execution time on CPU

## Slide 29: Single- vs. multi-threaded
One critical factor is available parallelism:
  single-threaded/blocking: CPU waits for accelerator;
  multithreaded/non-blocking: CPU continues to execute along with accelerator.
To multithread, CPU must have useful work to do.
  But software must also support multithreading.

## Slide 30: Total execution time
Single-threaded:
Multi-threaded:
P2
P1
A1
P3
P4
P2
P1
A1
P3
P4

## Slide 31: Execution time analysis
Single-threaded:
  Count execution time of all component processes.
Multi-threaded:
  Find longest path through execution.

## Slide 32: Sources of parallelism
Overlap I/O and accelerator computation.
  Perform operations in batches, read in second batch of data while computing on first batch.
Find other work to do on the CPU.
  May reschedule operations to move work after accelerator initiation.

## Slide 33: Data input/output times
Bus transactions include:
  flushing register/cache values to main memory;
  time required for CPU to set up transaction;
  overhead of data transfers by bus packets, handshaking, etc.

## Slide 34: Scheduling and allocation
Must:
  schedule operations in time;
  allocate computations to processing elements.
Scheduling and allocation interact, but separating them helps.
  Alternatively allocate, then schedule.

## Slide 35: Example: scheduling and allocation
P1
P2
P3
d1
d2
Task graph
Hardware platform
M1
M2

## Slide 36: First design
Allocate P1, P2 -> M1; P3 -> M2.
time
M1
M2
P1
P2
P3
P1C
P2C

## Slide 37: Second design
Allocate P1 -> M1; P2, P3 -> M2:
M1
M2
P1
P2
P3
P1C
time

## Slide 38: Example: adjusting messages to reduce delay
Task graph:
Network:
P1
P2
P3
d1
d2
M1
M2
M3
allocation
3
4
3
execution time
Transmission time = 4

## Slide 39: Initial schedule
time
M1
M2
M3
network
0
20
10
5
15
P1
P2
d1
d2
P3
Time = 15

## Slide 40: New design
Modify P3:
  reads one packet of d1, one packet of d2
  computes partial result
  continues to next packet

## Slide 41: New schedule
time
M1
M2
M3
network
0
20
10
5
15
P1
P2
d1
P3
d2
d1
P3
d2
d1
P3
d2
d1
P3
d2
Time = 12

## Slide 42: Buffering and performance
Buffering may sequentialize operations.
  Next process must wait for data to enter buffer before it can continue.
Buffer policy (queue, RAM) affects available parallelism.

## Slide 43: Buffers and latency
Three processes separated by buffers:
B1
A
B2
B
B3
C

## Slide 44: Buffers and latency schedules
A[0]
A[1]
…
B[0]
B[1]
…
C[0]
C[1]
…
A[0]
B[0]
C[0]
A[1]
B[1]
C[1]
…
Must wait for
all of A before
getting any B

## Slide 45: I2C bus
Designed for low-cost, medium data rate applications.
Characteristics:
  serial;
  multiple-master;
  fixed-priority arbitration.
Several microcontrollers come with built-in I2C controllers.

## Slide 46: I2C physical layer
master 1
master 2
slave 1
slave 2
SCL
SDL
data line
clock line

## Slide 47: I2C data format
SCL
SDL
...
MSB
start
...
ack
...

## Slide 48: I2C electrical interface
SDL
+
Open collector interface:
SCL
+

## Slide 49: I2C signaling
Sender pulls down bus for 0.
Sender listens to bus---if it tried to send a 1 and heard a 0, someone else is simultaneously transmitting.
Transmissions occur in 8-bit bytes.

## Slide 50: I2C data link layer
Every device has an address (7 bits in standard, 10 bits in extension).
  Bit 8 of address signals read or write.
General call address allows broadcast.

## Slide 51: I2C bus arbitration
Sender listens while sending address.
When sender hears a conflict, if its address is higher, it stops signaling.
Low-priority senders relinquish control early enough in clock cycle to allow bit to be transmitted reliably.

## Slide 52: I2C transmissions
multi-byte write
read from slave
write, then read
S
adrs
0
data
data
P
S
adrs
1
data
P
S
adrs
0
data
S
adrs
1
data
P