## Slide 1: Networks and multiprocessors
Example: video accelerator

## Slide 2: Concept
Build accelerator for block motion estimation, one step in video compression.
Perform two-dimensional correlation:
Frame 1
f2
f2
f2
f2
f2
f2
f2
f2
f2
f2

## Slide 3: Block motion estimation
MPEG divides frame into 16 x 16 macroblocks for motion estimation.
Search for best match within a search range.
Measure similarity with sum-of-absolute-differences (SAD):
  S | M(i,j) - S(i-ox, j-oy) |

## Slide 4: Best match
Best match produces motion vector for motion block:

## Slide 5: Full search algorithm
bestx = 0; besty = 0;
bestsad = MAXSAD;
for (ox = - SEARCHSIZE; ox < SEARCHSIZE; ox++) {
for (oy = -SEARCHSIZE; oy < SEARCHSIZE; oy++) {
int result = 0;
for (i=0; i<MBSIZE; i++) {
for (j=0; j<MBSIZE; j++) {
result += iabs(mb[i][j] - search[i-ox+XCENTER][j-oy-YCENTER]);

## Slide 6: Full search algorithm, cont’d.
}
}
if (result <= bestsad) { bestsad = result; bestx = ox; besty = oy; }
}
}

## Slide 7: Computational requirements
Let MBSIZE = 16, SEARCHSIZE = 8.
Search area is 8 + 8 + 1 in each dimension.
Must perform:
  nops = (16 x 16) x (17 x 17) = 73984 ops
CIF format has 352 x 288 pixels -> 22 x 18 macroblocks.

## Slide 8: Accelerator requirements

## Slide 9: Accelerator data types, basic classes
Motion-vector
x, y : pos
Macroblock
pixels[] : pixelval
Search-area
pixels[] : pixelval
PC
memory[]
Motion-estimator
compute-mv()

## Slide 10: Sequence diagram
:PC
:Motion-estimator
compute-mv()
memory[]
memory[]
memory[]
Search area
macroblocks

## Slide 11: Architectural considerations
Requires large amount of memory:
  macroblock has 256 pixels;
  search area has 1,089 pixels.
May need external memory (especially if buffering multiple macroblocks/search areas).

## Slide 12: Motion estimator organization
Address
generator
search area
macroblock
network
ctrl
network
PE 0
comparator
PE 1
PE 15
Motion
vector
...

## Slide 13: Pixel schedules
M(0,0)
S(0,2)

## Slide 14: System testing
Testing requires a large amount of data.
Use simple patterns with obvious answers for initial tests.
Extract sample data from JPEG pictures for more realistic tests.