## Slide 1: TI C55x instruction set
C55x programming model.
C55x assembly language.
C55x memory organization.
C55x data operations.
C55x flow of control.

## Slide 2: TI C55x overview
Accumulator architecture:
  acc = operand op acc.
  Very useful in loops for DSP.
C55x assembly language:
  MPY *AR0, *CDP+, AC0
  Label: MOV #1, T0
C55x algebraic assembly language:
  AC1 = AR0 * coef(*CDP)

## Slide 3: Intrinsic functions
Compiler support for assembly language.
Intrinsic function maps directly onto an instruction.
Example:
  int_sadd(arg1,arg2)
  Performs saturation arithmetic addition.

## Slide 4: C55x data types
Data types:
  Word: 16 bits.
  Longword: 32 bits.
Instructions are byte-addressable.
Some instructions operate on register bits.

## Slide 5: C55x registers
Terminology:
  Register: any type of register.
  Accumulator: acc = operand op ac.
Most registers are memory-mapped.

## Slide 6: C55x program counter and control flow registers
PC is program counter.
XPC is program counter extension.
RETA is subroutine return address.

## Slide 7: C55x accumulators and status registers
Four 40-bit accumulators: AC0, AC1, AC2, and AC3.
  Low-order bits 0-15 are AC0L, etc.
  High-order bits 16-31 are AC0H, etc.
  Guard bits 32-39 are AC0G, etc.
ST0, ST1, PMST, ST0_55, ST1_55, ST2_55, ST3_55 provide arithmetic/bit manipulation flags, etc.

## Slide 8: C55x stack pointers
SP keeps track of user stack.
SSP holds system stack pointer.
SPH is extended data page pointer for both SP and SSP.

## Slide 9: C55x auxiliary registers and circular buffer pointers
AR0-AR7 are auxiliary instructions.
CDP points to coefficients for polynomial evaluation instructions. CDPH is main data page pointer.
BK47 is used for circular buffer operations along with AR4-7.
BK03 addresses circular buffers.
BKC is size register for CDP.

## Slide 10: C55x block repeat registers
BRC9 counts block repeat instructions.
RSA0L and REA0L keep track of start and end points of blocks.
BRC1 and BRS1 are used to repeat blocks of instructions.
RSA0 and RSA1 are the start address registers for block repeats.

## Slide 11: C55x addressing mode and interrupt registers
DP and DPH set base address for data access.
PDP determines base address for I/O.
IER0 and IER1 are interrupt mask registers.
IFR0 and IFR1 keep track of currently pending registers.
DBIER0 and DBIER1 are for debugging.

## Slide 12: C55x memory map
24-bit address space, 16 MB of memory.
Data, program, I/O all mapped to same physical memory.
Addressability:
  Program space address is 24 bits.
  Data space is 23 bits.
  I/O address is 16 bits.
main data page 0
main data page 1
main data page 2
main data page 127
…
memory mapped registers

## Slide 13: C55x addressing modes
Three addressing modes:
  Absolute addressing supplies an address in an instruction.
  Direct addressing supplies an offset.
  Indirect addressing uses a register as a pointer.

## Slide 14: C55x direct addressing
DP addressing accesses data pages:
  ADP = DPH[22:15](DP+Doffset)
SP addressing accesses stack values:
  ASP = SPH[22:15](SP+Soffset)
Register-bit direcdt addressing accesses bits in registers.
PDP addressing accesses data pages:
  APDP = PDP[15:6]PDPoffset

## Slide 15: C55x indirect addressing
AR indirect addressing uses auxiliary register to point to data.
Dual AR indirect addressing allows two simultaneous accesses.
CDP indirect addressing uses CDP to access coefficients.
Coefficient indirect addressing is similar to CDP indirect but for instructions with 3 memory operands per cycle.

## Slide 16: C55x stack operations
Two stacks: data and system.
Three different stack configurations:
  Dual 16-bit stack with fast return has independent data and system stacks.
  Dual 16-bit stack with slow return, independent data and system stacks but RETA and CFCT are not used for slow returns.
  32-bit stack with slow return, SP and SSP are both modified by the same amount.

## Slide 17: C55x data operations
MOV moves data between registers and memory:
  MOV src, dst
Varieties of ADDs:
  ADD src,dst
  ADD dual(LMEM),ACx,ACy
Multiplication:
  MPY src,dst
  MAC AC,TX,ACy

## Slide 18: C55x flow of control
Unconditional branch:
  B ACx
  B label
Conditional branch:
  BCC label, cond
Loops:
  Single-instruction repeat
  Block repeat

## Slide 19: Efficient loops
General rules:
  Don’t use function calls.
  Keep loop body small to enable local repeat (only forward branches).
  Use unsigned integer for loop counter.
  Use <= to test loop counter.
  Make use of compiler---global optimization, software pipelining.

## Slide 20: Single-instruction repeat loop example
STM #4000h,AR2
; load pointer to source
STM #100h,AR3
; load pointer to destination
RPT #(1024-1)
MVDD *AR2+,*AR3+
; move

## Slide 21: C55x subroutines
Unconditional subroutine call:
  CALL target
Conditional subroutine call:
  CALLCC adrs,cond
Two types of return:
  Fast return gives return address and loop context in registers.
  Slow return puts return address/loop on stack.

## Slide 22: C55x interrupts
Handled using subroutine mechanism.
Four step handling process:
  Receive interrupt.
  Acknowledge interrupt.
  Prepare for ISR by finishing current instruction, retrieving interrupt vector.
  Processing the interrupt service routine.
32 possible interrupt vectors, 27 priorities.