## Slide 1: TI C64x
High-performance VLIW DSP.
  Up to eight instructions per cycle.
  Divided into two data paths A and B.
Floating-point and integer arithmetic
Harvard architecture.
Instruction grouping:
  Fetch packet is a group of instructions executed together.
  Execute packet instructions are executed together.

## Slide 2: C64x block diagram
Exeuction divided between two data paths.
Each data path has its own register file.
Data must be explicitly copied from one register file to the other.

## Slide 3: Function units
.L1 and .L2 perform 32/40-bit arithmetic, 32-bit logical, data packing/unpacking.
.S1 and .S2 perform 32-bit arithmetic, 32/40-bit shift and bit-field ops, 32-bit logical ops, branches, etc.
.M1 and .M2 perform multiplications, bit interleaving, rotation, Galois field multiplication, etc.
.D1 and .D2 perform address calculations, loads/stores, etc.

## Slide 4: Constraints on execution packets
Each instruction must execute on a separate function unit.
Most .M write combinations are illegal.
Most cases of reading multiple values from opposite register file.
Delay cycle added for register read after update from cross-path.
Cannot execute two load/store usign dest/source from same reg file.
At most four reads of a register.
Can’t write to register twice.

## Slide 5: Other features
Atomic operations for semaphores.
Circular addressing modes.
Delay slots to use instruction slots after a multi-cycle operation.
Interrupts mediated by registers IFR and IER.