## Slide 1: PICmicro PIC16F
PIC16F processor and memory organization.
PIC16F data operations.
PIC16F flow of control.

## Slide 2: Processor and memory organization
Exact features vary from model to model.
Harvard architecture.
Instruction flash memory up to 8192 words.
  Instructions are 14 bits long.
Data memory includes up to 368 words SRAM and 256 bytes EEPROM.
  Data is byte-addressable.

## Slide 3: Addresses and instructions
PC<12:0>
reset vector
interrupt vector
page 0
page 1
…
stack
0000h
0004h

## Slide 4: Program counter and status register
PC can be loaded from 8-level stack.
  Separate from program and data memory.
Stack operates as a circular buffer.
Used by CALL, RETURN/RETLW/RETFIE.
STATUS located in bank 0.
  ALU status, reset, bank select.

## Slide 5: Data space
General purpose register: data memory location.
Special function register: I/O devices, etc.

## Slide 6: Addressing modes
Terminology:
  f: general-purpose register.
  W: accumulator.
  b: bit address in register.
  k: literal, constant, or label.
Indirect addressing controlled by INDF and FSR registers.
  Access to INDF causes indirect load through FSR.

## Slide 7: Data instructinos
Arithmetic.
Boolean.
Move.
Rotate.
Swap.
Watchdog timer.

## Slide 8: Flow of control
Unconditional branch.
Conditioanl branch.
Subroutine call/return.
Interrupt return.
Standby mode.