## Slide 1: CPUs
Caches.
Memory management.

## Slide 2: Caches and CPUs
CPU
cache
controller
cache
main
memory
data
data
address
data
address

## Slide 3: Cache operation
Many main memory locations are mapped onto one cache entry.
May have caches for:
  instructions;
  data;
  data + instructions (unified).
Memory access time is no longer deterministic.

## Slide 4: Terms
Cache hit: required location is in cache.
Cache miss: required location is not in cache.
Working set: set of locations used by program in a time interval.

## Slide 5: Types of misses
Compulsory (cold): location has never been accessed.
Capacity: working set is too large.
Conflict: multiple locations in working set map to same cache entry.

## Slide 6: Memory system performance
h = cache hit rate.
tcache = cache access time, tmain = main memory access time.
Average memory access time:
  tav = htcache + (1-h)tmain

## Slide 7: Multiple levels of cache
CPU
L1 cache
L2 cache

## Slide 8: Multi-level cache access time
h1 = cache hit rate.
h2 = rate for miss on L1, hit on L2.
Average memory access time:
  tav = h1tL1 + (h2-h1)tL2 + (1- h2-h1)tmain

## Slide 9: Replacement policies
Replacement policy: strategy for choosing which cache entry to throw out to make room for a new memory location.
Two popular strategies:
  Random.
  Least-recently used (LRU).

## Slide 10: Cache organizations
Fully-associative: any memory location can be stored anywhere in the cache (almost never implemented).
Direct-mapped: each memory location maps onto exactly one cache entry.
N-way set-associative: each memory location can go into one of n sets.

## Slide 11: Cache performance benefits
Keep frequently-accessed locations in fast cache.
Cache retrieves more than one word at a time.
  Sequential accesses are faster after first access.

## Slide 12: Direct-mapped cache
valid
=
tag
index
offset
hit
value
tag
data
1
0xabcd
byte byte byte ...
byte
cache block

## Slide 13: Write operations
Write-through: immediately copy write to main memory.
Write-back: write to main memory only when location is removed from cache.

## Slide 14: Direct-mapped cache locations
Many locations map onto the same cache block.
Conflict misses are easy to generate:
  Array a[] uses locations 0, 1, 2, …
  Array b[] uses locations 1024, 1025, 1026, …
  Operation a[i] + b[i] generates conflict misses.

## Slide 15: Set-associative cache
A set of direct-mapped caches:
Block 1
Block 2
Block n
...
hit
data

## Slide 16: Example: direct-mapped vs. set-associative

## Slide 17: Direct-mapped cache behavior
After 001 access:
  block tag data
  00 - -
  01 0 1111
  10 - -
  11 - -
After 010 access:
  block tag data
  00 - -
  01 0 1111
  10 0 0000
  11 - -

## Slide 18: Direct-mapped cache behavior, cont’d.
After 011 access:
  block tag data
  00 - -
  01 0 1111
  10 0 0000
  11 0 0110
After 100 access:
  block tag data
  00 1 1000
  01 0 1111
  10 0 0000
  11 0 0110

## Slide 19: Direct-mapped cache behavior, cont’d.
After 101 access:
  block tag data
  00 1 1000
  01 1 0001
  10 0 0000
  11 0 0110
After 111 access:
  block tag data
  00 1 1000
  01 1 0001
  10 0 0000
  11 1 0100

## Slide 20: 2-way set-associtive cache behavior
Final state of cache (twice as big as direct-mapped):
  blk set 0 tag set 0 data set 1 tag set 1 data
  00 1 1000 - -
  01 0 1111 1 0001
  10 0 0000 - -
  11 0 0110 1 0100

## Slide 21: 2-way set-associative cache behavior
Final state of cache (same size as direct-mapped):
  blk set 0 tag set 0 data set 1 tag set 1 data
  0 01 0000 10 1000
  1 10 0111 11 0100

## Slide 22: Example caches
StrongARM:
  16 Kbyte, 32-way, 32-byte block instruction cache.
  16 Kbyte, 32-way, 32-byte block data cache (write-back).
SHARC:
  32-instruction, 2-way instruction cache.

## Slide 23: Memory management units
Memory management unit (MMU) translates addresses:
CPU
main
memory
memory
management
unit
logical
address
physical
address

## Slide 24: Memory management tasks
Allows programs to move in physical memory during execution.
Allows virtual memory:
  memory images kept in secondary storage;
  images returned to main memory on demand during execution.
Page fault: request for location not resident in memory.

## Slide 25: Address translation
Requires some sort of register/table to allow arbitrary mappings of logical to physical addresses.
Two basic schemes:
  segmented;
  paged.
Segmentation and paging can be combined (x86).

## Slide 26: Segments and pages
memory
segment 1
segment 2
page 1
page 2

## Slide 27: Segment address translation
segment base address
logical address
range
check
physical address
+
range
error
segment lower bound
segment upper bound

## Slide 28: Page address translation
page
offset
page
offset
page i base
concatenate

## Slide 29: Page table organizations
flat
tree
page descriptor
page
descriptor

## Slide 30: Caching address translations
Large translation tables require main memory access.
TLB: cache for address translation.
  Typically small.

## Slide 31: ARM memory management
Memory region types:
  section: 1 Mbyte block;
  large page: 64 kbytes;
  small page: 4 kbytes.
An address is marked as section-mapped or page-mapped.
Two-level translation scheme.

## Slide 32: ARM address translation
offset
1st index
2nd index
physical address
Translation table
base register
1st level table
descriptor
2nd level table
descriptor
concatenate
concatenate